## Slide 1
The Gaia experience: an INAF Legacy for science and technology
Mario G. Lattanzi
INAF-OATo
Il primo di due contributi (segue la Dott.ssa Deborah Busonero) che si vuole concentrare sull’aspetto della legacy Gaia, che è ora (!), e come la stiamo affrontando in pratica. Un contributo ai temi 2 (Infrastrutture INAF di supporto alla scienza) e 5 (Infrastrutture HW e SW) messi a punto dal CS di questo workshop.
Deborah andrà oltre la semplice conservazione del dato, ovvero: una legacy come quella di Gaia senza ‘pipelines’ tornerebbe ad essere una collezione di dati freddi (‘cold data’).

## Slide 2
1- The Gaia DPCT 2- From DPCT to the Gaia Legacy: The Living Sky Prototype 3- What is the Gaia Legacy? 4- The transition: OPS4-TLS
5- Criticità
Content

## Slide 3
Il DPCT è uno dei 6 centri di processamento dati (DPC) del Gaia Science Ground Segment, ubicato in ALTEC a Torino. La sua realizzazione ed operatività è il risultato del lavoro di un team integrato INAF-OATo/ALTEC.
Ideazione e progettazione del DPCT e dei sistemi AVU iniziata nel lontano 2005.
INAF in DPCT: Catania e Torino
1. DPCT

## Slide 4
Infrastruttura HW
Piattaforma Operativa e di test & sviluppo
Procurement performed incrementally according to mission needs (via specifi ASI contracts)
INTERNET LINK : 1Gbps (300 Mbps guaranteed) via GARR
STORAGE CAPACITY: 2.5 PB overall raw disk space distributed between two HP P7400 storage units and one P8400.
COMPUTING : 14 servers HP DL580 G7/G9 with a total of about 600 CPU cores and 4.5TB RAM.
DEV & TEST: 7 servers HP
DB SERVERS: 3 servers HP DL580 G7 (32 cores, 256MB RAM each) based on Oracle RAC technology (DBMS Oracle).
NETWORK CONNECTION: LAN network up to 10 Gbps. SAN network redundant at 8 Gbps.
SECURITY SERVICE: redundant firewall based on pfSense, enabling secure remote access via VPN.
INFRA MONITORING AND MANAGEMENT: services based on VMWare virtual environment configured with two HP DL 580 G7 servers clustered and managed by vCenter Server.
BACKUP SERVERS: HP DL580 G7 dedicated to DB and filesystem backups from data volume snaphots.
3 LEVELS BACKUP : L1 on primary storage array, L2 on disks (StoreOnce 6600) and L3 on tape libraries (HP ESL G3).
HPC INTERCONNECTION: access to HPC super computer at CINECA for dedicated processing.
L2
back-up
Dev&Test
Operation Platform
Collegamento diretto con sistemi HPC CINECA via MOU dedicato

## Slide 7
Generic Data Requests

## Slide 8
3. What is the Gaia Legacy?

## Slide 10
N. B. BAV= Biblioteca Apostolica Vaticana

## Slide 11
4. The transition: OPS4-TLS

## Slide 13
Oracle ZFS file system compatibile con DPCT.
(Current DPCT)

## Slide 16
5. Criticità
FTE stabilizzate ASI (supporto INAF alle operations  dalla EDR3 science driven)
Strettissimo controllo ASI sull’utilizzo fondi (tagli su miscellanea, HW….) : solo attività strettamente legate alle operations di Gaia finanziabili
Supporto (in «matching funds») di Dottorati : problema serio
Legacy (scientifica e tecnonologica –DPCT/OPS4/TLS)
Coinvolgimento di ma giusto equilibrio con Aziende
Con ASI

## Slide 17
Team Dedicato (FTE stabilizzate ASI, supporto INAF alle operations to 2030)
Strettissimo controllo ASI sull’utilizzo fondi (tagli su miscellanea, HW….) : solo attività strettamente legate alle operations di Gaia finanziabili
Supporto (in «matching funds») di Dottorati : problema serio
Coinvolgimento di ma giusto equilibrio con Aziende
……………….
Con INAF

## Slide 18
Central Governance/Coordination. Need for direct relations with Project PI’s (should a PI coordination panel be put into effect?)
Clear strategy on Legacy (science & technology –DPCTOPS4TLS)
Adequate Administrative support. Direct suppor from Headquarters (the role of «RUP»’s)?
PNRR?
……Con INAF