## Slide 1
ASTRI Mini-Array Status & Implementation
Giovanni Pareschi– INAF / Brera
INAF RSN4 - Nopoli – 24 Nov 2022

## Slide 2
The ASTRI Mini-Array Project
The ASTRI Mini-Array is a project whose purpose is to construct, deploy and operate an array of 9 Cherenkov telescopes of the 4 meters class at the Observatorio del Teide in Tenerife (Spain) in collaboration with IAC.
More than 150 researchers belonging to
  INAF institutes (IASF-MI, IASF-PA, OAS, OACT, OAB, OAPD, OAR)
  Italian Universities (Uni-PG, Uni-PD, Uni-CT, Uni-GE, PoliMi) & INFN
  Fundacion Galileo Galilei
  International institutions (IAC - Spain, University of Sao Paulo – Brazil, North-West University – South Africa, IAC – Spain, Université / Observatoire de Geneve - CH).
Italian and foreign industrial companies are involved in the ASTRI Mini-Array project with important industrial return.

## Slide 3
ASTRI: Astrophysics with Italian Replicating Technology Mirrors
ASTRI-Horn Prototype
INAF-led Project funded by Italian Ministry of Research
End-to-end prototype installed and operational on Mount Etna volcano (Sicily, Italy)
First detection of a gamma-ray source (Crab Nebula) above 5s with a dual-mirror, Schwarzschild-Couder Chrenkov telescope (Lombardi et al., 2020)
Array of 9 ASTRI telescopes
INAF-led Project with international partners: Univ. of Sao Paulo/FPESP (Brazil), North-West Univ. (S. Africa), IAC (Spain), FGG, ASI/SSDC, Univ. of Padova, Perugia and INFN
Being deployed at the Observatorio del Teide (Spain) in collaboration with IAC and FGG-INAF.
First 4 years  Core Science, following 4  Observatory Science. Science operation  2024

## Slide 4
Name given by Nanni Bignami
ASTRI - Astrofisica con Specchi a Tecnologia Replicante Italiana
Astrophysics with Mirrors via Italian Replication Technology
(No mirrors, no party!)

## Slide 5
INAF + Media Lario
Adventure started with MAGIC II (2006)
Principal Inventor: Oberto Citterio

## Slide 6: The Schwarzschild Aplanatic Telescope
1905: Karl Schwarzschild solved the Seidel ‘s equations for spherical aberration and coma finding a relation between parameters capable to make a telescope aplanatic. (Couder 1926  also correction of astigmatism with curved focal plane)
“For any geometry, 2 aspheric mirrors allow the correction of SI and SII to give an aplanatic telescope”
6
Technology challenge: Aspherical Optics manufacturing + large secondary mirror
Schwarzschild telescope
KS: f/3.0
bS1= -13.5 (Hyperbola)
bS2= 1.963 (Spheroid)
FoV:2.8 deg
RMSedge~12’’
Vladimir Vassiliev, UCLA

## Slide 7: Segmented reflecting surface
7
JWST, reflecting surface cost:  a few of M$/m2
ASTRI, reflecting surface cost:
 2.5 K$/m2
(see Canestrari et al., SPIE, 2014)
Credits: NASA
7

## Slide 8
ASTRI Camera
ASIC board
SiPM matrices
The SiPM produced by Hamamatsu photonics (7x7 mm2) grouped in matrices of 8x8 pixels
37 matrices are arranged to adapt to the curved focal plane of the telescope.
innovative electronics for peak detection(CITIROC ASICS , WEEROC-INAF) ⇒ smalls mount of data
Interferential filter as front window (Romeo et al. (2018) and Catalano et al. (2018)) that allows to reduce the contribution from the night sky background at wavelengths greater than 550 nm where the sensitivity of SiPM detector is still high.
FIELD OF VIEW OF 10.5 Deg IN DIAMETER

## Slide 9
24 September 2014

## Slide 10: The ASTRI-Horn results
Giro et al. 2017
Lombardi et al. 2020

## Slide 11: The NEW Mirrors
The new set of M1 DIE segments
The new M2 mirror

## Slide 12
THE SHOWERS
Ev# 13385
Size = 1110 pe
Ev# 13245
Size = 1193 pe
Ev# 17539
Size = 1081 pe
Ev# 12797
Size = 834 pe
Ev# 20556
Size = 1157 pe
Ev# 6643
Size = 927 pe
Ev# 1250
Size = 721 pe
P
Ev# 53900
Size = 1157 pe
P

P
P
P
P


## Slide 13
THE MUON

## Slide 14: The mini-array @Teide: the adventure starting!
14
12 June 2019

## Slide 15
ASTRI Mini-Array @ Teide Observatory
L.A. Antonelli – ASTRI Mini-Array – ICRC 2021
29/06/2021

## Slide 16
Infrstructure… 1 year ago

## Slide 17
Infrastructure: foundations

## Slide 18
Infrastructure
ASTRI-1
ASTRI 5
ASTRI-3
ASTRI-9
ASTRI-2
ASTRI-6
ASTRI-7
Infrastructure delivery:
18th of November

## Slide 19: Telescope pre-assembly & testing at the EIE GROUP workshop (Mira, Venezia)
I/F Cabinet

## Slide 20
ASTRI-1 on site integration
Telescope integration takes 3-4 weeks (working days) including:
Base grouting 2-3 days
M1 panels integration 2 days
M2 mirror integration 2 days
Acceptance at the end of January 2023

## Slide 21
ASTRI-1
Optical support structure
1st truck leaving 6/6/2022
Photo CREDITS Tommaso Marchiori

## Slide 22
The ASTRI Mini-Array locations
The ASTRI Mini-Array in Tenerife
Telescope Array & auxiliaries (Observatorio del Teide - OT)
Local Control Room @ THEMIS building (OT)
On site Data Centre @ IAC Teide Residencia (OT)
Array operation center @IACTEC in La Laguna
The ASTRI Mini-Array in Italy
Data Centre in Rome
Remote Array operation centers

## Slide 24
The ASTRI Mini-Array – Performance
Sensitivity: better than current IACTs (E ≳ 3 TeV)
  Extended spectrum and cut-off constraints
Energy/Angular resolution: ~10% / ~0.05° (E =10 TeV)
  Identify and characterize extended sources morphology
10° field of view with homogeneous off-axis performance
  Multi-target fields, surveys, and extended sources
  Enhanced chance for serendipitous discoveries
Vercellone et al., to be submitted
PRELIMINARY
PRELIMINARY

## Slide 25
The LHAASO PeVatrons
Cao et al., 2021, Nature
The ASTRI Mini-Array will investigate these and future PeVatron sources providing important information on their identification and morphology
Discovery of 12 sources emitting at several hundreds of TeV, up to 1.4 PeV
Crab apart, the majority of remaining sources represent diffuse g-ray structures with angular extensions up to 1°, and all of them are located along the Galactic plane
The actual sources responsible for the ultra high-energy g-rays have not yet been firmly localized and identified (except for the Crab Nebula), leaving open the origin of these extreme accelerators

## Slide 26
Stellar Intensity Interferometry with the ASTRI Mini-Array
Imaging (aperture synthesis) with unprecedented angular resolution!!!
Monnier et al. (2014)
ASTRI SI3 can image many A/B-type stars in visible light, extending the sample collected with CHARA in the IR CREDITS: L. Zampieri
CHARA/MIRC IR (H band) synthetized images of eps Aur (A9I)
Long partial eclipse of the star eps Aur produced by an absorber with a disc-like geometry
Kloppenborg et al. (2010)

## Slide 27
The ASTRI White Book
Le IRF di ASTRI sono appena state pubblicate su Zenodo
«ASTRI Project. (2022). ASTRI Mini-Array Instrument Response Functions (Prod2, v1.0)»
https://zenodo.org/record/6827882#.YtFCjZNBx60 - DoI: 10.5281/zenodo.6827882

## Slide 28
ASTRI Mini-Array implementation timeline
Timeline based on current available information
Teide infrastructure almost complete -> Contract closed next week
ASTRI-1 telescope site acceptance review in January 2023
ASTRI-8 & ASTRI-9 telescopes procurement ongoing
  Shipping to Tenerife end of March 2023
  Acceptance at the site end of May 2023
First Cherenkov camera (engineering camera)
   ready for lab test at the end of January 2023
   first Cherenkov light at the end of April 2023
First three telescopes (ASTRI-1, 8, 9) complete with cameras  summer 2023
Second batch of telescopes will start to arrive @ end of 2023
ASTRI Mini-Array ready for commissioning at the end of 2024
Scientific observations start mid 2025
Photo credits: Tommaso Marchiori (EIE group)

## Slide 29
High Energy (TeV to PeV) gamma-ray astronomy in the ’20 years of the new century
Hadronic accelleration seen up tp the PeV renergy in gamma.
Extended emission or some specific sources?
GRBs up to tens of TeVs
Ehi guys…HIC SUNT LEONES!
GHE MINGA ASTRI?