## Slide 1
Tunable Imaging Spectropolarimeters and Fixed-Band Imagers for the European Solar Telescope
Luis Bellot Rubio1, Francisco J. Bailén1, Javier Sánchez1, J.C. del Toro Iniesta1, Luca Giovannelli2, Francesco Berrilli2, Matteo Munari3, Ilaria Ermolli3, Göran Scharmer4, Mihalis Mathioudakis5
1Instituto de Astrofísica de Andalucía (IAA-CSIC), 2Università di Roma Tor Vergata, 3Istituto Nazionale di Astrofisica (INAF), 4Institute for Solar Physics (Stockholm University), 5Queen’s University Belfast

## Slide 2: EST and the TIS/FBI instruments
  Largest telescope ever built in Europe (4.2 m)
  Optimized to study the magnetic and dynamic coupling of the solar atmosphere
  Simultaneous measurement of photospheric and chromospheric magnetic fields
  45% of programs in EST SRD require large FOVs
  TIS/FBIs: etalon-based imaging spectropolarimeters, covering three spectral bands (380-500, 500-680, 680-1000 nm)

## Slide 3
Ca 8542
Mg 5173
Low chromosphere
SST/CRISP
Fe 6173
Upper photosphere
Low photosphere
Q
I
U
V
Gošić et al, ApJ, 2021

## Slide 4: TIS/FBI scientific requirements
Tunable Imaging Spectropolarimeters (TIS) and Fixed-Band Imagers (FBI) are part of same instrument
Operation modes (simultaneous) | Narrowband spectropolarimeter (TIS) Broadband context imager (FBI)
Spatial resolution | Diffraction-limited. Critical sampling: 0.010” at 396 nm, 0.013” at 517 nm, 0.017” at 854 nm
FOV | 60” diameter circular
Tunable | 4-5 spectral lines in each spectral arm
Resolving power | 50 000 at 396 nm, 100 000 at 630 nm, 80 000 at 854 nm
Spectral sampling | 10 wavelength positions per line (goal: 20 positions)
Scanning time | 10 s per spectral line
Polarimetry (TIS mode) | Polarimetric sensitivity of 10-3 Dual-beam to reduce seeing-induced crosstalk
Operation modes (simultaneous) | Narrowband spectropolarimeter (TIS) Broadband context imager (FBI)
Spatial resolution | Diffraction-limited. Critical sampling: 0.010” at 396 nm, 0.013” at 517 nm, 0.017” at 854 nm
FOV | 60” diameter circular
Tunable | 4-5 spectral lines in each spectral arm
Resolving power | 50 000 at 396 nm, 100 000 at 630 nm, 80 000 at 854 nm
Spectral sampling | 10 wavelength positions per line (goal: 20 positions)
Scanning time | 10 s per spectral line
Polarimetry (TIS mode) | 

## Slide 5: TIS/FBI concept
Pre-filter allows only a narrow spectral band (~0.5 nm) to enter the instrument
Light divided between TIS (95%) and FBI (5%)
TIS channel
  Polarization modulation using 2 nematic LCVRs
  Spectral analysis by dual-FPI system
  Polarization analysis using polarizing BS
FBI channel
  Focused camera for image reconstruction (MOMFBD)
  Defocused camera to extend MOMFBD with Phase Diversity (Scharmer et al. 2010; Löfdahl & Hillberg 2022)
FW: filter wheel
BS: beam splitter
LCVRs: Liquid crystal variable retarders
FPI: Fabry-Pérot interferometer
F: focal plane
FW
BS
BS
BS
FPI
FPI
F (focused)
F (def)
F
F
LCVRs
TIS
FBI
Light from telescope

## Slide 6: FPI optimization
High image quality (Strehl > 95%): telecentric mount
Small pupil apodization effects: F-ratio of 147 at etalons
Required FOV: 60” circular
Required resolving power: R=100 000 at 630 nm
Very low parasitic light (<1%)
High transmission at peak wavelength (>90%)
Reflectivities/cavity ratios chosen as in Scharmer (2006)
Etalon clear aperture | 180 mm
Cavity ratio (d2/d1) | 0.382
Reflectivities | FP1: 94%. FP2: 86%
Assumed rms cavity error | 2 nm
Parasitic light | 0.91%
Transm. at peak wavelength | 93.5%
Strehl at optimum refocus | 95.8%
FWHM for f/147 | 6.41 pm (R = 98,300)
TIS-V specs (at 630.2 nm)
Optimization drivers
ICOS ET150
Courtesy: UTOV
Carried out by G. Scharmer (ISP)
Notes: Very low parasitic light (< 1%): optimization of cavity ratio, reflectivities and prefilter width
Parasitic light decreases with increasing reflectivities of FP1 and FP2
Transmission at peak wavelength decreases with increasing reflectivity of FP2
Strehl at optimum refocus decreases with increasing reflectivity of FP1

## Slide 7: TIS optical design
First design by UTOV, updated by ISP
Simple, all-refractive design similar to CRISP/CHROMIS
Etalons illuminated with f/147 telecentric beam to reduce pupil apodization problems (Beckers 1998, von der Lühe & Kentischer 2000, Bailén et al. 2020)
No folding mirrors needed
  High throughput, no instrumental polarization
  Compact linear design, ~4700 mm for each TIS
  Etalons mounted vertically: same deformation as horizontally (Greco et al. 2022)
FW
BS
FP1
FP2
Transfer optics
F3
IM
F
F3: focal plane provided by telescope (f/50)
FW: filter wheel
LCVRs: Pol modulator
BS: beam splitter
IM: intermediate image plane (f/147)
FP: Fabry-Pérot etalon
F: final focal plane
LCVRs
BS
Transfer optics

## Slide 8: TIS optical design
Total instrument transmission
  TIS-B: 46.7%
  TIS-V: 63.2%
  TIS-R: 67.3%
Challenges
  FOV of 60” on sky creates beam of 61 mm diameter at F3
  Prefilters and LCVRs need to have 65 mm clear aperture
FW
BS
FP1
FP2
Transfer optics
F3
IM
F
F3: focal plane provided by telescope (f/50)
FW: filter wheel
LCVRs: Pol modulator
BS: beam splitter
IM: intermediate image plane (f/147)
FP: Fabry-Pérot etalon
F: final focal plane
LCVRs
BS
Transfer optics

## Slide 9: TIS-V image quality
Diffraction-limited design
Airy disk
Strehl ratios for TIS-V with 12 mm pixels
Notes: This is a very good design also in terms of optical quality…

## Slide 10: FBI optical design
FBI provides broad-band images at very high cadence
Also used to correct TIS/FBI observations for seeing effects and telescope aberrations (MOMFBD-PD)
Design recipe (based on CRISP/CHROMIS)
  Similar TIS and FBI channels introduce similar optical aberrations
  The two large doublets can be excluded as they have a limited impact on the aberrations
TIS (~ 4.7 m)
FBI (~ 1.4 m)

## Slide 11: FBI-V image quality
Diffraction-limited design
Airy disk
Strehl ratios for FBI-V with 12 mm pixels
Notes: This is a very good design also in terms of optical quality…

## Slide 12
TIS ( m)
FBI (m)
F3
TIS (~ 4.7 m)
FBI (~1.4 m)

## Slide 13: Summary
TIS/FBI capabilities in a nutshell
  Excellent optical quality (diffraction-limited)
  10-3 polarimetric sensitivity
  Large FOV: 60” circular
  Powerful diagnostics: observation of three spectral lines simultaneously at very high cadence
  Simple (all-refractive) design, high throughput
  Moderate dimensions (4.7m x 1.4m)
Challenges
  Large-format etalons (cost driver and difficult to manufacture)
  Large-format prefilters and LCVRs (difficult to manufacture, slow switching times)
  Data rate per TIS/FBI ( detectors of 6k x 6k at 30 fps): ~100 TB/hour (raw)
Current status
  Preparing for CoDR (early 2025): finalizing optical design, detector selection, cost estimate