## Slide 1: LEM-X Lunar Electromagnetic Monitor in X-rays
Y. Evangelista INAF-IAPS
on behalf of the EMM/LEM-X Team
LGWA Workshop – 8 October 2024

## Slide 2
A high performance, wide FoV, X-ray monitor is essential to provide prime observation
of the violent high-energy sky
Photon-based Astronomy is now integrated into the broader multi-messenger framework, together with GWs, neutrinos and cosmic-rays
Interesting phenomena for multi-messenger Astronomy are produced in transient events and variable sources, thus require the simultaneous observation of all the sky
The Moon offers an interesting platform for an all-sky X-ray monitor since we can install larger and heavier instruments than on a satellite. The all-sky coverage can be obtained by exploiting the rotation of the Moon itself

## Slide 3
What we need:
High energy (100 keV – 102 keV)
Large instantaneous FoV (goal π/2π steradians)
All sky coverage/long continuous observations
Arcmin-level angular res.
Sub-arcmin level PSLA
Moderate/large effective area (102 cm2)
Good sensitivity (1 Crab in 1s)
Photon-by-photon capability
Good energy resolution (better than 500eV @ 6 keV)
High time resolution (better 10 µs)
Low (~negligible) dead time
What does our MOON offer?

## Slide 4
What we need:
High energy (100 keV – 102 keV)
Large instantaneous FoV (goal π/2π steradians)
All sky coverage/long continuous observations
Arcmin-level angular res.
Sub-arcmin level PSLA
Moderate/large effective area (102 cm2)
Good sensitivity (1 Crab in 1s)
Photon-by-photon capability
Good energy resolution (better than 500eV @ 6 keV)
High time resolution (better 10 µs)
Low (~negligible) dead time
What does our MOON offer?
No atmosphere

## Slide 5
What we need:
High energy (100 keV – 102 keV)
Large instantaneous FoV (goal π/2π steradians)
All sky coverage/long continuous observations
Arcmin-level angular res.
Sub-arcmin level PSLA
Moderate/large effective area (102 cm2)
Good sensitivity (1 Crab in 1s)
Photon-by-photon capability
Good energy resolution (better than 500eV @ 6 keV)
High time resolution (better 10 µs)
Low (~negligible) dead time
What does our MOON offer?
No atmosphere
Full-sky (equator)/half sky (poles) accessibility
Stable environment
~Continuous operation

## Slide 6
What we need:
High energy (100 keV – 102 keV)
Large instantaneous FoV (goal π/2π steradians)
All sky coverage/long continuous observations
Arcmin-level angular res.
Sub-arcmin level PSLA
Moderate/large effective area (102 cm2)
Good sensitivity (1 Crab in 1s)
Photon-by-photon capability
Good energy resolution (better than 500eV @ 6 keV)
High time resolution (better 10 µs)
Low (~negligible) dead time
What does our MOON offer?
No atmosphere
Full-sky (equator)/half sky (poles) accessibility
Stable environment
~Continuous operation
Resources (volume, power, telemetry)
Modular assembly capability
Instrument serviceability

## Slide 7
What we need:
High energy (100 keV – 102 keV)
Large instantaneous FoV (goal π/2π steradians)
All sky coverage/long continuous observations
Arcmin-level angular res.
Sub-arcmin level PSLA
Moderate/large effective area (102 cm2)
Good sensitivity (1 Crab in 1s)
Photon-by-photon capability
Good energy resolution (better than 500eV @ 6 keV)
High time resolution (better 10 µs)
Low (~negligible) dead time
What does our MOON offer?
No atmosphere
Full-sky (equator)/half sky (poles) accessibility
Stable environment
~Continuous operation
Resources (volume, power, telemetry)
Modular assembly capability
Instrument serviceability
“Mild” radiation environment (wrt high elliptical orbits) and/or possibly stable low temperature

## Slide 8
→ The coded-mask technique is not yet surpassed for wide FoV imaging with large Eff
Each detector pixel detects photons from the whole FoV. Coded-mask camera requires that every sky position is uniquely encoded on the detector
How?

## Slide 9
Coded-mask assembly
Collimator assembly
Detector tray assembly
Micrometeoroid filter
Digital electronics/PSU

## Slide 10
The Lunar Electromagnetic Monitor in X-rays (LEM-X) project aims at developing a large, permanent X-ray observatory.
The instrument is a coded-aperture all-sky monitor, operating in the X-ray energy band (2–50 keV).
Each LEM-X camera is equipped with four large-area Silicon Drift Detectors (SDDs) and is capable of monitoring and imaging the high-energy sky in a 1sr field-of-view

## Slide 11
The high-resolution SDD detection plane will allow for a source localization accuracy of ~1 arcmin and a spectral resolution better than 350 eV FWHM at 6 keV, with a sensitivity better than 5 mCrab in 50 ks and 1 Crab in 1 s.
Each LEM-X module is:
Autonomous (with integrated BEE and PSU electronics)
Compact (about 35×35×35 cm3)
Light-weight (~15 kg)
With low power consumption (15 W).

## Slide 12
LEM-X in the context of EMM
LEM-X is an Italian R&D project aiming to build the foundation for an Astrophysics instrument on the surface of the Moon
LEM-X belongs to the Earth-Moon-Mars (EMM) project funded by MUR and lead by INAF under PNRR (Next Generation EU)
The project relies on the heritage and technology readiness of the WFM aboard eXTP

## Slide 13
In the contest of the Italian National Recovery and Resilience Plan (PNRR/NRRP), INAF is now developing the LEM-X detector tray, composed by 4× Detector Assemblies (DA) based on the heritage of the WFM designed for the Sino-European mission eXTP.
Project will be completed by 0612/2025.
The DA is based on the Large-Area Silicon Drift Detectors (monolithic 7x7 cm2 sensors) designed & developed by a collaboration involving INFN, INAF and FBK
The read-out (AFE) and ADC (DFE) ASICs design rely on the heritage of the VEGA, LYRA and ORION ASICs developed by PoliMi and UniPV in the framework of the ReDSoX collaboration (+HERMES, +THESEUS)
The AlO2 thick-film FEE PCB is being developed to ensure electrical and thermoelastic (i.e. alignment) performance

## Slide 14
Field of View: 1.0 sr (50% effective area)
Angular res. < 4.7 arcmin
PSLA: < 1 arcmin PSLA
Sensitivity: 1 Crab/1s, 4.5 mCrab/50 ks
Energy band: 2-50 keV
Energy res.: <350 eV FWHM @ 6 keV
Eff. area: 80 cm2 @ 6 keV (on-axis)
Time resolution: < 7 µs
Dead time: < 1% @ 10 Crab
LEM-X camera anticipated performance

## Slide 15
Camera pair sensitivity – 1s
Single camera monthly exposure

## Slide 16
Instrument monthly exposure vs observation latitude (0°, -70°, -90°)

## Slide 17: Comparison between THESEUS and LEM-X
 | THESEUS | LEM-X
Payload | 2 Soft X-ray Imagers 2 X/Gamma Imaging Spectrometers InfraRed Telescope | 7 camera pairs
Energy band(s) | SXI: 0.3 – 5 keV XGIS: 2 keV – 10 MeV IRT: 0.7 – 1.8 m | 2 – 30 keV
Field of View | SXI: 0.5 sr – 31x61 degrees2 XGIS: 2 sr (2 – 150 keV) – 117x77 degrees2 4 sr (>150 keV) | 1 sr per camera 2 sr overall
Source Location Accuracy | SXI: ≤ 2 arcminutes (99 % c.l.) XGIS: ≤ 7 arcminutes (90 % c.l.) | 1 arcmin
Sensitivity (XGIS) | 10-8 erg/cm2/s (2 – 30 keV) 3x10-8 erg/cm2/s (30 – 150 keV) 2.7x10-7 erg/cm2/s (150 keV – 1 MeV) | 2.1x10-8 erg/cm2/s (2 – 50 keV, 1 s at 3) 9.4x10-11 erg/cm2/s (2 – 50 keV, 50 ks at 3)

## Slide 18: Expected transient rates in LEM-X
 | Expected rate
X-ray Bursts | 5000 events/year
X-ray Flashes | 50 – 60 events/year
Gamma Ray Bursts | 190 events/year
Gamma Ray Bursts at z > 6 | 2 – 3 events/year

## Slide 19
Thank you

## Slide 20
GRB 090618 - BB+PL vs Band
GRB detection sensitivity in terms of peak flux sensitivity as a function of the spectral peak energy Ep (Band, 2003) and cumulative Z distribution of long GRBs computed assuming a broken power-law luminosity function and a pure density evolution
Amati et al., 2015
GRB 090618 prompt spectrum (50s, FERMI/GBM)
Both
  Band function (white)
  Power-law plus black-body model (green)
equally fit the Fermi/GBM measured spectrum (red).
WFM observation (sim) allows to disentangle between the two spectral model

## Slide 21
Spin history
Super-orbital spectra
Orlandini et al., 2015
Long term continuous spin monitoring and single observation spectrum of the HMXB OAO 1657-415
Red/blue shifted Fe Kα fluorescence lines from the SS 433 precessing jets. in two different superorbital phases (p ~ 160d)

## Slide 22
High-energy (MeV) extension – HERMES-like?
Short
GBM
HERMES
HERMES-X
Ghirlanda, Nava, Fiore 2023
Long
GBM
HERMES
HERMES-X
Ghirlanda, Nava, Fiore 2023
Low-energy/high-sensitivity extension – Lobster-eye?