## Slide 1: The EARTH MOON MARS (EMM) PNRR project
Lunar and Martian
Simulation Chambers
INAF - OACN
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.

## Slide 2
EMM-PNRR project:
to study the electrostatic dust transport
to test the sensor LD GRIDS
Lunar Simulation Chamber
under development to characterize
the electrostatically levitating dust grains,
measuring their charge (Q > 1 fC)
and velocity (1-100 m/s)
Charging and transport of dust particles on dusty surface
exposed to plasmas and/or UV sources
[Wang et al., 2009-2016]
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.

## Slide 3
Open Questions
Does electrostatic levitation occur on the Moon? When? Where? At what rate?
What is the charge on a dust grain on the lunar surface? What is its velocity? What is its dynamics?
Motivation
Dust deposition on spacecraft poses a considerable threat to spacecraft
Electrostatic dust motion is a process that may influence the properties and the evolution of the Moon's surface
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.

## Slide 4
_
+
+
_
_
q

## Slide 5
To simulate the UV-induced photoemission
dust grains will be illuminated by an UV Lamp,
with λ = 172 nm,
i.e. Eph = 7.2 eV > the work function of the dusty surface (~ 5.5 eV)
To simulate the Solar wind effect
dust grains will be exposed to
Testing facility: Lunar Simulation Chamber
  an Electron Gun
  Beam energy: 10 - 1500 eV
  Beam diameter: 1 - 100 mm
  an Ion Gun
Beam energy: 0 - 3000 eV
Beam diameter: 5 - 25 mm
Electrostatic levitation
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.
Notes: To simulate the Solar wind effect
dust grains will be exposed to a thermal plasma
with an electron temperature of ~12 eV
with a proton temperature of ~10 eV
by exploiting:
an Electron Gun
Beam energy: 10 - 1500 eV
Beam diameter: 1 - 100 mm
an Ion Gun
Beam energy: 0 - 3000 eV
Beam diameter: 5 - 25 mm

## Slide 6
A high-voltage (up to ± 8 kV) gridded electrode
will be placed ~ 5 mm above the dusty surface to attract charged grains.
A system based on electrostatic lenses is being developed to accelerate the dust grains towards LDGRIDS under controlled conditions.
Testing facility: Lunar Simulation Chamber
LD GRIDS
LD GRIDS testing
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.

## Slide 7
Electron Gun
Ion Gun
UV Lamp
High-speed Camera
150.000 fps
6,5 µm/px
Sample 1
Sample 2
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.
To simulate the UV-induced photoemission
dust grains will be illuminated by an UV Lamp,
with λ = 172 nm,
i.e. Eph = 7.2 eV > the work function of the dusty surface (~ 5.5 eV)
To simulate the Solar wind effect
dust grains will be exposed to
Testing facility: Lunar Simulation Chamber
  an Electron Gun
  Beam energy: 10 - 1500 eV
  Beam diameter: 1 - 100 mm
  an Ion Gun
Beam energy: 0 - 3000 eV
Beam diameter: 5 - 25 mm
Electrostatic transport
Notes: To simulate the Solar wind effect
dust grains will be exposed to a thermal plasma
with an electron temperature of ~12 eV
with a proton temperature of ~10 eV
by exploiting:
an Electron Gun
Beam energy: 10 - 1500 eV
Beam diameter: 1 - 100 mm
an Ion Gun
Beam energy: 0 - 3000 eV
Beam diameter: 5 - 25 mm

## Slide 8
Testing facility: Lunar Simulation Chamber
Electron Gun
Ion Gun
UV Lamp
High-speed Camera
150.000 fps
6,5 µm/px
Sample 1
Sample 2
Subsystems
Giuseppe Mongelluzzo, Carmen Porto, Gabriele Franzese, Francesca Esposito, Ciprian Popa, Simone Silvestro.
Dust Charging System: UV lamps, Electron and Ion Gun.
Environmental sensors: Langmuir probe, Faraday Cup.
Gas injection system.
Sample holders.
High-voltage gridded electrode.
High-speed camera
Notes: To simulate the Solar wind effect
dust grains will be exposed to a thermal plasma
with an electron temperature of ~12 eV
with a proton temperature of ~10 eV
by exploiting:
an Electron Gun
Beam energy: 10 - 1500 eV
Beam diameter: 1 - 100 mm
an Ion Gun
Beam energy: 0 - 3000 eV
Beam diameter: 5 - 25 mm

## Slide 9
Why dust?

## Slide 10
Why dust?
Strong influence on Mars global climate
Global dust cycle
Dust storms, dust devils are relevant phenomena (also on Earth); dust storms can become global
Influence on instrumentation (and on human explorers?)
Why dust?

## Slide 11
  New subsystems
  Wind Tunnel: logaritmic wind profile up to ~15 m/s
  Thermal plate and sand bed: down to -80 °C
  Vertical Electrodes: up to ~150 kV/m
  UV radiation
  Environmental Sensors System: Faraday Cup and Langmuir probe
  Camera System: resolution up to 10 µm
  Controlled injection system
  All the new subsystems are removable, hence the chamber can always return to the original condition
Martian Simulation Facility
Grain Injection
Sandbed
UV
source
MicroMED
Faraday cup
Electrodes
Fan

## Slide 12
Martian Simulation Facility
Possible test: Dust lifting due to electrification
Notes: su Marte la causa principale del sollevamento è sempre il vento quindi la causa principale della carica dei grani sono gli urti tra loro e col terreno noi vogliamo vedere se quel poco di carica che gli da l'UV può abbassare un poco la threshold necessaria al vento il campo vero si genera dopo che i grani sono in moto (dovuto ai grani appunto) e vogliamo vedere se una volta avviato il processo il campo E e l'interazione coi grani può aiutare a tenerlo attivo anche quando il vento cala

## Slide 13
Martian Simulation Facility
Possible test: Martian instrumentation testing

## Slide 14
Martian Simulation Facility
Possible test: Instrumentation testing in presence of wind
Notes: Vogliamo ottenere efficienza con velocità vento
Qui disuniformità quantità polvere con velocità, e picco minimo a metà che è strano

## Slide 15
Martian Simulation Facility
Possible test: Sandbed evolution in presence of wind

## Slide 16
Thank you!
Thank you!
  Giuseppe Mongelluzzo; Carmen Porto;
  Osservatorio Astronomico di Capodimonte (INAF – OACN)
  giuseppe.mongelluzzo@inaf.it; carmen.porto@inaf.it;
  Contact us!