## Slide 1: USCVIII – General Assembly
Multivariate Time Series Forecasting for the ASTRI-Horn Historical Monitoring Data
Monday, 14 October 2024 - Friday, 18 October 2024 Galzignano Resort Terme & Golf
Federico Incardona*
Notes: Voglio ringraziare innanzitutto gli altri

## Slide 2
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
*Authors
Federico Incardonaa, Alessandro Costaa, Farida Farsiana, Francesco Franchinaa, Giuseppe Letoa, Emilio Mastriania, Kevin Munaria, Giovanni Pareschib, Salvatore Scuderic, Sebastiano Spinelloa, and Gino Tostid for the ASTRI Project1
aINAF, Osservatorio Astrofisico di Catania
bINAF, Osservatorio Astronomico di Brera
cINAF, Istituto di Astrofisica Spaziale e Fisica Cosmica di Milano
dUniversità di Perugia, Istituto di Astrofisica Spaziale e Fisica Cosmica
1http://www.astri.inaf.it/en/library/

## Slide 3
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
ASTRI-Horn for the Mini-Array
ASTRI Mini-Array will be 9 Cherenkov telescopes deployed at the Teide Observatory (Tenerife) of the SST class (~4 m) of the CTAO:
first light for the first telescope in Tenerife (ASTRI 1)
ASTRI-Horn prototype deployed and operated in Serra La Nave (Mt. Etna, Sicily) since late 2017
ASTRI Horn – Mt. Etna

## Slide 4
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
ASTRI-Horn Database
+-----------------+------------------+
| Monitoring database |
+-----------------+------------------+
| Assembly | Number of tables |
+-----------------+------------------+
| ASC | 16 |
| CameraControl | 91 |
| ICT_ICMP | 37 |
| PMC | 50 |
| SQM | 11 |
| TCU | 110 |
| THCU | 85 |
| WS | 21 |
| WeatherStation | 29 |
| WeatherStation1 | 28 |
| logbook | 1 |
+-----------------+------------------+
+---------+----------+
| Field | Type |
+---------+----------+
| timetag | bigint |
| value | char(30) |
+---------+----------+
479 tables each one corresponding to a time series of a monitored property (sampling rate corresponding to ~ 15 sec)
Notes: The CHAR data type stores character data in a fixed-length field. Data can be a string of single-byte or multibyte letters, numbers, and other characters that are supported by the code set of your database locale.

## Slide 5
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
ASTRI-Horn Database
+-----------------+------------------+
| Monitoring database |
+-----------------+------------------+
| Assembly | Number of tables |
+-----------------+------------------+
| ASC | 16 |
| CameraControl | 91 |
| ICT_ICMP | 37 |
| PMC | 50 |
| SQM | 11 |
| TCU | 110 |
| THCU | 85 |
| WS | 21 |
| WeatherStation | 29 |
| WeatherStation1 | 28 |
| logbook | 1 |
+-----------------+------------------+
+---------+----------+
| Field | Type |
+---------+----------+
| timetag | bigint |
| value | char(30) |
+---------+----------+
479 tables each one corresponding to a time series of a monitored property (sampling rate corresponding to ~ 15 sec)
Notes: The CHAR data type stores character data in a fixed-length field. Data can be a string of single-byte or multibyte letters, numbers, and other characters that are supported by the code set of your database locale.

## Slide 6
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Feature selection
We focused on a subset of 47 features from TCU and THCU by selecting only those that were related to the motors
ASTRI-Horn is moved by three-phase motors:
one for elevation
two for Azimuth (master and slave)
+-----------------+------------------+
| Monitoring database |
+-----------------+------------------+
| Assembly | Number of tables |
+-----------------+------------------+
| ASC | 16 |
| CameraControl | 91 |
| ICT_ICMP | 37 |
| PMC | 50 |
| SQM | 11 |
| TCU | 110 |
| THCU | 85 |
| WS | 21 |
| WeatherStation | 29 |
| WeatherStation1 | 28 |
| logbook | 1 |
+-----------------+------------------+

## Slide 7
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Active intervals selection
We selected only those time intervals when at least one of the motors was active
257609 rows × 47 columns; 346 intervals
Notes: Questo grafico mostra un istogramma della distribuzione dell’ampiezza degli intervalli attivi in minuti,
Come si vede da questo picco abbiamo molti intervalli brevi (tra 1 e 50 minuti)
Poi degli altri tra i 50 minuti e 600 minuti (circa 10 ore)
Ci sono invece pocchissimi intervalli lunghi, diciamo con una durata superiore alle 10 ore

## Slide 8
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
PdM Strategy
Since 2017 there have been three known faults involving the three-phase ASTRI motors:
May 2019: water infiltration caused a block in the Azimuth master motor November 2021: slow degradation of the Azimuth encoder tape
February 2022: condensation caused a block in the elevation motor
There is not enough evidence of degradation in the time series corresponding to these three faults
There is instead a fair amount of normal data starting from September 2022
We aim to develop a Normal Behaviour Model for the telescope’s time series
In this way, it is possible to build a PdM application that constantly compares, for each target feature, the actual measured values and the predicted ones and raises an alarm every time there is a deviation from the model

## Slide 9
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Regressor
The Multi-Layer Perceptron (MLP) Regressor is a fully connected neural network (NN) used for regression tasks, designed to predict continuous values.
Feedforward Neural Network: data flows in one direction, from input to output
Hidden Layers: enable the model to capture complex patterns in data
Activation Functions: introduce non-linearity to the model by determining whether a neuron should be activated or not based on its input
Backpropagation: training method that adjusts weights based on prediction errors using gradient descent
Notes: Each layer consists of neurons (nodes) connected by weights, using activation functions to introduce non-linearity.
2. Key Features:
• Feedforward Neural Network: Data flows in one direction, from input to output.
• Hidden Layers: Enable the model to capture complex patterns in data.
• Activation Functions: introduce non-linearity to the model, enabling it to learn and approximate complex patterns by determining whether a neuron should be activated or not based on its input.
Common choices include ReLU (Rectified Linear Unit) or tanh for hidden layers.
• Backpropagation: Training method that adjusts weights based on prediction errors using gradient descent.
Nel contesto delle reti neurali artificiali, il rettificatore è una funzione di attivazione definita come la parte positiva del suo argomento: f(x)=x+=max,
𝑓(𝑥)=𝑥+=max,
dove x è l'input a un neurone. È anche annoverata tra le funzioni rampa ed è l'analogo di un raddrizzatore in elettronica

## Slide 10
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Multivariate Forecasting (MF)
Make predictions of all the time series at the same time within the so-defined data window:
total window length (L) = input samples (I) + offset samples (O)
O is the actual prediction window corresponding to the time prior to the system fault within which the maintainer must be alerted
Tried several combinations of I and O
Limited by the high number of short intervals
Used sliding window approach
Increase the number of intervals and samples for the NN training
Notes: O deve tendere ad essere quanto più grande più possibile in modo che l’operatore sia informato quanto prima possibile

## Slide 11
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP architecture tuning
hidden_layer_sizes:
[100, 50]
[320, 160, 80]
[1440, 720, 360]
[1440, 720, 720, 360]
[1440, 720, 360, 180, 90, 40]
[5760, 2880, 1440]
[5760, 11520, 2880]
We tried several combinations of input (I) and offset (O) samples, in the two cases with and without outliers:
In each case, we tested the following NN architectures:
75 s + 15 s | 20 min + 5 min | 5h + 1h
Notes: Ciascu

## Slide 12
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 20 min + 5 min

## Slide 13
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 5h + 1h

## Slide 14
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 20 min + 5 min

## Slide 15
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 20 min + 5 min

## Slide 16
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Residuals
L = 20 min + 5 min

## Slide 17
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Longer intervals improve the metrics
Outliers remotion improve the metrics
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
La rimozione degli outliers migliora il modello

## Slide 18
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Longer intervals improve the metrics
Outliers remotion improve the metrics
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
La rimozione degli outliers migliora il modello

## Slide 19
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Longer intervals improve the metrics
Outliers remotion improve the metrics
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
La rimozione degli outliers migliora il modello

## Slide 20
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Longer intervals improve the metrics
Outliers remotion improve the metrics
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
la rimozione degli outliers migliora il modello
Rimuovendo gli outleiers otteniamoin un buon agreement nel caso di un intervallo di predizione di un’ora

## Slide 21
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Longer intervals improve the metrics
Outliers remotion improve the metrics
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
la rimozione degli outliers migliora il modello
Rimuovendo gli outleiers otteniamoin un buon agreement nel caso di un intervallo di predizione di un’ora

## Slide 22
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.218 | 6.737 | 0.191 | 4.920 | 0.198 | 2.810 | 0.133 | 2.470
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 160, 60) | 0.218 | 5.419 | 0.195 | 5.942 | 0.187 | 3.338 | 0.169 | 3.432
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(1440, 720, 360) | 0.124 | 4.026 | 0.109 | 4.208 | 0.113 | 1.144 | 0.104 | 1.123
L = 5 h 50 min + 10 min |  |  |  |  |  |  |  | 
(1440, 720, 360, 180, 90, 40) | 0.146 | 3.852 | 0.134 | 3.983 | 0.124 | 1.394 | 0.114 | 1.127
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MLP Results
Best results in the case of 5h + 1h with no outliers
Notes: Riportiamo in questa tabella l’architettura che ha dato i risultati migliori
Notiamo che
otteniamo migliori predizioni con input samples lunghi ma abbiamo visto che il risultato non migliora aumentando ancora l’input samples a scapito dell’offeset samples
La rimozione degli outliers migliora il modello

## Slide 23
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
LSTM model
The Long short-term memory (LSTM) is a type of recurrent neural network (RNN)
Connections exploit feedback loops to process sequential data, allowing information to be retained between time steps
Uses memory cells and gates (input, forget, output) to decide what information to keep, update, or forget
Able to capture long-term dependencies
Notes: Una rete neurale ricorrente o RNN (recurrent neural network) è una classe di rete neurale artificiale che include neuroni collegati tra loro in un ciclo. Tipicamente i valori di uscita di uno strato di un livello superiore sono utilizzati in ingresso di uno strato di livello inferiore.

## Slide 24
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
LSTM architecture tuning
hidden_layer_sizes:
- [50]
- [100]
- [360]
- [720]
[1440]
num_layers:
- 1
- 2
- 3
- 4
- 5
For each combination of input (I) and offset (O) samples, in the two cases with and without outliers, we tested the following NN architectures:

## Slide 25
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
LSTM results
 |  |  |  |  | Outliers remotion |  |  | 
 | Test MSE | Test MAPE | Train MSE | Train MAPE | Test MSE | Test MAPE | Train MSE | Train MAPE
L = 75 s + 15 s |  |  |  |  |  |  |  | 
(360, 360) | 0.248 | 6.816 | 0.096 | 2.940 | 0.226 | 3.691 | 0.107 | 2.691
L = 20 min + 5 min |  |  |  |  |  |  |  | 
(320, 360) | 0.383 | 8.764 | 0.386 | 8.386 | 0.162 | 2.803 | 0.155 | 2.864
L = 5 h + 1 h |  |  |  |  |  |  |  | 
(360, 360) | 0.114 | 5.585 | 0.090 | 4.820 | 0.096 | 1.167 | 0.081 | 1.055
Almost the same results as in the previous case
Notes: Ciascu

## Slide 26
Improve the outliers removal process
Try other algorithms, e.g., autoencoders
Develop the PdM software application
Test it on ASTRI-Horn
Use the new ASTRI 1 Monitoring Data
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Next steps
Notes: Rimozione delle variabili correlate per la riduzione del database

## Slide 27
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Thank you

## Slide 28
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Residuals
L = 5h + 1h

## Slide 29
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 75 s + 15 s

## Slide 30
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Plot
L = 75 s + 15 s

## Slide 31
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
MF Residuals
L = 75 s + 15 s

## Slide 32
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Feature correlation
 | Feature_1 | Feature_2 | Pearson
0 | TCU_AZSLAVETORQUE | TCU_AZSLAVECURRENT | 0.998421
1 | TCU_AZMASTERTORQUE | TCU_AZMASTERCURRENT | 0.997397
2 | THCU_PH3ENERGY | THCU_PH2ENERGY | 0.996919
3 | TCU_ELMOTORTORQUE | TCU_ELMOTORCURRENT | 0.994627
4 | THCU_PH2ENERGY | THCU_PH1ENERGY | 0.993376
5 | THCU_PH3ENERGY | THCU_PH1ENERGY | 0.991244
6 | THCU_PH3FREQUENCY | THCU_PH1FREQUENCY | 0.985690
7 | THCU_PH3FREQUENCY | THCU_PH2FREQUENCY | 0.985656
8 | THCU_PH2FREQUENCY | THCU_PH1FREQUENCY | 0.985536
2-sigma correlated features
Pearson coefficient
Notes: Example: 1 sigma -> 0.6827, 2 sigma -> 0.9545, 3 sigma -> 0.9973.

## Slide 33
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Residual Plot Explanation

## Slide 34
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Evalutaion metrics
Notes: Mean squared error
R2 score

## Slide 35
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Single Points Model (SPM)
Treat each point as independent from the others
Hyperparameter optimization over different shapes of the NN (hidden layers)

## Slide 36
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Forecast Plot

## Slide 37
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Forecast Plot

## Slide 38
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Residuals Plot

## Slide 39
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Results
 | Test MSE | Test R2 | Train MSE | Train R2
TCU_AZ_MASTERCURRENT |  |  |  | 
(160, 320, 80) | 0.0018 | 0.998 | 0.0017 | 0.998
5 Sigma outliers remotion |  |  |  | 
(160, 320, 80) | 0.0038 | 0.996 | 0.0011 | 0.999
2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0142 | 0.986 | 0.0059 | 0.994
5 Sigma outliers remotion; 2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0235 | 0.978 | 0.0074 | 0.993
Slight worsening due to outliers remotion
Slight worsening due to the remotion of the correlated features

## Slide 40
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
Slight worsening due to outliers remotion
Slight worsening due to the remotion of the correlated features
SPM Results
 | Test MSE | Test R2 | Train MSE | Train R2
TCU_AZ_MASTERCURRENT |  |  |  | 
(160, 320, 80) | 0.0018 | 0.998 | 0.0017 | 0.998
5 Sigma outliers remotion |  |  |  | 
(160, 320, 80) | 0.0038 | 0.996 | 0.0011 | 0.999
2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0142 | 0.986 | 0.0059 | 0.994
5 Sigma outliers remotion; 2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0235 | 0.978 | 0.0074 | 0.993

## Slide 41
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Results
Slight worsening due to outliers remotion
Slight worsening due to the remotion of the correlated features
 | Test MSE | Test R2 | Train MSE | Train R2
TCU_AZ_MASTERCURRENT |  |  |  | 
(160, 320, 80) | 0.0018 | 0.998 | 0.0017 | 0.998
5 Sigma outliers remotion |  |  |  | 
(160, 320, 80) | 0.0038 | 0.996 | 0.0011 | 0.999
2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0142 | 0.986 | 0.0059 | 0.994
5 Sigma outliers remotion; 2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0235 | 0.978 | 0.0074 | 0.993

## Slide 42
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Results
Slight worsening due to outliers remotion
Slight worsening due to the remotion of the correlated features
 | Test MSE | Test R2 | Train MSE | Train R2
TCU_AZ_MASTERCURRENT |  |  |  | 
(160, 320, 80) | 0.0018 | 0.998 | 0.0017 | 0.998
5 Sigma outliers remotion |  |  |  | 
(160, 320, 80) | 0.0038 | 0.996 | 0.0011 | 0.999
2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0142 | 0.986 | 0.0059 | 0.994
5 Sigma outliers remotion; 2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0235 | 0.978 | 0.0074 | 0.993
Notes: Questo comportamento non è atteso

## Slide 43
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
SPM Results
Slight worsening due to outliers remotion
Slight worsening due to the remotion of the correlated features
 | Test MSE | Test R2 | Train MSE | Train R2
TCU_AZ_MASTERCURRENT |  |  |  | 
(160, 320, 80) | 0.0018 | 0.998 | 0.0017 | 0.998
5 Sigma outliers remotion |  |  |  | 
(160, 320, 80) | 0.0038 | 0.996 | 0.0011 | 0.999
2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0142 | 0.986 | 0.0059 | 0.994
5 Sigma outliers remotion; 2 Sigma correlated variables remotion |  |  |  | 
(160, 320, 80) | 0.0235 | 0.978 | 0.0074 | 0.993
Notes: I valori per il train set sono molto migliori rispetto al test set

## Slide 44
Federico Incardona, USCVIII – General Assembly, 14-18 October 2024, Galzignano Resort Terme & Golf
TCU_AZMASTERCURRENT