## Slide 1: WP5 – Task 2 Software & algorithm
Review Meeting
Giovedì 12 Settembre - Venerdì 13 Settembre
Radiotelescopi di Medicina
IRA - Bologna
P. Di Lizia, M.F. Montaruli

## Slide 2
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Pierluigi Di Lizia
Marco Felice Montaruli

## Slide 3
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Pierluigi Di Lizia
Marco Felice Montaruli

## Slide 4: BIstatic Radar for Leo Survey (BIRALES)
Angular profile
Slant Range
Doppler Shift
RFT
Northern Cross
RFT
(Sardinia)
Northern Cross
(Bologna)

## Slide 5: BIRALES: MULTIBEAM APPROACH
Medicina (Bologna)
Salto di Quirra
(Sardinia)
Static beamforming [1]
Disadvantage: both main lobes and grating lobes appear in sensor FoV
Angular profile
[1] M. Losacco et al., Acta Astronautica, 2020
Beam 1
Beam 2

## Slide 6: BIRALES: MULTIBEAM APPROACH
Medicina (Bologna)
Salto di Quirra
(Sardinia)
Disadvantage: both main lobes and grating lobes appear in sensor FoV
Angular profile
Beam 1
Beam 2
Static beamforming [1]
[1] M. Losacco et al., Acta Astronautica, 2020

## Slide 7: BIRALES: MULTIBEAM APPROACH
Medicina (Bologna)
Salto di Quirra
(Sardinia)
Disadvantage: both main lobes and grating lobes appear in sensor FoV
Angular profile
Beam 1
Beam 2
Static beamforming [1]
[1] M. Losacco et al., Acta Astronautica, 2020

## Slide 8: BIRALES: ADAPTIVE BEAMFORMING APPROACH
Medicina (Bologna)
Salto di Quirra
(Sardinia)
Adaptive beamforming

## Slide 9: BIRALES: ADAPTIVE BEAMFORMING APPROACH
MUSIC [2]
DOA estimation
Raw signal
MUSIC - MUltiple SIgnal Classification [2]
Covariance matrix
[2] R. Schmidt et al., IEEE Transactions on Antennas and Propagation, 1986

## Slide 10: BIRALES: ADAPTIVE BEAMFORMING APPROACH
MUSIC [2]
DOA estimation
Raw signal
Covariance matrix
Direction of Arrival (DOA)
Angular track
MUSIC - MUltiple SIgnal Classification [2]

## Slide 11: DOA AMBIGUITY PROBLEM
5.67 m
10 m
0.73 m
DOA solution is unique if distance between antennas is less than
Presence of multiple DOA estimates
Ambiguity solving criteria needed
Signal DOA

## Slide 12
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Prof. Pierluigi Di Lizia
Prof. Marco Felice Montaruli

## Slide 13: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
Catalogued case

## Slide 14: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
State prediction
Catalogued case

## Slide 15: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
State prediction
Regression
Final track
Catalogued case

## Slide 16
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Prof. Pierluigi Di Lizia
Prof. Marco Felice Montaruli

## Slide 17: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
State prediction
Uncatalogued case

## Slide 18: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Uncatalogued case

## Slide 19: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
Uncatalogued case

## Slide 20: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
For each candidate track, use measured DS and SR to perform an initial orbit determination (IOD)
First approach:
N candidate tracks
Compute all predicted SNR profiles and compare with measured SNR
Uncatalogued case

## Slide 21
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
For each angular track, if range is available:
Range
Angles
Radar IOD [3]
[3] J. Siminski, 6th International Conference on Astrodynamics Tools and Techniques (ICATT), Darmstadt, Germany, 2016, 14-17 March
Predicted SNR
profiles
Uncatalogued case

## Slide 22
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
For each angular track, if only Doppler is available:
Range
Angles
Radar IOD [3]
[4] C. Yanez et al, 7th European Conference on Space Debris, 2017
Predicted SNR
profiles
Doppler shift
Range reconstruction[4]
Uncatalogued case

## Slide 23: Music Approach for Track Estimate and Refinement (MATER)
Measured
Predicted
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
Track 1
Track 2
Uncatalogued case

## Slide 24: Music Approach for Track Estimate and Refinement (MATER)
Estimate DOAs for each epoch
Signal
covariance matrix
Clustering based on RANSAC
Ambiguity solving criterion
Final track
Uncatalogued case

## Slide 25: REAL OBSERVATIONS
MUSIC pattern
Only large objects with small SR
Accuracy | 1e-02 - 1e-01 deg
ISS passage (April 28, 2021)
Current signal processing chain not suitable:
Still designed for a multibeam logics
Very noisy covariance matrices

## Slide 26
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Pierluigi Di Lizia
Marco Felice Montaruli

## Slide 27
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
November 2nd, 2022
h. 08:24 UTC
November 4th, 2022
h. 07:29 UTC
November 1st, 2022
h. 08:40 UTC
3rd Long March re-entry
From October 31st to November 4th, 2022
First operational involvement in SST services
Real data processing

## Slide 28
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Cassiopea-A
SARAL
SARAL transit
December 2°, 2022
Target: SARAL (norad ID 39086)
Radiosource: Cassiopea-A
Real data processing - channelisation

## Slide 29
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
8192 channels
Detection block
Channel selected
Correlate
Angular track accuracy
Detection rate
Multiple sources scenario
Real data processing - channelisation

## Slide 30
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Real data processing - channelisation
Aeolus re-entry campaign
July 24°-28°, 2023
The target was maneuvering during the observation
Uncatalogued case

## Slide 31
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Starlink-6051
DMSP 5D-2 F8
Disputed region
DMSP 5D-2 F8 break-up
July 24°, 2024
Target: DMSP 5D-2 F8 (norad ID 18123)
Additional targets
DMSP 5D-2 F8
Starlink-6051
Real data processing - overpopulation
Unrelated sources overlapping
Satellites constellation problem (starlink)
DMSP 5D-2 F8

## Slide 32
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
DMSP 5D-2 F8 break-up
July 24°, 2024
Target: DMSP 5D-2 F8 (norad ID 18123)
DMSP 5D-2 F8
Starlink-6051
Real data processing - overpopulation
Unrelated sources overlapping
Satellites constellation problem (starlink)
Starlink-6051
DMSP 5D-2 F8
Disputed region
Additional targets
Starlink-6051

## Slide 33
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
CZ-6A break-up
September 3°, 2024
Target: CZ-6A DEB (norad id 60649)
Real data processing - overpopulation
Critical clustering
Break-up on August 7°, 2024
QIANFAN constellation detected by 1N and 2N
Data associated to two starlinks
No fragments cloud detection

## Slide 34
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
September 3°, 2024
Target: CZ-6A DEB (norad id 60649)
Real data processing - overpopulation
CZ-6A break-up
Which detection associated to the target (if any)?

## Slide 35
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
September 3°, 2024
Target: CZ-6A DEB (norad id 60649)
Real data processing - overpopulation
CZ-6A break-up
57118
57885
60379
60383
60384
60385
60386
60387
60389
60649
Which target associated to this detection?

## Slide 36
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
September 3°, 2024
Target: CZ-6A DEB (norad id 60649)
Real data processing - overpopulation
CZ-6A break-up
Tumbling information Work on SNR reconstruction!

## Slide 37
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Pierluigi Di Lizia
Marco Felice Montaruli

## Slide 38
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
5.67 m
10 m
0.73 m
Current developments – East-West branch upgrade
5.67 m
10 m
North-south branch
Correct
Ambiguous
Correct
Ambiguous

## Slide 39
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
North-south branch
Current developments – East-West branch upgrade
East-west branch
Break the symmetry!
5.67 m
10 m
a
b
Correct
Ambiguous
Correct
Ambiguous

## Slide 40
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Current developments – admissible regions approach
Optical angular track
Constraints
Admissible region in range and range rate
Range boundaries
Energy boundaries
Eccentricity boundary
An accurate angular track is needed
G. Tommei et al., Orbit determination of space debris: admissible regions, Celestial Mechanics and Dynamical Astronomy, 2007

## Slide 41
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Current developments – admissible regions approach
To bistatic plane
To bistatic plane
Slant range

## Slide 42
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Current developments – admissible regions approach
Slant range

## Slide 43
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
OUTLINE
BIRALES data processing
MATER: Catalogued object
01
02
MATER: Uncatalogued object
03
Real data processing
04
Current developments
05
Conclusions
06
Pierluigi Di Lizia
Marco Felice Montaruli

## Slide 44
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Conclusions
To recap
Adaptive beamforming approach for BIRALES track reconstruction
Channelisation strategy
Performance improvement
Problems induced by the in-orbit overpopulation
New ways to solve the ambiguity problem
  East-west branch upgrade
  Admissible region approach
Publications:
M.F. Montaruli, M.A. De Luca, M. Massari, G. Bianchi, A. Magro, Operational Angular Track Reconstruction in Space Surveillance Radars through an Adaptive Beamforming Approach. Aerospace 2024
M.F. Montaruli, P. Di Lizia, S. Tebaldini, G. Bianchi, Adaptive track approach for multiple sources scenarios during radar survey for space surveillance applications, Aerospace Science and Technology, 2024

## Slide 45
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Conclusions
Next steps
New ways to solve the ambiguity problem
Operational pipeline implementation
  Work in progress (30%)
  Waiting for the automatic detection block
Radar light curves analysis
Operational support from PoliMi

## Slide 46
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Next Generation – Croce del Nord
IR0000026
Intervento finanziato nell’ambito del PNRR - Piano Nazionale di Ripresa e Resilienza
M4C2
Missione 4 - Istruzione e Ricerca Componente 2 - Dalla Ricerca alla Impresa
Linea di Investimento 3.1 - Rafforzamento e creazione di Infrastrutture di Ricerca
CUP C53C22000880006
GRAZIE
PER L’ATTENZIONE