## Slide 1: Metis data
R. Susino & the Metis team
2nd Metis Science Meeting - Napoli - January 27th 2024

## Slide 2: Solar Orbiter/Metis observation structure
Remote-sensing windows (RSWs) → VL + UV
  observations targeted to address mission science objectives
  coordination of RS instruments - Solar Orbiter Observing Programs (SOOPs)
Out of RS-windows
  synoptic program - coordinated observations at constant cadence → VL + UV (< 0.6 au)
  opportunities (comets, conjunctions/quadratures) → VL + UV
Every day: low-latency (LL) obsevations → VL + UV (< 0.6 au)
High latitude window
Perihelion window
Low latitude window
Out of RS-windows

## Slide 3: Data types
Visible-light channel
  sequences of 4 polarimetric images → polarised and total brightness, polarisation angle, Stokes parameters
  single total-brightness images
  fixed-polarisation images
UV channel
  analogue-mode images
pB
B
pol. angle
0° pol.
45° pol.
90° pol.
135° pol.
HI Lyα

## Slide 4: Data types & on-board processing
On-board processing
  frame average
  binning, masking
  compression (lossless, lossy)
  cosmic-ray/SEP correction
Secondary data products
  light curves (for each pB sequence)
  cosmic-ray/SEP correction maps (twice per day)

## Slide 5: On-ground processing and calibration
Level 0 (L0)
  uncalibrated data (units of DN) obtained from telemetry packets, that are uncompressed and formatted in standard FITS format
  metadata contain only the information that is available from the telemetry packet headers
Level 1 (L1)
  uncalibrated data (units of DN)
  metadata contain extra engineering data from housekeeping telemetry
  all the available orbital and attitude information is used and coordinates expressed in scientific coordinate systems (WCS)

## Slide 6: On-ground processing and calibration
Level 2 (L2)
  calibrated data (physical units) corrected for
    detector bias/dark current
    flat-field
    optical vignetting
    exposure normalisation
    radiometric calibration
    demodulation (applied only to polarimetric acquisitions)
  the most up-to-date calibration is always applied

## Slide 7: On-ground processing and calibration
Level 2 (L2)
  calibrated data (physical units) corrected for
    detector bias/dark current
    flat-field
    optical vignetting
    exposure normalisation
    radiometric calibration
    demodulation (applied only to polarimetric acquisitions)
  the most up-to-date calibration is always applied
Calibration papers
De Leo et al. (2023) A&A 676, A45 - VL
Liberatore et al. (2023) A&A 672, A14 - VL
Uslenghi et al. (2024) SPIE 13103, 1310324 - UV
De Leo et al. (2024) A&A in press - UV

## Slide 8: On-ground processing and calibration
Level 3 (L3)
  science-grade data derived from L2 data: images, movies, Carrington maps; and data obtained after scientific analysis, e.g., electron-density maps, solar-wind outflow velocity maps → JP2000 and PNG images available soon

## Slide 9: L2 FITS structure
Quality matrix
  image mask flagging:
    saturated/bad pixels (NaN)
    unreliable pixel values (0)
    good pixels (1)
Error matrix
  uncertainty map derived from measured counts through error propagation → under assessment
Main
header
Image*
Quality
matrix
Error
matrix
Stokes Q
Stokes U
* VL pB, B, pol. angle, or Stokes I or UV Lyα intensity

## Slide 10: Data flow
Solar Orbiter Archive
Metis Operations Facility (Altec, Torino)
Mission DB
Metis pipeline
L0
L1
L2
Mission Operation Centre
L2
Telemetry
Data

## Slide 11: Statistics for the nominal phase
Chart: L0
| LTP05 | LTP06 | LTP07 | LTP08 | LTP09 | LTP10 | LTP11 | LTP12 | LTP13 | LTP14 | LTP15 | LTP16 | LTP17
In mission DB | 11696 | 8128 | 6275 | 4808 | 13761 | 10397 | 11961 | 2004 | 20146 | 8036 | 15205 | 5848 | 43558
Planned | 0 | 7 | 0 | 1 | 28 | 0 | 123 | 0 | 109 | 0 | 403 | 33 | 12233
Chart: L1
Untitled 1 | 110460 | 62008
Chart: L2 (~265k)
Untitled 1 | 156737 | 108726
Chart: L0 (~175k)
Untitled 1 | 161823 | 12937
*
*
*
*
* perihelia
*
*

## Slide 12: Data availability
Nominal-phase L2 data
  publicly available through the Solar Orbiter Archive (SOAR) at https://soar.esac.esa.int/soar/ (~ 90 days after download) → data available up to March 2024
L2 data not yet available on the SOAR, L0, L1, or cruise-phase data
  available upon request, please write to metis@inaf.it
For the Metis team (authentication required)
  data available on the Metis mission DB (maintained by Altec) at http://mission-db-pro.metis.altecspace.it:8888

## Slide 13
http://metis.oato.inaf.it

## Slide 18: How to look into Metis data?
With any tool that can handle FITS files...
Recommended: iCID (IDL Coronal Images Display, developed and maintained by Silvio G.) or the python version pyCID (developed and maintained by Aleksandr B.)

## Slide 19
JHelioviewer

## Slide 20
JHelioviewer

## Slide 21
JHelioviewer

## Slide 22: Reference documents and useful links
Metis Data Product Description Document: http://metis.oato.inaf.it/docs/METIS-OATO-SPE-021_2.2_Solar_Orbiter_Metis_Data_Product_Description_Document.pdf
Metis Instrument Paper: https://www.aanda.org/articles/aa/pdf/2020/10/aa35338-19.pdf
Metis website: http://metis.oato.inaf.it
iCID: https://drive.google.com/drive/folders/1BESI7qkb2PQ_44RjmCOmapFPL93IYSCL?usp=drive_link and pyCID: https://www.ict.inaf.it/gitlab/metis/utilities/pycid.git
JHelioviewer: https://www.jhelioviewer.org