## Slide 1
Workpackage 9 on
X-ray Microcalorimeters
Rome, November 26-27, 2024
on behalf of WP 9:
Jan-Willem den Herder (SRON, Leiden)
Tasks leads (former and present):
R.H. den Hartog (SRON, Leiden)
J.-W. den Herder (SRON, Leiden)
L. Fàbrega et al. (CSIC, Madrid),
M. Barbera et al. (Uni. / INAF, Palermo)
F. Gatti et al. (Uni. Genoa)
C. Maculli (INAF, Rome)
J.-L. Sauvageot et al. (CEA, Saclay)
P. Dondero et al. (SWHARD SRL, Genoa)
S. Molendi et al. (INAF, Milano)
V. Fioretti et al. (INAF / OAS, Bologna)
J. Beyer et al. (PTB, Berlin / Braunschweig)
H. Akamatsu (SRON, Leiden)
G. de Lange (SRON, Groningen)
J. van der Kuur et al. (SRON, Groningen)

## Slide 2
WP objectives and their relevance
Diverse portfolio of activities, centered around present and future cryogenic instruments, applying microcalorimeter soft X-ray (transition edge) sensors.
The 9 tasks in the WP organized as follows:
Improvement of thermal filters for Athena (task 9.2b)
Improved sensor technologies for X-ray and cosmic ray detection beyond Athena (tasks 9.2a, 9.2c)
Analysis and modelling of the cosmic-ray particle background measured on XMM Newton, in support of Athena (tasks 9.3a, b, c)
New cryogenic multiplexing read-out technologies beyond Athena (tasks 9.2d, 9.4a, 9.4b)
AHEAD 2020 – General Meeting – 2024-11-26
Schematic lay-out of a generic space X-ray instrument, e.g. XIFU on Athena, showing the coherence between the various tasks in this workpackage

## Slide 3
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Activity progress
All tasks successfully delivered!
Task nr. / deliverable |  | Title | Responsible | Main goal that was achieved | Delivery date | 
9.1 | 9.1 | Management report | SRON Leiden |  | 2024-11-27 | 
9.2.a | 9.2 | Evaluation of TES transition parameters | CSIC Barcelona | Regimes for different transition models identified | 2024-01-30 | 
9.2.b | 9.3 | Filter test samples | Uni. Palermo | Design of Athena XIFU filters and subsequent qualification and particle contamination vibration tests, and wideband spectroscopic characterisation | 2024-11-21 | 
9.2.c | 9.4 | Spectroscopic CryoAC Sensor | Uni. Genoa | Spectroscopically capable CryoAC was verified | 2024-11-12 | 
9.2.d | 9.5 | Superconducting multilayer prototype | CEA Saclay | High electrical / low thermal conductivity wirebond pads were demonstrated | 2024-07-04 | 
9.3.a | 9.6 | Physics in GEANT | SWHARD | Monitored and evaluated Athena-relevant physics models through 4 updates of GEANT4 | 2024-03-01 | 
9.3.b | 9.7 | Non X-ray background modelling algorithms | INAF Milano | Use 15 years of XMM Epic-pn data for an improved NXB model at the L1 location | 2022-09-01 | 
9.3.c | 9.8 | Response matrices for proton reflection | INAF Bologna | Soft-proton response matrices for Athena | 2022-09-01 | 
9.4.a | 9.9 | Production of a Microwave Squid Multiplexer | PTB Berlin | A functional mwSQMUX was delivered | 2024-11-19 | 
9.4.b | 9.10 | Experimental evaluation of mwSQMUX readout | SRON Gron. | Functionality of the mwSQMUX readout was demonstrated | 2024-11-27 | 
9.1 | 9.11 | Final report & additional recommendations | SRON Leiden |  | 2024-11-27 | 

## Slide 4
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Key results of WP9.2
TES sensors, thermal filters and isolation
WP9.2a – TES transition parameters
WP9.2b – Thermal filters development
Parameters critical for the noise performance and sensitivity of Mo/Au Transition Edge Sensors (TES) were measured and interpreted in terms of two competing models for the transition: the RSJ (weak link) model and the BKT (flux motion) model.
For short enough TESs (< 50 µm) the weak-link effects dominate the transition and the RSJ model is applicable. For larger TES lengths (> 75 µm) the BKT model applies. In this regime the noise performance should be better. This is a direction for further optimization of the TES as an X-ray detector.
AHEAD2020 provided a serious contribution to the development of thermal filters in the filter stack of the XIFU instrument on Athena. This activity included design, modeling and testing. The tests consisted of mechanical vibration tests, particle contamination tests and transmission measurements from RF to UV.
Before vibration
After 18.5 g 0-peak
THF300

## Slide 5
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Key results of WP9.2
TES sensors, thermal filters and isolation
WP9.2c - Cryogenic anti-coincidence (CryoAC) sensor development
WP9.2d - High electrical / low thermal conductivity cryogenic hybrid pad
TEM crosssection of a multilayer pad
Thermal conductivity vs Temperature
In this task a prototype pad (suitable for either wirebonding or bumpbonding) was constructed from multiple layers of alternating TiN and Nb, which is electrically superconducting while at the same time having a very low thermal conductivity. This development helps to keep heatloads on low temperature cryostat stages manageable when connecting many pixels.
The goal of this activity was to improve the spectroscopic capability of the CryoAC sensor. In the milestone work the fast a-thermal phonons were identified as the culprit that spoils the energy resolution. A redesign of the CryoAC sensor was done in which many parallel connected TES sensors on top of the absorber were replaced by a single TES. With collimated exposures to 55Fe and 241Am an improvement of the energy resolution of a factor ~7.5 at 6 keV was demonstrated. This is improvement is implemented in future models of the CryoAC by applying one small TES to sense heat deposition in the absorber by cosmic rays.
Single Ir/Au TES
Au heater

## Slide 6
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Key results of WP9.3
Non-Xray Background Modeling
WP9.3a - Geant4 physics
WP9.3c – Understanding the interaction between soft protons and X-ray mirrors
WP9.3b - Non X-ray background modelling
Proton response files (consisting of a Redistribution Matrix File (RMF) and an Auxiliary Response File (ARF) in a common machine readable format) for the Athena telescope, allowing a fast evaluation of the soft-proton induced background, using results from task 9.3b as inputs to calibrate the model
Electron backscattering coefficient for Au at normal incidence, comparison among different Geant4 releases. This is an example of incremental changes that were monitored during this task.
Mean temperature profiles of a radial stacking of 30 galaxy clusters with different SOU/BKG (source over background) thresholds, obtained with the improved background modeling derived during this task. The profile could be extended well beyond the R500 radius

## Slide 7
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Key results of WP9.4
Microwave SQUID Multiplexed readout
WP9.4a - µwave MUX SQUID chip design and fabrication
WP9.4b - µwave MUX SQUID readout experiment
SEM scan of a µwave MUX SQUID chip
Spectrum of resonances measured on the chip
The insert for the Leiden cryogenics cooler on which the cold electronics, including the TES array and the µwave MUX SQUID chip are mounted
A photon induced pulse measured with the Groningen experimental set-up and an AIST chip demonstrating basic
These two coupled tasks were an open invitation to Murphy: a chip whose design, originally conceived at AIST, had to be completely reversed to fit the deposition process at PTB, and then to delivered in time to SRON for experimental verification with a GHz readout which was a modification of an MKID system.
It is safe to say that Murphy did not decline. But despite struggling with the lithographic processes, failing deposition equipment, yield problems, suppliers of IQ mixers that went bankrupt, frequency ranges of resonators that no longer overlapped with the frequency range of the alternative IQ mixer, and the usual hassle with cryostats the teams were able to demonstrate at least the basic functionality of the European µwave MUX SQUID readout.
The story does not end here: both the PTB and the SRON team are committed to take the work one step further and try for a spectroscopic demonstration in a few readout channels.
The hands-on experience with the GHz readout brought also deeper insight:
when scaling up to readout of 104 - 105 TES pixels, there is no fundamental advantage from GHz readout over MHz readout schemes such as TDM and FDM when we look at the dissipation per readout pixel, or the heatload on the coldest stages.

## Slide 8
AHEAD 2020 Second General Meeting, Rome 26-27 November 202
Lessons learned and conclusions
Tuning the aspect ratio of TESs to diminish the weak link effect is a route to performance improvement
Meshed thermal filters are very robust and are on their way to meet all flight requirements
Reducing the area of the TES covering the CryoAC absorber improves the spectroscopic capabilities
Using structures of alternating superconductors allows the fabrication of hybrid wirebond or bumpbond pads with high electrical conductivity and low thermal conductivity.
Accurate modeling of the Non X-ray Background in Athena was developed using the latest updates of GEANT4 plus an analysis of 15 years of data of the XMM Newton Epic pn and MOS data.
The soft-proton response file for both instruments of Athena has been generated
The route to produce microwave SQUID multiplexed readout has been opened in Europe.
In terms of power and heat dissipation per read-out pixel there is not a fundamental improvement to be expected from microwave SQUID multiplexed readout over more conventional MHz multiplexed readout schemes such as TDM and FDM.
The hybrid pad technology could thus be more crucial for the realization of the read-out of large-format TES arrays than the read-out scheme.