## Slide 1: AHEAD2020 WP10 Developing and Testing X-ray optics Final Report
Vadim Burwitz
Max-Planck-Institut für extraterrestrische Physik, Giessenbachstr, 85748 Garching (Germany)
Nov. 26, 2024, Rome, Italy
AHEAD 2020 2nd General Meeting
1

## Slide 2: Overview AHEAD2020
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
Funded by the Horizon 2020
Framework Program
of the European Union
Grant Agreement No. 87158
2
WP10

## Slide 3: AHEAD2020 Joint Research Activity Work Package 10: X-ray Optics  Aims
Task 10.1 Design, development, simulation and X-ray testing of grazing incidence X-ray mirror systems (MPG, CVUT, INAF/OAB, ULEIC)
Task 10.2 Development of optics for the beam conditioning in future calibration facilities and high precision metrology (INAF-OAB, MPG)
Task 10.3 Commissioning and testing of a microchannel plates test stand (ULEIC, MPG)
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
3

## Slide 4: AHEAD2020 X-ray Optics WP10: Leads
Institution | Leads
CVUT | René Hudec
INAF/OAB | Bianca Salmaso
MPG | Vadim Burwitz
ULEIC | Charly Feldman
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
4

## Slide 5: AHEAD2020 X-ray Optics WP10: Deliverables
Milestone # | Date | Date Held | Objective | Output
10.1 | T0 | 2020-03-25 | Kick-off and task detailing | MoM 
10.2 | T0+12 mo. | 2021-03-18 | Status of progress | MoM 
10.3 | T0+24 mo. | 2022-02-17 | Status of progress | MoM 
10.4 | T0+36 mo. | 2023-02-23 | Summary of work | MoM 
WP # | Del. Rel. # | Del. # | Title | Lead Beneficiary | Nature | Est. Del. Date
WP10 | D10.1 | D61 | Report on beam conditioning optics for test facilities | INAF | Report | 01 Feb 2021 
WP10 | D10.2 | D62 | Report on the technical assembly including a handbook for MPO test setup | ULEIC | Report | 01 Feb 2021
WP10 | D10.3 | D63 | First report on results of X-ray optics measured at PANTER | MPG | Report | 01 Feb 2022 
WP10 | D10.4 | D64 | Report on new high precision metrology systems for testing X-ray optics | INAF | Report | 01 Feb 2022 
WP10 | D10.5 | D65 | Report on the characterisation of MPOs using test setup and results comparison | ULEIC | Report | 01 Nov 2022 
WP10 | D10.6 | D66 | Report on the preparation of novel K-B and LE X-ray optics modules | CVUT | Report | 01 Nov 2022 
WP10 | D10.7 | D67 | Second report on results of X-ray optics measured at PANTER | MPG | Report | 01 Nov 2023 
WP10 | D10.8 | D68 | Report on the characterisation of novel optics modules at PANTER | CVUT | Report | 01 Feb 2023 
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
5

## Slide 6: AHEAD2020 X-ray Optics WP10: Task 10.1
MXT
Einstein Probe  “Tianguan”
Recently launched Missions supported
FXT
WXT
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
SVOM
Launched
Jan. 9, 2024
Launched
June 23, 2024
Launched on CAS  SATech-08 July 27, 2023
EP-WXT-QM optic
EP-WXT panoramic view of the Milky Way
6
EP-FXT supernova remnant Puppis A

## Slide 7: AHEAD2020 X-ray Optics WP10: Task 10.1
NewATHENA
Future Missions supported
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
Launch 2037
ATHENA SPO Modules
Row8 : 2.4mm rib spacing
mid radius : 1 mm rib spacing
Not selected
Arcus-Probe
Testing
SPO Optics + CAT Gratings
eXTP
eXTP optics
9 Mirror Modules
-- 3 Polarimetry
-- 6 Fast Spectroscopy
SDDs
Launch Jan. 2030
7
eXTP MM
protype

## Slide 8: AHEAD2020 X-ray Optics WP10: Task 10.1
Novel K-P Baez optics
see talk by Rene Hudec
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
Novel Optics Technology Development
Monolithic Thin Shell optics
work led by Marta Civitani
Cold Slumped Glass Module Optics
work led by Stefano Basso
KP-Baez Prototype
Dopamine coatings
see talk by Daniele Spiga
8

## Slide 9: Selected Campaign Photos – New Missions
ATHENA SPO
BEaTRiX Parabola
KP-Baez Prototype
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
LEXI FM
eXTP MM protype
9

## Slide 10: The MPE PANTER X-Ray Test Facility
  Located in Neuried, south west of Munich
  120 m X-ray beamline, 1 m diameter
  12 m instrument chamber, 3.5 m diameter
  Large cleanroom for handling X-ray optics
  Movable 10 m extension with 0.25 m diameter and a 3 m instrument chamber, 1.2 m diameter
Pumping
Station 2
Pumping
Station 3
Pumping
Station 1
X-ray
Source 1
Ø 3.5 m x 12 m
Vacuum Chamber
Clean Rooms
Small chamber
Ø 1.2 m x 3 m
Ø 1.0 m
Gate
valve
Ø 1.0 m x 120 m
Beamline
PANTER
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
10

## Slide 11: The MPE PANTER X-Ray Test Facility
13.333 m
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
11
134 m to X-ray source
12 m
3.5 m
Vacuum Chamber
Ø 1 m
Ø 0.1 m
Vacuum Tube
120 m
2m
Detector
Optic(s)
Divergent X-ray Beam
X-ray Source
Convergent X-ray Beam
Mask
  Open Multitarget Electron Impact source
  TRoPIC single photon counting pnCCD image detector 75µm pixels (256 x 256)
  PIXI imaging detector 20µm pixels (1300 x1340)
  Translation + rotary stages and Hexapods
  SDD beam stability monitor

## Slide 12: Optics in the PANTER chamber
13.333 m
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
EP-WXT
f = 0.375 m
EP-FXT
f = 1.6m
SVOM-MXT
f = 1.15m
ATHENA SPO MM
f = 12.0 m
PSO Optics with f = 9.0 m
12
134 m to X-ray source
12 m
3.5 m
Vacuum Chamber
Ø 1 m
Ø 0.1 m
Vacuum Tube
120 m
2m
eXTP
f = 5.25m
Detector
Optic(s)
Divergent X-ray Beam
X-ray Source
Convergent X-ray Beam
Mask

## Slide 13: Einstein Probe PSF results EP-FXT-QM EP-WXT-QM optics
Al-K
Cu-L
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
13

## Slide 14: Einstein Probe spectral results EP-WXT-QM3 EP-FXT-QM
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
14

## Slide 15: Campaigns (2024)
Campaign Name | Type of Optic | Measurement Quarter/Year
ATHENA first flight like Row-08 SPO MM-0058 : characterise | SPO | Q1 2023
Commission eROSITA/EP type pnCCD for PANTER – PIC02: setup | Detector | Q2 2024
OAB Dopamine Coated Optic with TRoPIC | Nickel | Q2 2024
eXTP – MM prototype | Nickel | Q3 2024
Commission eROSITA/EP type pnCCD for PANTER – PIC02: calibration | Detector | Q3 2024
OAB Dopamine Coated Optic with PIC02 | Nickel | Q3 2024
ATHENA first flight like Row-08 SPO MM-0058 : post thermal cycling | SPO | Q2 2024
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
15

## Slide 16: AHEAD2020 X-ray Optics WP10: Task 10.2
BEaTriX – commissioned – already used for trans-national access
Beam Expander improvements Finalised
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
16
SPO MM-0058
1st flight-like
ATHENA Optic

## Slide 17: AHEAD2020 X-ray Optics WP10: Task 10.3
VTF MCP test Facility
Best Theseus MPO image
Mask in Place
Facility now operational
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
17

## Slide 18: Summary AHEAD2020 WP10 / JRA2
Task | Decription (Institutions)
10.1 | Design, development, simulation and X-ray testing of grazing incidence X-ray mirror systems (MPG, CVUT, INAF/OAB, ULEIC)
10.2 | Development of optics for the beam conditioning in future calibration facilities and high precision metrology (INAF-OAB, MPG)
10.3 | Commissioning and testing of a microchannel plates test stand (ULEIC, MPG)
Insti-tution | Task Leads
CVUT | René Hudec
INAF/OAB | Bianca Salmaso
MPG | Vadim Burwitz
ULEIC | Charly Feldman
WP10 in numbers
4 Milestones (all achieved)
10 Deliverables (all completed)
42 PANTER campaigns supported (Apr. 2020- Nov. 2024)
3 Launches LEIA (07/2022), Einstein Probe (01/2024), SVOM(06/2024)
2 Flight Optics tested (LEXI, OGRE launch planned 2025/26)
2 facilities commissioned (BEaTRiX, MCP Vert. Facility)
SVOM MXT MOP FS
LEXI FM
EP WXT FM MA
Petal Thermo optical Tests
ATHENA SPO
SVOM-MXT-FS EP-WXT-FM optics
Burwitz (MPE), AHEAD2020 2nd General Meeting, 2024-11-26, Rome, Italy
BEaTriX – commissioned – already in use for TNA
Thin Monolithic
Shell development
Beam Expander improvements Finalised and in use
Designing and Testing
cold slumped glass modules
Novel K-P Baez optic X-ray tested at PANTER
MXT
Einstein Probe
SVOM
FXT x2
WXT x12
VTF MCP test Facility
Best THESEUS MPO image
LEIA 1st light
WXT x1
Launched
Launched
SPO
MM-0058
eXTP MM protype

## Slide 19: Summary
The joint research activity WP10: X-ray optics has been supported through AHEAD2020
This activity was structured into 3 tasks
  The Development and testing of new optics for upcoming and future missions
  Supporting BEaTriX and upgrading Mirror Metrology systems
  Supporting finalization of the VTF for characterising MPOs
Most of the optics testing was done at MPEs PANTER X-ray test facility
Since Apr 2020 more than 42 test campaigns have been performed and have been in part supported the AHEAD2020 Joint research Activity on X-ray optics
Both the BEaTriX and the VTF facilities have been commissioned and are in operation also the Beamexpander upgrade was completed.
All deliverables have been completed and the milestones reached.
Vadim Burwitz (MPE) 2024-11-26 AHEAD2020 2nd general Meeting, Rome, Italy
19