## Slide 1: ItaliaN Single-dish radio telescopes enhancement for studying Transients And GRAvitational Waves (INSTAGRAW)
Andrea Melis - INAF Cagliari
FRB – Italy 2025 – Area Territoriale di Ricerca di Bologna, May 8th 2025

## Slide 2: Techno Grant financed with 100k euros

## Slide 3: Short Abstract

## Slide 4: INSTAGRAW team

## Slide 5: Current digital platforms for transients at the three antennas
LEAP cluster (SRT only)
Pulsar Digital Filter Bank (SRT only)
SARDARA
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 6: Large European Array for Pulsars
- Two 512 MHz IF are split into 32 channels and outputs the spectrum over two 10GbE CX4 links. A switch distribute the 32 outputs over 32 possible servers. SRT only uses 8 sub-bands 16 MHz-wide each, for a total of 128 MHz bandwidth.
- ROACH board is deprecated, as well as the CX4 switch. LEAP nodes and the storage out of production.
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 7: Pulsar Digital Filter Bank
4 IF, max BW 1 GHz
Sample coded with 8 bits
No allowed raw data recording
Limited combinations BW/channels
Deprecated technology
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 8: SARDARA (Sardinia ROACH2-based Digital Architecture for Radio Astronomy)
Deployed for SRT, ported to Medicina and Noto for single-feed modes only.
ROACH2s deprecated and out of production
10G technology limits the throughput.
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 9: SKARAB (Square Kilometer Array Reconfigurable Application Board)

## Slide 10: SKARAB as a main processing engine at MeerKAT

## Slide 11: ADC mezzanine card
4 IF, maximum output sample rate 2800 Msample/sec
5.6 GHz of instantaneous bandwidth (4x1.4 GHz)
Each sample coded with 12 (full-band) or 16 (medium/narrow band) bits -> very high dynamic range.
A digital output devoted for the fast noise mark

## Slide 12: ADC available sampling rates

## Slide 13: MUSKAS (MUlti-feed SKARAB-based backend for the Sardinia radio telescope)
Medicina currently has a SKARAB board
Noto will have two SKARABs, purchased in the framework of the PNRR KM3
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 14: FPGA firmware designed in the framework of the CASPER (Collaboration for Astronomy Signal Processing and Electronics Research) Toolflow
256 MHz complex voltage baseband data
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 15: Pulsar/FRB search full-Stokes spectra
Main features:
2048 channels
Integration time: 16 microsec (62500 spectra/sec)
Data saved in binary files
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 16: Pulsar B03354+54 observed at 5 GHz with the SRT
Pulse profile of B03354+54, the signal to noise ratio is in agreement with corresponding literature measurements.
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 17: Coherent mode first tests
Single tone in input
2x16 MHz bandwidth successful raw data recording mode (128 MB/sec)
Next steps: optimizing code to gradually widen the bandwidth to be recorded on SP4000C
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 18: High-performing SSD based recorder SP4000C to be installed at SRT, Medicina and Noto
Main features:
96 TB (48 disks 2TB)
QSFP+ port
Recording capacity: up to 38 Gbit/sec
Fully operational at MeerKAT as a large memory buffer
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 19: SKARAB + Recorder SP4000C
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 20: Efficient Data Acquisition Using the Producer-Consumer Model
Advantages:
Separation of concerns to improve efficiency
Facilitates handling of high-speed, high-volume data streams
PRODUCER
CONSUMER
Retrieves data packets from the NIC and inserts them into a shared queue
Processes, formats, and writes the data to file

## Slide 21: Examples of Producers: PF_RING Library
High performance: up to 40 Gbps
Low CPU overhead thanks to "zero-copy" mode
Packets are acquired directly in kernel space without transfer to user space
Compatibility with libpcap-based applications and tools
Optimized for traffic monitoring and analysis applications
RING BUFFER
Release old data
Fetch data
Add new data

## Slide 22: Examples of Producers: DPDK (Data Plane Development Kit)
Superior performance: up to 40–100+ Gbps on compatible hardware
Very low latency (kernel bypass)
Optimized for multi-core CPUs
Advanced control over packet flow and scheduling
Broad hardware support and active community
Linux kernel
Network Controller
Application
DPDK

## Slide 23: Deliverables and Milestones
M1: Beginning of the project (TBD)
D1: Completion of all SKARAB FPGA firmware
D2: Testing the overall chain SKARAB + Recorder SP4000C
M2: Payment of the three recorders
D3: Full integration in the control software of the three telescopes and
scientific commissioning
M3: Submitting a paper describing the whole project
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 24
Notes: Allineare le informazioni per tipo sui tre slot, integrazione antenne con il frontend aggiungere nei punti

## Slide 25: THANKS!
Email: andrea.melis@inaf.it
INAF - Astronomical Observatory of Cagliari
Notes: Sorry if the presentation was very high-level, but if you have any very specific questions, you can also contact me via email, and I will forward them to the colleagues who deal with that