## Slide 1: Imaging Cherenkov Telescopes: A New Window into the Universe Made Possible by Segmented Mirrors W. Hofmann, MPIK
Very High Energy Gamma-Ray Astronomy
at Teraelectronvolt Energies
Apologies for some overlap with
Giorgia’s talk yesterday

## Slide 2: Birth of very high energy (TeV) gamma ray astronomy: WHIPPLE telescope 1989
Whipple Telescope 1968
Trevor
Weekes
ƚ 2014

## Slide 3: Birth of very high energy (TEV) gamma ray astronomy: WHIPPLE telescope 1989
Whipple Telescope 1968
Credit: G. Dubner (IAFE, CONICET-University of Buenos Aires) et al.; NRAO/AUI/NSF; A. Loll et al.; T. Temim et al.; F. Seward et al.; Chandra/CXC; Spitzer/JPL-Caltech; XMM-Newton/ESA; and Hubble/STScI

## Slide 4: Birth of very high energy (TEV) gamma ray astronomy: WHIPPLE telescope 1989
T. Weekes et al., ApJ 342 (1989) 379
“Observation of TeV Gamma Rays from the Crab Nebula using the Atmospheric Cerenkov Imaging Technique”
Whipple Telescope 1968
about 90 h of data

## Slide 5: Birth of very high energy (TEV) gamma ray astronomy: WHIPPLE telescope 1989
T. Weekes et al., ApJ 342 (1989) 379
“Observation of TeV Gamma Rays from the Crab Nebula using the Atmospheric Cerenkov Imaging Technique”
Whipple Telescope 1968
about 90 h of data
On source
Off source

## Slide 6: The teV southern sky
In the whole sky, over 200 sources
Supernova remnants
Pulsars and pulsar wind nebulae
Stellar clusters
Binary systems
Novae
Microquasars
Superbubbles
Starburst galaxies
Blazars
FSRQs
…
Sky maps with few arc-min resolution
Energy spectra over 3 decades in energy
Light curves on all scales from minutes to years

## Slide 7: The teV southern sky
In the whole sky, over 200 sources
Supernova remnants
Pulsars and pulsar wind nebulae
Stellar clusters
Binary systems
Novae
Microquasars
Superbubbles
Staburst galaxies
Blazars
FSRQs
…
Sky maps with few arc-min resolution
Energy spectra over 3 decades in energy
Light curves on all scales from minutes to years
PKS 2155-304
2-3 min variability

## Slide 8
Since then
Explosion in # of sources
Driven by IACTS
Real astronomy
Extreme objects
What have we learned
Gamma rays are produced when high-energy particles interact ➜ Gamma rays trace cosmic particle accelerators
Particle acceleration is ubiquitous – every object with fast (1000 km/s) outflows
Particle acceleration is efficient – often 10% or more of the kinetic energy is converted into relativistic particles
Feedback of particles is relevant for dynamics both on small and large scales
The detailed physics of particle acceleration and particle propagation is quite complex and not well understood
Field for more than 2 decades driven by Cherenkov telescopes

## Slide 9
A bit like a meteor track, but
very faint (few photons per m2)
very short-lived (some 10-9 seconds)
Cherenkov
telescopes
300 m ∅ “light pool”, 105 m2
Multiple telescopes
provide stereoscopic
views of the cascade
Use the Earth’s atmosphere
as detector medium

## Slide 10
H.E.S.S., Namibia
MAGIC, La Palma
VERITAS, Arizona
Stereoscopic systems of
Imaging Atmospheric
Cherenkov Telescopes
currently in operation

## Slide 11
300 m ∅ “light pool”, 105 m2
Cascade starts at 20-30 km
Maximum at ∼10 km
Stochastic process, strong
fluctuations from one cascade
to the next
Transverse scale of cascade: few 10 m,
corresponding to ∼0.1o in the image
Cherenkov light peaks in the blue, 300-500 nm;
Nanosecond flash with ∼1 (detected) photon /m2 at 1 TeV
Length of image ∼1o

## Slide 12: Requirements on mirror
Large area, O(100 m2)
Time dispersion ≲ few ns
High reflectivity at 300 – 500 nm
Length of image ∼1o
Transverse scale of cascade: few 10 m,
corresponding to ∼0.1o in the image
Useful field of view of (at least) few degrees
PSF ≲ 0.1o
Cherenkov light peaks in the blue, 300-500 nm;
Nanosecond flash with ∼1 (detected) photon /m2 at 1 TeV
Very inexpensive compared to astronomical instruments of same size
Robust over years, when exposed to weather (cannot afford enclosure)

## Slide 13: INSPIRATION: optical telescopes & Solar concentrators
Solar Energy, vol. 1, 1957

## Slide 14: DAVIES-COTTON optics
Single mirror composed of
identical facets of focal length f arranged on a sphere of radius f (rather than 2f)
Parabolic
DC
Off-axis angle
f/d = 1.2

## Slide 15: DAVIES-COTTON optics
Single mirror composed of
identical facets of focal length f arranged on a sphere of radius f (rather than 2f)
f/d = 1.2
Quality of facets and of facet alignment
Parabolic
DC

## Slide 16: DAVIES-COTTON optics
Single mirror composed of
identical facets of focal length f arranged on a sphere of radius f (rather than 2f)
Quality of facets and of facet alignment
Slope ∼(d/f)2
f/d = 1.2
Time dispersion ∼0.1 ns per m mirror diameter
Parabolic
DC

## Slide 17: DAVIES-COTTON optics
Single mirror composed of
identical facets of focal length f arranged on a sphere of radius f (rather than 2f)
Parabolic
DC
Quality of facets and of facet alignment
Slope ∼(d/f)2
f/d = 1.2
Image of a star at
different off-axis angles (H.E.S.S.)

## Slide 18: DAVIES-COTTON optics
Parabolic
DC
DTrms ≃ 0.1 Dm [ns]
Not isochronous
Ok for mirrors up to ∼10 m;
larger mirrors are parabolic
Single mirror composed of
identical facets of focal length f arranged on a sphere of radius f (rather than 2f)
f/d = 1.2

## Slide 19
Four 12-m telescopes

## Slide 22
Two 17-m
Telescopes on
La Palma
Parabolic,
continuous
active mirror
alignment

## Slide 23
H.E.S.S. CT5 (2012)
600 m2 parabolic mirror
28 m diameter
36 m focal length

## Slide 24: Cherenkov “camera”
1000 – 2000 pixels of ∼0.1o size
Record air shower ”movies” at GHz frame rate
Select and save “interesting” frames

## Slide 25: Cherenkov “camera”
1000 – 2000 pixels of ∼0.1o size
Record air shower ”movies” at GHz frame rate
Select and save “interesting” frames

## Slide 26: Cherenkov “camera”
1000 – 2000 pixels of ∼0.1o size
Record air shower ”movies” at GHz frame rate
Select and save “interesting” frames

## Slide 27: 1989 VS TODAY

## Slide 28: 1989 VS TODAY
Crab detection in 90 h
1% Crab in < 10 h

## Slide 29: 1989 VS TODAY
Whipple 1989 shower image
Modern camera

## Slide 30: 1989 VS TODAY
Modern array
Whipple 1989 shower image
Modern array

## Slide 31
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating

## Slide 32
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Time
from Whipple to CTAO

## Slide 33
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Facets get larger – 0.3 m2 to 2 m2

## Slide 34
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Larger
Less expensive
Suitable for mass production
Ground solid glass ➜ cold-slumped glass sandwich mirrors
D. Vernani et al.,
Proc. of SPIE Vol. 7018

## Slide 35
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Simple al/quartz coatings ➜
multilayer coatings

## Slide 36
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Increasing fields of view
3o ➜ 10o

## Slide 37
 | Whipple | HESS I | MAGIC I | VERITAS | MAGIC II | HESS II | CTAO LST | CTAO SST/ASTRI | CTAO MST
1st operation | 1968 | 2002 | 2003 | 2005 | 2009 | 2012 | 2018 | 2025 | 2026
Area | 75 m2 | 108 m2 | 236 m2 | 110 m2 | 240 m2 | 614 m2 | 370 m2 | 5 m2 | 88 m2
Diameter | 10 m | 12 m | 17 m | 12 m | 17 m | 28 m | 23 m | 4.3 m | 11.5 m
Focal length | 7.3 m | 15 m | 17 m | 12 m | 17 m | 36 m | 28 m | 2.25 m | 16 m
f/D | 0.7 | 1.3 | 1.0 | 1.0 | 1.0 | 1.3 | 1.2 | 0.5 | 1.4
Field of view |  |  |  |  |  |  |  |  | 
Optics | DC | DC | Parab. | DC | Parab. | Parab. | Parab. | SC’ | DC’
# facets | 248 | 382 | 964 | 350 | 247 | 875 | 198 | 18 (M1) | 86
Facet shape | hex | round | square | hex | square | hex | hex | hex | hex
Facet size | 61 cm | 60 cm | 50 m | 61 cm | 100 cm | 90 cm | 151 cm | 85 cm | 120 cm
Facet material | Glass | Glass | Diamond-milled aluminum sandw. | Glass | Milled aluminum & Cold-slumped glass sandw. | Glass | Cold-slumped glass sandw. | Cold-slumped glass sandw | Cold-slumped glass sandw.
Reflector | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum. | Alum.
Protection | Anodized | Quartz-coating | Quartz-coating | Anodized | Quartz-coating | Quartz-coating | Multilayer coating | Multilayer coating | Multilayer coating
Dual mirror telescopes
appear (Schwarzschild-Couder)

## Slide 38
V. Vassiliev et al.
Astroparticle Physics
28 (2007) 10
Benefits:
Improved PSF over large FoV
Compact focal plane
Primary
Secondary
Compact
focal plane

## Slide 39
ASTRI ARRAY
V. Vassiliev et al.
Astroparticle Physics
28 (2007) 10
Benefits:
Improved PSF over large FoV
Compact focal plane
Primary
Secondary
Compact
focal plane
Source: ASTRI

## Slide 40
ASTRI ARRAY
Primary
Secondary
Compact
focal plane
V. Vassiliev et al.
Astroparticle Physics
28 (2007) 10
Benefits:
Improved PSF over large FoV
Compact focal plane

## Slide 41
ASTRI ARRAY
First optical validation of a Schwarzschild Couder telescope: the ASTRI SST-2M Cherenkov telescope
E. Giro et al., arXiv:1709.08418 (2017)

## Slide 42
Inauguration
Schwarzschild-Couder Prototype Telescope (pSCT)
Whipple Observatory, 2019

## Slide 43
Weekes and Rieke
1967, at the site of
the present Whipple Observatory

## Slide 44
The Cherenkov Telescope Array Observatory
The next big step:

## Slide 49
Higher statistics of
detected gamma rays
Higher quality of
detected gamma rays

## Slide 50
HESS
CTAO g-ray PSF
HESS g-ray PSF
50
Sgr B2 Sgr A*
Galactic center seen
with Meerkat
G0.9

## Slide 54
50 GeV
500 GeV
Gamma ray flux decreases with increasing energy
Detection area increases
➜ Huge dynamic range
LST
MST
SST

## Slide 55
CTAO South
(Chile)
CTAO North
(La Palma)
Bologna
Headquarters
SDMC @ DESY
Source: CTAO

## Slide 56
Large Telescopes (LST) at
CTAO North
Dec. 17
Groundbreaking
CTAO South
Source: CTAO

## Slide 57
Theme 1: Cosmic Particle Acceleration
How and where are particles accelerated?
How do they propagate?
What is their impact on the environment?
Theme 2: Probing Extreme Environments
Processes close to neutron stars and black holes?
Characteristics of relativistic jets, winds and explosions?
Cosmic voids: their radiation fields and magnetic fields
Theme 3: Physics Frontiers
What is the nature of Dark Matter?
Is the speed of light a constant?
Do axion-like particles exist?

## Slide 58: Dark matter at the galactic center
Weakly Interacting
Dark Matter Particles
Annihilation
cross section
“known” from
Dark Matter
abundance
95% CL upper limits
H.E.S.S. Coll.
arXiv:2207.10471
Spectral signature
known from particle physics
CTAO
W-
W+

## Slide 60
A New Window into the Universe Made Possible by Segmented Mirrors