## Slide 1
S.S.-QE-DETECTOR parade today tomorrow
Fernando Pedichini INAF OAR

## Slide 2
families of standard DETECTOR
CCD (slow)
Large pixels
Megapixels
High Dark Current
3-5e- RON
Binning
High far-red QE
Complex control
Radiation weak
Mechanical shutter (most)
CMOS (fast)
Small pixels
Megapixels++
Low Dark Current
1-2e- RON
Binning only a few
BI and Microlens
Simple control
Radiation Good
Electronic shutter
HYBRID (CMOS)
Wavelength [μm] 0.3 – 14+
Megapixels
Cryogenics
2-4e- RON
Sub-Window readout
Expensive and critical
Very complex control
Are in Space!
Electronic Shutter

## Slide 3
CCDs @ the shelf (ANDOR & Teledyne-E2V)
AO ccd 220
iXon serie
EM-CCD low dynamic
0.2-0.3 e- RON
2kFps
CCD & EM-CCD
0.2-0.3 e- RON
1Mpix El. Shutter
CCD 36Mpix
monolithic

## Slide 4
CMOS @ the shelf
sCMOS
qMOS
4Mpix
1e- RON
1kFps
qORCA HAMAMATSU
8Mpix
0.25e- RON
1kFps
photon counting mode

## Slide 5
CMOS @ the shelf
2e-4 @107mas
SHARK-VIS experience
AB Aurigae Halpha
VESTA
IO R band

## Slide 6
0 : 4 γ/pix
(0.8 γ/pix)
CMOS @ the shelf qORCA HAMAMATSU
0.25 e- RON

## Slide 7
HYBRID @ the shelf
NIR
MIR
FIR
320 x 256 e-APD MCT
24 μm pixel pitch
SWIR 0.8 - 2.43 μm
70% QE, wavelength from 0.9 to 1.7 μm
Up to 3500 fps full frame
Subelectron readout noise

## Slide 8
CMOS
SILIOS / XIMEA hyperspectral filters
4Mpixel
2.4 μm pixel pitch
Fully customizable chip and filters
SPACE ready

## Slide 9
1µm x 1µm pixel
64 Mpix (8x8)
Dynamic: a few photon/pix
Dark: 0.002 e-/pix @ room temp
Spatial & Time binning of fast exposures
Image after post-processing
CMOS gigajot

## Slide 10
CMOS
SONY IMX 990-1-2-3
Up to 5.3 Mpix
Cooler embedded
Avg QE  75%
RON 10e- (tbd)

## Slide 11
HYBRID
qDOT
Up to 4 Mpix
Good for SWIR-MIR
will be color tuned by
control electronic

## Slide 12
VISION-I (photons are expensive)
X-SHOOTER / MUSE / SPHERE-IFS / ALES
LENSLET SLICER
SLIT SLICER
= 650 (
500

## Slide 13
CMOS
FOVEON
15 x 3 Mpix
3 levels R, G, B stack
Detection depth: deeper for longer wavelengths
Photometry Compatible
see: Pedichini+ SDW 2006, ASSL

## Slide 14
CMOS
PIXEL-ONE
Microlenses allow to use only a small area of your pixel for detection
Lot of space for amplifier, A/D converter and logics
Automatic RESET and ADD of bright pixels >> Infinite dynamic range
No need for shutter
Always running
SONY is working on this technology
see: Pedichini+ SPIE 2010

## Slide 15
VISION-II going to the 4th dimension (X,Y,E and t)
Bruno Keller Foundation
TOF detector
SPAD array
“NDA”
Curved Detectors
simplify and speed-up
optical design

## Slide 16
DATT @ OAR PNRR STILES WP 5401 (Pedichini OAR)
Detector Advanced Test Track
Hexapod positioner
Fully automated
Super-K source
Spectral engine
Fully Acromatic
Turbulence injector
Astro sources DLP projector
High contrast targets

## Slide 17
GRAZIE per la VOSTRA
ATTENZIONE
circa 30-35 anni fà la performance dei sensori CCD era ancora limitata e si discuteva se mai avessero soppiantato le emulsioni fotografiche e riguardo ai primi CMOS poi non se ne poteva neppure parlare.
Oggi i detector “strani” ed innovativi superano già di gran lunga i primi CCD usati in Astrofisica… basta lavorare e saremo pronti nel 2040!