## Slide 1: Orbit determination techniques for Resident Space Object catalog maintenance
Training Meeting
NG-Croce
Lunedì 12 Maggio - Giovedì 15 Maggio
Radiotelescopi di Medicina
IRA - Bologna
Mauro Massari

## Slide 2: Outline
RSO Catalogs
Orbit determination problem
Typical measurements
Minimum set of measurements
Initial Orbit Determination
  Gauss’ method
  Effect of uncertainties
Precise Orbit Determination
  Least-square problem
  Kalman filter

## Slide 3: Resident Space Objects Catalogs
A catalog of resident space objects (RSOs) typically includes detailed information about artificial objects orbiting Earth.
Common elements found in such a catalog:
Object Name: Common name or designation (e.g., Hubble Space Telescope, COSMOS 2251).
International Designator: A standardized code that includes the launch year, launch number, and piece identifier (e.g., 1998-067A).
NORAD Catalog Number: Unique number assigned by the North American Aerospace Defense Command.
Object Type: Classification such as satellite, rocket body, debris, or payload.
Owner/Operator: Country or organization responsible for the object.
Launch Date: Date the object was placed into orbit.
Launch Vehicle: The rocket used to deploy the object.
Orbit Type: General classification (e.g., LEO – Low Earth Orbit, MEO – Medium Earth Orbit, GEO – Geostationary Orbit, HEO – Highly Elliptical Orbit).
Current Status: Active, inactive, decayed, or unknown.
Radar Cross Section (RCS): Estimate of size or detectability by radar.
Decay Date: If applicable, the date the object re-entered Earth’s atmosphere.
Mission or Function: Intended use or mission purpose (e.g., communications, Earth observation, scientific research).
Tracking Information: Most recent TLE (Two-Line Element set) or ephemeris data for object tracking.

## Slide 4: Resident Space Objects Catalogs
A catalog of resident space objects (RSOs) serves multiple critical functions in space operations, safety, and policy.
Collision Avoidance: Enables satellite operators to predict and prevent potential collisions (conjunctions) between satellites or with debris.
Orbital Traffic Management: Assists space agencies and private companies in planning satellite launches and maneuvers to avoid overcrowding or unsafe orbital paths.
Tracking Space Debris: Identifies and monitors debris objects to assess risks and develop mitigation strategies.
Re-entry Prediction: Supports the forecasting of when and where objects will re-enter Earth’s atmosphere, important for safety and risk assessment.
Anomaly Investigation: Helps investigate unexpected satellite behavior, such as loss of contact or damage, by analyzing nearby RSOs.
Research and Analysis: Provides data for scientific studies on orbital mechanics, long-term space sustainability, and debris population growth.
Historical Recordkeeping: Maintains a database of past and present objects for archival, forensic, and legal purposes.

## Slide 5: Resident Space Objects Catalogs Maintenance
RSO Catalogs Are Updated:
Detection: Sensors detect new objects or movements (e.g., from launches, breakups, or maneuvers).
Identification: Analysts determine whether it's a new object, a known one with updated data, or a fragmentation/debris piece.
Orbit Determination: Orbital elements are calculated, often using the TLE (Two-Line Element) format for public distribution.
Tracking: Multiple observations are used to refine the orbit using radar, optical telescopes, and infrared sensors.
Catalog Entry or Update: The catalog is updated with the new object’s details, or the trajectory of an existing object is revised.

## Slide 6: Resident Space Objects Catalogs Maintenance
RSO Catalogs Are Updated:
Detection: Sensors detect new objects or movements (e.g., from launches, breakups, or maneuvers).
Identification: Analysts determine whether it's a new object, a known one with updated data, or a fragmentation/debris piece.
Orbit Determination: Orbital elements are calculated, often using the TLE (Two-Line Element) format for public distribution.
Tracking: Multiple observations are used to refine the orbit using radar, optical telescopes, and infrared sensors.
Catalog Entry or Update: The catalog is updated with the new object’s details, or the trajectory of an existing object is revised.

## Slide 7: Orbit Determination
Orbit determination problem

## Slide 8: Orbit Determination Problem
Orbit determination consists in computing the state of an orbiting object at a given epoch starting from a set of measurements
  Compute the orbit of an newly discovered asteroid observed with a telescope
  Compute the position and velocity of a spacecraft using measurements obtained by Earth-based systems or on-board sensors
8

## Slide 9: Orbit Determination Problem
Orbit determination consists in computing the state of an orbiting object at a given epoch starting from a set of measurements
  Compute the orbit of an newly discovered asteroid observed with a telescope
  Compute the position and velocity of a spacecraft using measurements obtained by Earth-based systems or on-board sensors
All missions require spacecraft navigation and orbit determination
9

## Slide 10: Orbit Determination Problem
Do we actually know exactly where a spacecraft is?
10

## Slide 11: Orbit Determination Problem
Do we actually know exactly where a spacecraft is?
No, there are many sources of error
  Modeling errors
  Launch errors
  Spacecraft performance
  Observation errors
11

## Slide 12: Orbit Determination Problem
  mean
  covariance
Do we actually know exactly where a spacecraft is?
No, there are many sources of error
  Modeling errors
  Launch errors
  Spacecraft performance
  Observation errors
The set of possible positions of the spacecraft is usually described by the mean state and the covariance matrix C
12

## Slide 13: Orbit Determination Problem
  mean
  covariance
Orbit determination objective: estimating the mean and covariance describing the state of the object
  Be careful: mean and covariance are not always the best choice
13

## Slide 14: Orbit Determination Problem
Orbit determination objective: estimating the mean and covariance describing the state of the object
  Be careful: mean and covariance are not always the best choice
14
  covariance
  mean
  mean
  covariance

## Slide 15: Orbit Determination Problem
What is the accuracy level we need on the knowledge of the spacecraft state?
For most situations in spacecraft navigation:
  Positions: meter level accuracy
  Velocities: m/s accuracy
15

## Slide 16: Orbit Determination Problem
What is the accuracy level we need on the knowledge of the spacecraft state?
For most situations in spacecraft navigation:
  Positions: meter level accuracy
  Velocities: m/s accuracy
For relative navigation:
  Positions: cm level accuracy
  Velocities: cm/s accuracy
16
Credits: NASA

## Slide 17: Orbit Determination
Typical Measurements

## Slide 18: Typical Measurements
Ground measurements
What are the possible measurements to estimate spacecraft position?
Optical observations with telescopes:
  Right ascension
  Declination
18

## Slide 19: Typical Measurements
Typical optical observation of an Earth-orbiting spacecraft
19

## Slide 20: Typical Measurements
Typical optical observation of an Earth-orbiting spacecraft
  Identify the tracklet
20

## Slide 21: Typical Measurements
Typical optical observation of an Earth-orbiting spacecraft
  Identify the tracklet
  Matches observed stars with catalogue
21

## Slide 22: Typical Measurements
Typical optical observation of an Earth-orbiting spacecraft
  Identify the tracklet
  Matches observed stars with catalogue
  Retrieve observables of catalogued stars
22

## Slide 23: Typical Measurements
Typical optical observation of an Earth-orbiting spacecraft
  Identify the tracklet
  Matches observed stars with catalogue
  Retrieve observables of catalogued stars
  Compute observables of the spacecraft w.r.t. catalogued stars
23

## Slide 24: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Radar observations with radar antenna:
  Range
  Doppler shift
range rate
24
Ground measurements

## Slide 25: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Radar observations with radar antenna:
  Range
  Doppler shift
range rate
25
Ground measurements

## Slide 26: Typical Measurements
  Range
  Doppler
Typical radar observation of an Earth-orbiting spacecraft
26

## Slide 27: Typical Measurements
  Range
  Doppler
Typical radar observation of an Earth-orbiting spacecraft
27

## Slide 28: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Differential One-Way Ranging (DOR):
28
deep-space spacecraft
Ground measurements

## Slide 29: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Differential One-Way Ranging (DOR):
29
Ground measurements
deep-space spacecraft

## Slide 30: Typical Measurements
What are the possible measurements to estimate spacecraft position?
30
deep-space spacecraft
Delta-DOR: obtained by correcting DOR with simultaneous tracking of radio signals from a quasar
Differential One-Way Ranging (DOR):
Ground measurements

## Slide 31: Typical Measurements
Onboard measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
31

## Slide 32: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
GPS
32
GPS-1
GPS-2
GPS-3
GPS-4
Onboard measurements

## Slide 33: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
GPS
33
GPS-1
GPS-2
GPS-4
Onboard measurements
GPS-3

## Slide 34: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
GPS
34
GPS-1
GPS-2
GPS-4
Onboard measurements
GPS-3

## Slide 35: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
GPS
35
GPS-1
GPS-2
GPS-4
Onboard measurements
GPS-3

## Slide 36: Typical Measurements
What are the possible measurements to estimate spacecraft position?
Accelerations
GPS
36
GPS-1
GPS-2
GPS-4
Onboard measurements
GPS-3

## Slide 37: Orbit Determination
Minimum Set of Measurements

## Slide 38: Minimum Set of Measurements
Consider one optical observation: and
  given the position vector of the spacecraft w.r.t. the observer in the inertial reference frame
How many measurements do we need to estimate spacecraft state ?
38

## Slide 39: Minimum Set of Measurements
How many measurements do we need to estimate spacecraft state ?
Consider one optical observation: and
  given the position vector of the spacecraft w.r.t. the observer in the inertial reference frame
2 equations with 6 unknowns
cannot be solved
39

## Slide 40: Minimum Set of Measurements
How many measurements do we need to estimate spacecraft state ?
Consider one radar observation: and
  given the position vector of the spacecraft w.r.t. the observer in the inertial reference frame
40

## Slide 41: Minimum Set of Measurements
How many measurements do we need to estimate spacecraft state ?
Consider one radar observation: and
  given the position vector of the spacecraft w.r.t. the observer in the inertial reference frame
41
2 equations with 6 unknowns
cannot be solved

## Slide 42: Minimum Set of Measurements
How many measurements do we need to estimate spacecraft state ?
  Idea: consider 3 optical observations at 3 different epochs
42

## Slide 43: Minimum Set of Measurements
How many measurements do we need to estimate spacecraft state ?
  Idea: consider 3 optical observations at 3 different epochs
6 equations with 6 unknowns
43

## Slide 44: Measurements
As the unknowns are 6 (position and velocity vectors) the problem could be:
  underdetermined if the number of linearly independent measurements is < 6
  well posed if the number of linearly independent measurements is = 6
  overdetermined if the number of linearly independent measurements is > 6
44

## Slide 45: Measurements
As the unknowns are 6 (position and velocity vectors) the problem could be:
  underdetermined if the number of linearly independent measurements is < 6
  well posed if the number of linearly independent measurements is = 6
  overdetermined if the number of linearly independent measurements is > 6
Associated to each case we have:
  infinite solutions, i.e. the problem cannot be solved
  one solution (or multiple solutions that can be reduced to one)
  the solution is the best solution that better fits all the measurements (least square method)
45

## Slide 46: Orbit Determination Sequence
Orbit determination is split in two phases
  Initial orbit determination: is the process of determining an initial orbit
    It is possible when the number of independent measurements is equal to the unknowns (i.e., 6)
    It requires the solution of a set of nonlinear equations (usually an iterative procedure as Newton’s method)
    It asks for an initial guess or a way to discern from different solutions
46

## Slide 47: Orbit Determination Sequence
Orbit determination is split in two phases
  Initial orbit determination: is the process of determining an initial orbit
    It is possible when the number of independent measurements is equal to the unknowns (i.e., 6)
    It requires the solution of a set of nonlinear equations (usually an iterative procedure as Newton’s method)
    It asks for an initial guess or a way to discern from different solutions
  Orbit determination refinement: it is the process of updating the solution exploiting new measurements
    An initial orbit is necessary
    The best estimation is obtained by solving a least square problem
    The covariance on the measurements are mapped in the state vector space
47

## Slide 48: Orbit Determination
Initial Orbit Determination

## Slide 49: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
49

## Slide 50: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
50

## Slide 51: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
51

## Slide 52: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
52

## Slide 53: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
defect
defect
53

## Slide 54: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
54

## Slide 55: Initial Orbit Determination
Basic idea: given three observations and associated observables
  Find a first guess for the spacecraft state at one observation epoch
  Propagate the state to the epochs of the remaining observations
  Compute the predicted observables and the defects w.r.t. the true observables
  Correct the spacecraft state to cancel the defects
iterate
55

## Slide 56: Dynamical Model
56
As the measurements are performed at different epochs a function to compute the evolution of the state vector is necessary
  Find the solution of a set of ordinary differential equations

## Slide 57: Dynamical Model
As the measurements are performed at different epochs a function to compute the evolution of the state vector is necessary
  Find the solution of a set of ordinary differential equations
In the case of an Earth-orbiting spacecraft can include
  Earth’s gravitational harmonics
  atmospheric drag
  solar radiation pressure
  third-body effect
The solution can be found only using numerical integrators
In initial orbit determination a two-body approximation is considered
57

## Slide 58: Gauss’s Method: Some History
Gauss’s method was derived for the "recovery" of the dwarf planet Ceres (1801):
  Ceres orbit is between Mars and Jupiter in the main asteroid belt
  Ceres was discovered by Father Giuseppe Piazzi 1801
  Initially classified as a planet and later demoted an asteroid
  Upgraded a dwarf planet in 2006, along with Pluto (downgraded)
58
Credits: NASA

## Slide 59: Gauss’s Method: Facts
After more than 200 years it is the baseline for initial orbit determination of celestial bodies and spacecraft
Gauss’s method:
  is a method for initial orbit determination when three observations with telescopes are available (3 sets of right ascensions and declinations)
  assumes two-body dynamics
  exploits truncated Lagrangian expansions to determine a first guess solution at the epoch of the second observation
  iterates using Kepler’s dynamics until the three sets of observations are exactly satisfied in the two-body framework
59

## Slide 60: Lagrange Coefficient
Given an initial state and under Keplerian dynamics, the position at epoch can be obtained as:
60
with
Lagrange coefficients

## Slide 61: Lagrange Coefficient
Given an initial state and under Keplerian dynamics, the position at epoch can be obtained as:
Given the first guess at , the positions at epochs and are
61
with
Lagrange coefficients

## Slide 62: Observer's Inertial Location
Compute observer’s location w.r.t. Earth’s center in inertial frame:
Observation’s date is defined by year, month, day, and UT
Defining T0 the centuries past J2000, Greenwich sidereal time at 0hr UT is
Greenwich sidereal time and that of the observer at observation epochs are
62

## Slide 63: Observer's Inertial Location
Compute observer’s location w.r.t. Earth’s center in inertial frame:
Finally the observer’s inertial position wrt Earth’s center is
63

## Slide 64: Observer's Inertial Location
Compute observer’s location w.r.t. Earth’s center in inertial frame:
Finally the observer’s inertial position wrt Earth’s center is
The unknown inertial positions of the object can be expressed as:
with
64

## Slide 65: Observer's Inertial Location
Compute observer’s location w.r.t. Earth’s center in inertial frame:
Finally the observer’s inertial position wrt Earth’s center is
The unknown inertial positions of the object can be expressed as:
with
65
is unknown

## Slide 66: Object Inertial Locations
For the general case of interplanetary spacecraft:
The inertial position vector of the observer w.r.t. Sun is obtained by adding the inertial position vector of the Earth’s center
Earth’s position can be evaluated using JPL ephemeris
The unknown inertial positions of the object at observation epochs are:
66

## Slide 67: Gauss’s Algorithm
67
(1)
(2)
Write the inertial position vector of the objects as
As we consider two-body problem (thus planar) we can write or
Take the cross products
Thus
Use now the Lagrangian coefficients:
Obtain:

## Slide 68: Gauss’s Algorithm
The expression of the c coefficients are
In the hypothesis of sufficiently close observations
Retaining terms up to the third-order in time
By substituting Eq. (1) in Eq. (2):
68
(3)
(4)

## Slide 69: Gauss’s Algorithm
Rewrite in matrix form
Thus
Recalling that c2 = -1
Substituting Eq. (5) in Eq. (7):
69
(5)
(7)
with
(6)
(8)

## Slide 70: Gauss’s Algorithm
From Eq. (1) for the second observation:
Substitute Eq. (8) into Eq. (9) which is a 8th order polynomial in r2 that can be solved numerically
Once r2 is computed, c1 and c3 are calculated from Eq (4) and ρk from Eq (6)
Finally the velocity at t2 is computed as
Some considerations:
  In general we have 8 solutions for r2, but only real solutions are feasible
  The matrix S must be invertible (sk shall not be coplanar)
  The solution does not exactly satisfy the observations (due to truncation errors of the f and g series)
70
(9)
(10)

## Slide 71: Gauss’s Algorithm
From Eq. (1) for the second observation:
Substitute Eq. (8) into Eq. (9) which is a 8th order polynomial in r2 that can be solved numerically
Once r2 is computed, c1 and c3 are calculated from Eq (4) and ρk from Eq (6)
Finally the velocity at t2 is computed as
Some considerations:
  In general we have 8 solutions for r2, but only real solutions are feasible
  The matrix S must be invertible (sk shall not be coplanar)
  The solution does not exactly satisfy the observations (due to truncation errors of the f and g series)
71
(9)
(10)

## Slide 72: Iterative Correction
An iterative procedure is necessary to cancel errors w.r.t. observations
From r2 and v2 compute the orbital parameters of the object
Compute exact f and g coefficients
Compute c1 and c3 from Eq (3)
Compute G and Eq (5) and ρk with Eq (6)
Obtain rk with Eq (1) and v2 from Eq (10)
Note:
72
The iterative procedure can diverge if the observation are far in time (separation should be less than a radiant)
The matrix S must be invertible (sk shall not be coplanar)
If the observations are too close S is ill-conditioned and the algorithm becomes unreliable

## Slide 73: Effect of Uncertainties
When it converges the Gauss method delivers a solution that exactly fits the observations in the two-body approximation
  The observations are not exact, each measurement is affected by errors usually modeled with normal distributions
  Dynamical perturbations deviate the object’s path from two-body solution
Where is the star?
73

## Slide 74: Effect of Uncertainties
When it converges the Gauss method delivers a solution that exactly fits the observations in the two-body approximation
  The observations are not exact, each measurement is affected by errors usually modeled with normal distributions
  Dynamical perturbations deviate the object’s path from two-body solution
exact
estimated
74

## Slide 75: Effect of Uncertainties
Example: Apophis encounter with Earth in April 2029
Earth’s SoI
Earth
75

## Slide 76: Effect of Uncertainties
18 Nov 2028
15 Sept 2029
3 Apr 2030
8 Apr 2032
Example: Apophis encounter with Earth in April 2029
Earth’s SoI
76

## Slide 77: Orbit Determination
Precise Orbit Determination

## Slide 78: Precise Orbit Determination
As time goes on, several measurements become available ( > 6 )
78

## Slide 79: Precise Orbit Determination
As time goes on, several measurements become available ( > 6 )
The spacecraft state is found by fitting the measurements by solving a least-square problem
79

## Slide 80: Least-square Problem
dynamics
unknown
real measurements
measurement model
errors
Problem statement: given
  Dynamics:
  Measurements:
80

## Slide 81: Least-square Problem
dynamics
unknown
real measurements
measurement model
errors
Problem statement: given
  Dynamics:
  Measurements:
Find that minimises
vector of all errors
81

## Slide 82: Least-square Problem
Problem statement: given
  Dynamics:
  Measurements:
Example:
  Dynamics:
  Measurements:
82

## Slide 83: Least-square Problem
  Manipulate the dynamics to relate equations to :
with
Linearize the equations
  Define the displacements:
83

## Slide 84: Least-square Problem
  Manipulate the dynamics to relate equations to :
with
State Transition Matrix
Linearize the equations
  Define the displacements:
84

## Slide 85: Least-square Problem
State transition matrix computation
  Differentiate:
  Replace in
  Obtain the matrix equation:
  Integrate to obtain:
85
Note:
with
Note: can be found analytically in specific cases

## Slide 86: Least-square Problem
Let’s go back to the original problem:
86

## Slide 87: Least-square Problem
Let’s go back to the original problem:
87

## Slide 88: Least-square Problem
Let’s go back to the original problem:
Measurements equations are now:
Define:
88

## Slide 89: Least-square Problem
We can now find that minimizes
(1)
and
positive definite
Rewrite measurements equations in matrix form:
From (1) we have
  Minimize
89

## Slide 90: Least-square Problem
Thus, the best estimate of is:
90

## Slide 91: Least-square Problem
Thus, the best estimate of is:
NOTE 1: An estimate of the uncertainty associated to can also be computed
91

## Slide 92: Least-square Problem
Thus, the best estimate of is:
NOTE 1: An estimate of the uncertainty associated to can also be computed
NOTE 2 : The same procedure applies if we want to obtain the estimate at any measurement epoch
k
92

## Slide 93: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
93

## Slide 94: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
iterate
94
Credits: Brandon A. Jones

## Slide 95: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
iterate
measurements
95
Credits: Brandon A. Jones

## Slide 96: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
predicted measurements
iterate
96
Credits: Brandon A. Jones

## Slide 97: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
iterate
97
Credits: Brandon A. Jones

## Slide 98: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
iterate
98
Credits: Brandon A. Jones

## Slide 99: Least-square Problem
The previous procedure relies on the linearisation of the dynamics and of the measurements equation
  What if the system is nonlinear?
iterate
99
Credits: Brandon A. Jones

## Slide 100: Least-square Problem
Weighted least-square:
  Sometimes we want to give “preference” among measurements
100
weights

## Slide 101: Least-square Problem
Weighted least-square:
  Sometimes we want to give “preference” among measurements
101
weights

## Slide 102: Least-square Problem
Weighted least-square:
  Sometimes we want to give “preference” among measurements
  Minimize:
  Results: the best estimate is
102
weights

## Slide 103: Least-square Problem
Minimum variance estimate:
  Statistical approach to identify estimated mean and covariance
  Given:
  With statistics:
  Find that minimizes the covariance matrix at :
103

## Slide 104: Least-square Problem
Minimum variance estimate:
  Solution:
104

## Slide 105: Kalman Filter
Assume we have an initial estimate of mean and covariance
  Kalman filter processes the measurements one by one as they arrive
E.g., consider the measurements acquired at
How can we updated the knowledge of the mean and covariance at ?
105

## Slide 106: Kalman Filter
Assume we have an initial estimate of mean and covariance
  Kalman filter processes the measurements one by one as they arrive
E.g., consider the measurements acquired at
How can we updated the knowledge of the mean and covariance at ?
106

## Slide 107: Kalman Filter
Real system
107

## Slide 108: Kalman Filter
Real system
Prediction
108

## Slide 109: Kalman Filter
Real system
Prediction
109

## Slide 110: Kalman Filter
Update
Real system
Prediction
110

## Slide 111: Kalman Filter
Real system
Update
Prediction
111

## Slide 112: Kalman Filter
Real system
Update
Prediction
Kalman Filter
112

## Slide 113: Kalman Filter
Prediction
Usually performed with linearised dynamics:
113

## Slide 114: Kalman Filter
Prediction
Usually performed with linearised dynamics:
114
NOTE: Extended Kalman Filter perform new linearisation at each

## Slide 115: Kalman Filter
Prediction
Usually performed with linearised dynamics:
115
Not accurate for highly nonlinear dynamics:
  Example: Kepler’s dynamics, eccentricity 0.5, after 0.8 orbits
MC (104 samples)
EKF - order 1

## Slide 116: Kalman Filter
MC (104 samples)
EKF - order 1
EKF - order 2
EKF - order 3
Prediction
Using differential algebra we obtain:
116
Expectation are then computed on the monomials of the polynomial with Isserlis’ formula
  Example: Kepler’s dynamics, eccentricity 0.5, after 0.8 orbits
high-order Taylor expansion

## Slide 117: Kalman Filter
Update
Solved with a minimum variance approach:
  Given and the measurement noise
117

## Slide 118: Kalman Filter
Update
Solved with a minimum variance approach:
  Given and the measurement noise
  Compute and with:
118

## Slide 119: Orbit Determination
Conclusions

## Slide 120: Conclusions
If no estimates are already available
Initial orbit determination
120

## Slide 121: Conclusions
If no estimates are already available
Initial orbit determination
If an estimated state is already available
Least-squares method
121

## Slide 122: Conclusions
If no estimates are already available
Initial orbit determination
If an estimated state is already available
Least-squares method
If an estimated mean and covariance is already available
Kalman filter
122

## Slide 123: Orbit Determination
References

## Slide 124: References
Schutz, Bob, Byron Tapley, and George H. Born. Statistical orbit determination. Elsevier, 2004
Milani, Andrea, and Giovanni Gronchi. Theory of orbit determination. Cambridge University Press, 2010
Crassidis, John L., and John L. Junkins. Optimal estimation of dynamic systems. CRC press, 2011
Beutler, Gerhard. Methods of celestial mechanics: volume I: physical, mathematical, and numerical principles. Springer Science & Business Media, 2004
Armellin, Roberto, and Pierluigi Di Lizia. "Probabilistic optical and radar initial orbit determination." Journal of Guidance, Control, and Dynamics 41.1 (2018): 101-118