## Slide 1: BUILDING A NEW DATA PROCESSING SYSTEM
Training Meeting
NG-Croce
Monday 12th May - Thursday 15th May
Medicina Radiotelescopes
IRA - Bologna
Giovanni Naldi

## Slide 2
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Outline
Review of the task’s purposes
Hardware components of the system:
  Back-end boards
  HPC Cluster
  Contracts for development activities:
  Firmware
  Software
  Other ongoing activities
  Conclusions

## Slide 3
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Goal of the Task
To equip the upgraded Northern Cross Radiotelescope with a new digital acquisition and processing system for data coming from both arms (North-South and East-West)
  System components:
    FPGA boards (digital backend)
    High Performance Computing (HPC) cluster
  Software/Firmware Development
  Applications:
    monitoring of LEO space objects
    (space debris, SD)
    detection of the Fast Radio Bursts (FRBs)
    radio transients

## Slide 4
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
General Scheme

## Slide 5
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Hardware components: FPGA boards
Sub-rack
Tile Processing Module
1x FPGA Board
2x Analogue Receivers
21 FPGA boards arranged in 6 sub-racks
Main characteristics of the FPGA board:
Dimension | 6U
Number of RF input signals | 32
Analog to Digital Converter | 16 dual, 14-bit ADCs
FPGA device | 2 Xilinx Ultrascale+
RAM memory | 32 GB
40 GbE interface | 2 QSFP (1 per FPGA)
Status of the procedure:
  Contract issued
  Material delivered
  Procedure about to be closed (next month)

## Slide 6
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Hardware components: HPC Cluster

## Slide 7
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Hardware components: HPC Cluster
Data center building
3x Master Nodes | 18x HPC Nodes | 9x Object Storage Nodes
System management (monitor and control) | Massive and parallel computing | Mid term storage for processed and reduced data
Login Nodes | Dual CPU (multi-core) | Raw data to be post-processed and post-analysed
 | 2x NVIDIA L40S GPU | 8 PB of total disk space
 | 2 TB RAM | 30GB/s writing; 45GB/s reading (aggregate)
 | 2x SSD (3 TB each) | 
 | 2x NIC (dual-port) 100Gb/s | 
Status of the procedure:
  Tender concluded
  Supplier awarded
  Contract about to be signed

## Slide 8
Firmware Development
Priority
Missione 4 • Istruzione e Ricerca

## Slide 9
Firmware Development: Contract
The work must complete a design already started and in an advanced phase
Added the design for the Noto Radiotelescope (many common parts to be reused)
3 main Milestones:
Milestone | Description | Deadline
MS1 | Packetiser and 40 GbE interface included in the design for NCR | T0+1month
MS2 | FW design for NCR completed | T0+4months
MS3 | FW design for Noto Radiotelescope completed | T0+6months
Status of the procedure:
  SoW completed
  Contract to be written and signed
Missione 4 • Istruzione e Ricerca

## Slide 10
Software Development
See Alessio’s Talk…
Missione 4 • Istruzione e Ricerca

## Slide 11
Software Development: Contract
Approach: building the system gradually, releasing step by step new features with respect to the system currently in use
4 main Milestones:
Milestone | Description | Deadline
MS1 | Initial Firmware and Software Tests | T0+1month
MS2 | 64 (or 32) cylinders, 1 Beam, No Real-Time | T0+3months
MS3 | 64 (or 32) cylinders, 1 Beam, Real-Time | T0+6months
MS4 | 64 cylinders (or 32), Multi-Beam, Real-Time | T0+8months
Status of the procedure:
  SoW completed
  Contract written
  Contract to be signed
Missione 4 • Istruzione e Ricerca

## Slide 12
Ongoing Activities
Efforts to make the currently used data analysis pipelines portable
  Containerization (Docker, Podman) of:
    FETCH (deep-learning based classifier)
    FRB Baseband (pipeline to post-process the data of Noto RT)
Set up of a Gitlab server hosted in Medicina
  Code repository (distributed revision control system)
  Collaborative software development platform
  Enable CI/CD automation
  Mirroring in INAF Trieste (disaster recovery)
Missione 4 • Istruzione e Ricerca

## Slide 13
Ongoing Activities
Set up of a secure remote access system to Medicina servers
  Through VPN
  Using isolated VLAN with access to the desired service
Software tools for the monitoring and control of:
  Analogue receivers
    Configuration set-up (DSA)
    Power levels check
    RFI monitoring
    ADC clipping monitoring
  Digital boards
    Power on/off
    FPGA programming
    Temperature monitoring
    Synchronization check
Missione 4 • Istruzione e Ricerca

## Slide 14
Receivers Monitor & Control
Courtesy: A. Mattana
Missione 4 • Istruzione e Ricerca

## Slide 15
(Some) Criticalities and Strategies to Mitigate them
Tender for HPC Cluster: long and complex procedure
  It could affect the development of other activities depending on it
Purchased a computing node with GPUs and a storage system
  it will be used to deploy the system for 32 cylinders (first 2 milestones of SW development)
Difficulties in awarding contracts for FW/SW development
Some activities already started
Few people for many and complex tasks (with a tight timeline!)
Efforts to find additional manpower
  Internship (5/6 months) for Master in HPC
  PhD proposal (FRB search pipeline with HPC platforms)
  Investigate possible synergies with CHORD?
Missione 4 • Istruzione e Ricerca

## Slide 16
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Next Generation – Croce del Nord
IR0000026
Intervento finanziato nell’ambito del PNRR - Piano Nazionale di Ripresa e Resilienza
M4C2
Missione 4 - Istruzione e Ricerca Componente 2 - Dalla Ricerca alla Impresa
Linea di Investimento 3.1 - Rafforzamento e creazione di Infrastrutture di Ricerca
CUP C53C22000880006
THANKS
FOR THE ATTENTION