## Slide 1: Writing Software Pipelines The Northern Cross Case
Training Meeting
NG-Croce
Lunedì 12 Maggio - Giovedì 15 Maggio
Radiotelescopi di Medicina
IRA - Bologna
Alessio Magro

## Slide 2
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca

## Slide 3: Channelized Data Stream from TPMs
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Data stream goes to the beamformer/correlator nodes
Ingested using an optimized version of the SKA DAQ software
  Support for multiple producers and consumer
  Optimization to ring buffer locking mechanism
  Optimizations to channelized data consumer
  Concurrent multi-container support for consumer processing

## Slide 4: Channelized Data Stream from TPMs
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
8 producers 8 consumer
SL: Spinlock
MCS: Mellor Crumney Scott lock

## Slide 5: Channelized Data Simulator
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
A packet simulator was implemented to aid development and benchmarking
Accepts JSON for packet and tile config
Two threads per tile, one updating packet metadata and the other transmitting the packets
Simulator set up to match a particular data rate

## Slide 6: Beamformer
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Data stream goes to the beamformer/correlator nodes
Beamformer implemented on GPU within a Bifrost pipeline
Various versions of the beamforming kernel implemented and benchmarked
Top performing on RTX ADA 6000, with 256 antennas, 512 channels, 64 beams gives 2x real-time
Further profiling and optimization is possible

## Slide 7: Correlator
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
New CUDA kernel developed based on xGPU
Several variations of the kernel implemented and benchmarked
For 256 antennas, hardware managed caching delivers best performance
Top performing on RTX ADA 6000, with 256 antennas and 512 channels, gives 10x real-time
Further profiling and optimization is possible

## Slide 8: Beamformed/Correlated Data Stream
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Beamformer and correlated data needs to be streamed to FRB/SD nodes for processing
Currently investigating possible protocols and frameworks suitable for this, such as Open Fabrics Interfaces
Implemented basic workflows to support RMA and RDMA, and to simulate the orchestration between the components using containers
RDMA operations needs to be synchronized

## Slide 9: FRB Pipeline
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Heimdall benchmarked to determine a good performance to sensitivity ratio
Simulated dataset generated by Andrea Geminardi used to cover the FRB search space
Each file ran through 25 parameters combination in Heimdall (boxcar 21-512, DM tolerance 1.001-1.2), with their detection values and running times extracted
T-SNE and Friedman tests run on the resulting timings and detection values to narrow down selection of optimal parameter combinations

## Slide 10
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca

## Slide 11: BIRALES Update
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Updated TPM firmware to use DDC
PyBIRALES extended to support 256 antennas, 256 beams and allows for sub-array configurations.
All primary signal-processing blocks extended to support offload to GPU for processing (beamformer, channelizer, correlator)
Standardized output file format for all modes (using HDF5)
Updated User Interface
Preliminary commissioning performed earlier this year
In theory, only changes to the channelizer required to support PNRR FW

## Slide 12: Radar Signal Simulator
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
A physics-based simulator that mimics raw radar antenna signals from orbiting LEO objects
  Signal generation based on realistic orbital dynamics using TLE data
  Emulates raw I/Q data as received by a radar antenna
  Compatible and integrated with PyBIRALES pipeline
Build from first principles. Implements signal propagation, Doppler effects, and realistic noise
Ground truth embedded for ML training/labelling
Useful for labelled dataset generation, regression testing, benchmarking

## Slide 13: Radar Signal Simulator
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca

## Slide 14: Radar Signal Simulator
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca

## Slide 15: Software Infrastructure
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
The NCR will be a sophisticated observatory, leveraging advanced software frameworks and methodologies
We need to specify parameters for scalability, extensibility and interoperability
A solid automated testing framework needs to be developed
Ideally, a policy for development environments, tooling specifications, version control and coding standard is put into place