## Slide 1: An Overview of Three Decades of Infrared Detectors in Space
Massimo Robberto
Space Telescope Science Institute
Johns Hopkins University

## Slide 2: Why Infrared Astronomy
Star formation occurs in dusty environments
Cosmological redshift
Cool objects radiate mostly in IR
Why IR from Space
Earth's atmosphere absorbs most IR
Earths atmosphere emits in the VIS-IR windows
300K thermal background mitigated or remoed
Notes: nfrared detectors opened new astrophysical regimes.

## Slide 3: Early Infrared Detectors (pre-1986)
Pre-history:
Single element detectors
Small linear arrays
Mechanical scanning systems
Limitations:
Slow mapping
Limited imaging capability
“Chopping and Nodding”
“Bustrophedic Mapping”
Notes: ESO NIRSPEC: 32 InSb diodes

## Slide 4: IRAS (Infrared Astronomical Satellite, 1983)
Detector Type: Discrete, single-element detectors arranged in linear strips.
Technology: 62 detectors (mostly Silicon and Germanium based) that scanned the sky to build maps
Maker: Rockwell ~1980-1981
IRAS Detectors
Air and Space
Museum Collection
Washington, DC

## Slide 5: Orion Molecular Clouds
Janice Lee (STScI), Thomas Williams (Oxford), and the PHANGS team

## Slide 6: Mid 80’s: the first generation
1983: InSb 32x32 (SBRC Raytheon)
1986: Si:Ga, SiAs 10x64 (Rockwell)
1986/87: InSb, Si:Ga 58x62 (SBRC Raytheon)
University of Hawaii, Institute for Astronomy, 1987
I. Mc Lean “The IRCAM Revolution” in Thirty Years of Astronomical Discovery with UKIRT, Astrophysics and Space Science Proceedings 37, A. Adamson et al. (eds.)

## Slide 7: TIRCAM: 1986 - 1994
Rockewell 10x64 Si:Ga
TC-MIRC
1994-1998
Two channels
MIR Camera
- InSb 58x62
- Si:Ga 58x62
Pioneering projects in Italy
at the TIRGO 1.5m telescope

## Slide 8: ISO (Infrared Space Observatory, 1995–1998)
  Detector Type: Early-generation 2d arrays.
  Technology: 32x32 pixel InSb (CID, 1000 e/pix RON) and Si:Ga (In-bumped to Si Mux, 300e/pix RON)
  Maker: SAT & CEA-LETI (France)
SPIE Proceedings Volume 1130, New Technologies for Astronomy; (1989)

## Slide 9: ISOCAM gallery
Pilbratt et al. A&A333,L9 (1998)
M51
M16

## Slide 10: IR Arrays: the 1990s boom
Hybrid Detector Architecture
Direct Readout with Source Follower
  Non-Destructive Read: Fowler, SUTR sampling
HgCdTe (tunable!) and InSb photodiodes
Increasingly larger format
  128 × 128
  256 × 256
  … early 1K x 1K
Rapid Growth and adoption by major observatories

## Slide 11: Family Portraits: Rockwell/Teledyne

## Slide 12: SBRC - Raytheon
Ando et al., in “Scientific Detectors for Astronomy”, P.Amico, J. W. Beletic & J.E. Beletic eds., Springer (2004)

## Slide 13: NASA enters the game IR from space poses hard requirements
Challenges:
Extremely LOW signal flux
Thermal backgrounds LOW
Electronics and Thermal: STABLE
Cosmic Ray Environment
Key parameters:
High Quantum efficiency
Ultra-Low Read noise
Virtually Zero Dark current
Stability (allows calibration)

## Slide 14: HST/NICMOS (1997-2008)
https://gerbil.phys.uvic.ca/~gwyn/MMM/nicmos.html
NICMOS3 256 x 256 (1-2.4micron)
HgCdTe on Sapphire (PACE)
30e CDS RON
77K operation

## Slide 15: Despite issues… exceptional discoveries!
Amplifier Glow
Pedestal
Fluctuations
Quadrant-to-quadrant
fluctuation
Notes: PACE-I (Producible Alternative to CdTe for Epitaxy), Sapphire has excellent CTE matching to Si MUX

## Slide 16: In the Mid-IR: Spitzer (2003-2020)
- InSb 256 x 256
- SiGa 256 x 256
- in parallel,
- dual instrument
(adjacent fields)
IRAC: 3.6, 4.5, 5.8, and 8 microns

## Slide 17: Spitzer Science highlights

## Slide 18: Lessons learned drive progress

## Slide 19: HST/Wide Field Camera 3-IR` - detector development 2000-2004 - launched 2009… ongoing!
Hawaii -1R (0.6 – 1.72micron)
HgCdTe on ZnCdTe
  MBE grown
  T ~150K
Reference Pixels
Amp-Glow mitigation
Rad-induced luminescence
  Substrate removal (“thinning”)
  Sensivity down to 0.4micron
24e CDS RON

## Slide 20: We learned more and more…
Persistence/latency
Flux dependent non-linearity
1/f noise limittions
Interpixel capacitance
...
Notes: Westerlund 2

## Slide 21: Wise/Neowise (2009-present) Herschel (2009-2014)
PACS Camera 51-220micron
2 x Bolometer arrays (4/8 x 16x16 format)
2 x Ge:Ga photoconductor array (16x25 format)
Four bands: 3.4, 4.6, 12.0 and 22.2 μm
HgCdTe 1Kx1K and Si:As 1Kx1K

## Slide 22: Andromeda with WISE and Herchel
Notes: Herschel image with SOURE @250 micron.
WISE used all four of its infrared detectors to capture this picture: 3.4- and 4.6-micron light is blue; 12-micron light is green; and 22-micron light is red.

## Slide 23: The JWST Era
Near-IR instruments:
NIRCam: 10 detectors
NIRSpec: 2 detectors
NIRISS: 1 detector
FGS: 2 detectors
+ Sidecar ASICS
Mid-IR:
MIRI: 3 detectors

## Slide 24: Hawaii 2-RG
2048×2048 HgCdTe
High QE (>80%)
Very low noise
0.25 um technology
  Guide Mode: 32x32subarray at 100Hz
  IRS2 very low noise readout (ask Bernie)
1/4/32 outputs => read time 42/10.5/1.3s
Low Power (60microW/channel)
Buttable on 3 sides
Gained more profound understanding of metallurgy
James Webb Space Telescope ( JWST ) Detector Degradation Failure Review Board
(ask Jim and Bernie for details)

## Slide 25: MIRI Detectors
Raytheon Vision System (Spitzer/IRAC heritage)
Si:As detectors
1024x1024 active pixels, 25um pitch
  4+4 columns of reference pixels at the sides
4 output channels, 3s read time
Wavelength range: 5–28 μm
Operating temperature: ~7 K
=> M. Regan talk
JWST is (6.5/0.85)4 = 3,419 times faster than Spizer

## Slide 26: The current Hi-2RG generation
3x Hawaii-2RG 2.5 µm 3x Hawaii-2RG 5.3 µm
SPHEREX
Euclid
16x Hawaii-2RG 2.3 µm

## Slide 27: Entering the 4K era
Nancy Grace Roman Space Telescope
Future dedicated IR missions
future large panchromatic observatory
=> Habitable World Observatory
Roman: 18 Teledyne H4RG

## Slide 28: This meeting
Tackling increasingly harder requirements to deliver transformational science

## Slide 29: The importance of an ERROR BUDGET

## Slide 31: Conclusion: we went a long way
From 32x32 → megapixel focal planes
Impact:
- transformed fundamental physics and astrophysics
enabled search for exo-Earths, life elsewhere in the Universe
Our journey continues… the best has to come!

## Slide 32: Ancillary slides

## Slide 33: Why Infrared Astronomy
Star formation occurs in dusty environments
Notes: nfrared detectors opened new astrophysical regimes.

## Slide 34: Looking through the dust

## Slide 35: Looking through the dust

## Slide 36: Why Infrared Astronomy
Star formation occurs in dusty environments
High-redshift galaxies are redshifted into IR
Notes: nfrared detectors opened new astrophysical regimes.

## Slide 37: Hubble “J-band dropout”
6σ
7σ
6σ
10σ
15σ
12σ
J-band
26.9 AB
27.2 AB
27.9 AB
25.9 AB
26.1 AB
27.3 AB
JD = “J-band dropout”
Coe et al. (2013)
Notes: (skip remaining notes)
=====
TITLE
These are the magnitudes and detection significances in the two reddest filters.
It drops out of detection in the J-band F125W and all bluer filters.
(0:30)

## Slide 38: Why Infrared Astronomy
Star formation occurs in dusty environments
High-redshift galaxies are redshifted into IR
Cool objects radiate mostly in IR:
Notes: nfrared detectors opened new astrophysical regimes.

## Slide 39: Why Space
Earth's atmosphere absorbs most IR
Earths atmosphere emits in the VIS-IR windows
Thermal background dominates observations
1-2.5
3
Notes: Space telescopes are essential

## Slide 41: Size matters…