## Slide 1: The Moons And Jupiter Imaging Spectrometer (MAJIS) on ESA/JUICE
IRIS Calibration and Performance Workshop 2026
F. Poulet and MAJIS team

## Slide 2
JUICE science themes: broad & interdisciplinary
Emergence of habitable worlds around gas giants
  Ganymede as a planetary object & potential habitat
  Europa’s recently active zones
  Callisto as a remnant of the early Jovian system
The Jupiter system as a model for gas giants
  Jovian atmosphere
  Jovian magnetosphere
  Jovian satellite & ring system
  Complex system interactions

## Slide 3
JUICE S/C overview
  Spacecraft dry mass: 2450 kg
  Propellant tank capacity: 3650 kg
  Launch mass: ~6.1 tonnes
  Solar array power: ~790 W at end-of-life
  On-board memory: 1.25 Tbits at end-of-life
  Data rate: > 1.4 Gbits/day
  Communications round-trip: ~90 minutes
PEP sensors
(nadir side)
PEP sensors
(zenith side)
RIME antenna
Langmuir probes x 4
UVS
JANUS
MAJIS
GALA
SWI
3GM: KaT+USO
(in vault)
MAG boom
3 x J-MAG sensors
2 x RPWI sensors
High gain antenna
Medium gain antenna
Solar panels
(85 m2 total)

## Slide 4
Geophysics instruments
RIME ice-penetrating radar
  Subsurface structure of icy moons to 9km depth
3GM radio science
  Study of the gravity fields & interiors of icy moons, ephemerides of moons, structures of atmospheres & ionospheres of Jupiter, its moons, torus, & rings
GALA laser altimeter
  Tidal deformation of Ganymede, topography of surfaces of icy moons
PRIDE radio interferometry
  Precise determination of spacecraft position & ephemerides of moons via VLBI
Transponder
Ultrastable oscillator

## Slide 5
In situ instruments
PEP particle environment package
  Space environment in the Jovian system via electrons, ions, neutrals, energetic neutrals
RPWI radio & plasma waves
  Radio emission & plasma environment of Jupiter & its icy moons
J-MAG magnetometer
  Jovian & Ganymede magnetic fields, subsurface oceans of icy moons
RADEM radiation monitor

## Slide 6
Remote sensing instruments
JANUS camera
  Geology of icy moons, Io monitoring, Jovian atmosphere, dust rings, minor moons
MAJIS vis-IR imaging spectrometer
  Composition of icy moon surfaces & atmospheres, Io, Jovian atmosphere, dust rings, minor moons
Sub-mm wave instrument (SWI)
  Jupiter’s stratosphere & troposphere, atmospheres & surface of icy moons
UV spectrometer (UVS)
  Composition of icy moon atmospheres, Jovian & Ganymede aurorae, Jovian atmosphere

## Slide 7
Mission overview
  Tour (07/2031, ~3.5 years) including 8 F/Bs of Ganymede, 21 of Callisto, 2 of Europa
  High-phase inclination (>33°)
  Ganymede orbital phase
GCO5000
GEO
GCO500
GCO200
GEO
Ganymede orbital phase (9 months)

## Slide 8: MAJIS overview
Optical Head
Dimensions: 912x765x356 mm3, 41 kg
Main electronics
Dimensions: 320 x 249 x 161 mm3, 8.2kg
Parameter | Value | Comments
Spectral range VISNIR | 0.50 – 2.35 µm | 
Spectral range IR | 2.28 – 5.56 µm | 
Spectral sampling VISNIR | < 4 nm | 
Spectral sampling IR | < 7 nm | 
Number of spectels per channel | 508 | Up to 640 by TC, Spectral editing, Spectral binning x2 or x4 by TC
FOV | 0.06 rad x150 µrad | 30 km x 75 m during GCO500
Number of pixels along FOV for both channels | 400 | Spatial binning x2 or x4 by TC Windowing functionality
Scanning mechanism | ±4° | Motion compensation
Power | 26 W | Calibration mode: 35W
Poulet et al. SSR 2024 https://link.springer.com/article/10.1007/s11214-024-01057-2

## Slide 9: MAJIS is « primary » for 9 / 18 investigations
Primary
Supporting
Icy moons
Jupiter system

## Slide 10: Main design constraints
IR detector with cut-off at 5.56 µm
  Dark current (IR <90 K)
  Thermal contribution of the instrument (OH <130 K)
Power limitation due to solar panels at 5 a.u.
Highly variable radiation doses are expected around Jupiter
  high energy electrons (most frequent events) from 0.5 to 3 MeV
  high energy protons
Degradation of the coating of the optical elements
Detectors
  Potential increase of the dark current
  Spikes
Degradation of main electronics components
- Passive cooling
- Low conductance bipods
- Passive spot shielding
- On-board despiking procedure

## Slide 11: Overview
MAJIS OH
Nadir (Z_sc)

## Slide 12: Observation modes
Pushbroom:
  Scan mirror is not activated: rest (boresight) position
  Cross-slit motion provided by a spacecraft slew
  Repetition time = dwell time (time needed to cross the projected IFOV, taking into account detector binning)
Scan/pointing implemented by the scanning mirror (± 4°LOS)
  Cross-slit motion provided by the scan mirror
  Repetition time defined from SNR / available time constraints
Motion compensation
  Close to satellites, the dwell time is far too short (Europa F/B: 18 msec)
  The scanning mirror rotates back, LOS remains ~560 ms over each IFOV

## Slide 13: Internal Calibration Unit
Samples
Spectels

## Slide 14: Cruise events
EGA-3 17/1/29
EGA-2 28/9/26
LEGA-1 19-20/8/24
VGA 31/8/25
checkout
Lunar Earth GA
Payload checkouts
Star field observations
Planetary flybys
3I/Atlas
Launch (2023)
Jupiter insertion (2031)
Today
(a third of the cruise)

## Slide 15: Cruise events
EGA-3 17/1/29
EGA-2 28/9/26
LEGA-1 19-20/8/24
VGA 31/8/25
checkout
Lunar Earth GA
Launch (2023)
Jupiter insertion (2031)
  Validating the in-flight performance (radiometric, spectral, spatial, geometric, straylight, contamination, on-board S/W, thermal behavior) + Science opportunities
Today
(a third of the cruise)
Payload checkouts
Star field observations
Planetary flybys
3I/Atlas

## Slide 16: Payload checkouts and Cruise events
NECP, Payload Checkout #1 (January 2024),PC2 (July 2024), PC3 (March 2025), PC4 (February 2026): MAJIS works nominally on the nominal and redundant electronics using Internal Calibration Unit (ICU) measurements
Earth-Moon flyby (19-20 August 2024) major milestone to assess the in-flight performances with two spatially resolved external sources
3I/Atlas (November 2025, data received 2 weeks ago) major opportunity to check low signal readout mode (similar to exospheres, rings during the nominal science)
VISNIR channel
IR channel

## Slide 17: Lunar Earth Gravitational Assist on August 19/20, 2024
First-ever dual planetary flyby

## Slide 18: Operational constraints due to hot cruise conditions
S/C continuously protected from high solar flux and elevated temperatures, by orienting the HGA toward the Sun  Observation opportunity occurred during a quite short time window only when the boresight of MAJIS crossed the Moon and Earth surfaces
5 MAJIS cubes
19 MAJIS cubes

## Slide 19: Earth Flyby on August 20, 2024
MAJIS boresight = Z axis

## Slide 20: Moon flyby: MAJIS footprints
FOV windowing (64 pixels instead of nominal 400) to mitigate the signal saturation (Moon and Earth are very bright target for MAJIS !)
Sample various types of terrains (mare, highlands, crater rim,…) with a spatial sampling between 130 and 350 m
Incidence angle: from 92° to 26°

## Slide 21: Earth flyby: MAJIS footprints
Spatial sampling from 1 to 3 km

## Slide 22: Earth flyby: MAJIS footprints
Pixel resolution from 1 to 3 km
Malesia
Sumatra
IR

## Slide 23: LEGA data analyses
The Moon-Earth flyby observations of MAJIS provided a unique and first insight into the instrument performance in a real operative field

## Slide 24: LEGA data analyses: SNR performance
Moon observation
SNR in line with expected performance
Extrapolation to Ganymede indicates SNR in the range of 100-3000
Ganymede observation simulation

## Slide 25: LEGA data analyses
The Moon-Earth flyby observations of MAJIS provided a unique and first insight into the instrument performance in a real operative field
Besides the importance for the calibration and performance verification, the data also offers
  very interesting science investigations (in spite of the limited spatial coverage)
  contextualization of possible science at Jupiter
Poulet et al. Ann. Geo. (2026)
+ 5 other MAJIS papers (submitted)

## Slide 26: Moon flyby data analyses: mineralogy in the VISIR
#1
Band depth @ 950 nm
Maturity index
    Identify and map spectral mafic units with the VISNIR channel
    Derive spectral maturity and correlation with other spectral parameters
Reflectance
Pyroxene + Olivine
Pyroxene
Wavelength (nm)
1000
2000
1500
Identification of a km-sized fresh crater

## Slide 27: Moon flyby data analyses: thermal assessment in the IR
    Planck function dominated the signal in the IR channel Map diurnal temperature variations using the spectral range 3.0–5.5 µm
    Derive spectral emissivity (3.0–5.5 µm) and its dependence on surface texture for the first time  Increase in emissivity over mare regions (Müller et al. 2021)

## Slide 28: Earth flyby data analyses
The data opens also to very interesting science investigations for Earth atmosphere in spite of the very limited spatial and temporal coverage

## Slide 29: Earth flyby data analyses: cloud properties
Fresnel peaks
ICE CRYSTALLINITY
Spectral slope
Thermal intensity
ICE OPACITY / CLOUD TOP
Identification of areas dominated by water ice clouds (convective plumes)
Cloud top altitude based on the O2 760 nm band depth or water ice reflectance peak  10-17 km depending on the plumes
Vertical extension based on the projected shadows is ~9 km above the surrounding cloud layer
Ice boundaries
Shadow
Map of cloud top altitude (km)
MAJIS RGB map

## Slide 30: Earth flyby data analyses: cloud properties
H2O ice
Liquid H2O
Clouds Forward Model
Spectral modeling (MITRA) highlights the clouds microphysical properties
Some spectra require the presence of 2 layers of ice of different microphysics
Promising in enabling accurate retrievals of physical properties of icy satellites surfaces
Parameter | DECK 1 H2O ice | DECK 2 H2O ice
reff [μm] | 20 | 0.01
2.5 | > 20 | < 10-3
top [km] | 15 | unconstrained
Parameter | DECK 1 H2O liquid | DECK 2 featureless (we used H2O ice)
reff [μm] | 1 | 1
2.5 | 1.5 | < 10-2
top [km] | 1 | 11
model
model
MAJIS data
MAJIS data

## Slide 31: Earth flyby data analyses: lightening detection
Several emissions in the visible range were identified
The observed lines are attributable to atomic O and N and possibly H  First spectroscopic detection from space of lightning flashes at night
Lightning from the edges of a thick thunderstorm

## Slide 32: Earth flyby: comparison with other datasets
IASI (3.63-15.5 µm)
PRISMA (0.4-2.5 µm)
ENMAP (0.3-2.5 µm)
RT models (4A, NEMESIS, MITRA, …)
TROPOMI (bands 4,5,6,7,8)
Exciting comparison with several instruments (IASI, PRISMA, Enmap, TROPOMI) and RT model

## Slide 33: Earth flyby: comparison with other datasets
Excellent agreement with Enmap, PRISMA and IASI near-simultaneous observations in terms of spectral shapes, positions and radiance levels
Specular reflection

## Slide 34
Go JUICE !
Go MAJIS !