## Slide 1: The Roman Space Telescope
A Mission for the Community by the Community
Timothy D. Brandt
Associate Astronomer, Space Telescope Science Institute
on behalf of the Science Operations Center and the Mission
+++ The Community:
Partner Infrastructure Teams
Roman Wide Field Science Teams
Roman Science Collaboration

## Slide 4
Schlieder et al. 2024
Filter Wheel

## Slide 5
Schlieder et al. 2024
Calibration System

## Slide 6
Schlieder et al. 2024
Focal Plane Array

## Slide 7
Wide Field Instrument

## Slide 12
Big, Well-Defined Goals
Roman will measure:
Distribution of mass in the Universe
Universe’s expansion and expansion history
Demographics of planets down to ~Mars mass
Object: make the error bars as small as possible
Spergel et al. (2015)

## Slide 13
A Fundamental Change for NASA Flagship Missions
HST: four current instruments (ACS, COS, WFC3, STIS)
JWST: four instruments (MIRI, NIRISS, NIRCam, NIRSPEC)
NGRST: one core instrument (WFI), one tech demo (CGI)
Large pre-planned surveys replace disparate observing programs
Roman-WFI: only one core moving part (a filter wheel), 300 Mpixels.
Science requires, instrumental simplicity enables extreme precision.
Heavy lifting falls to detector characterization.

## Slide 14
18 H4RG-10 detectors, 301,989,888 pixels. Too much data.
Some reads will be averaged on-board into resultants.

## Slide 15
Detector gremlins and personalities
Correlated noise
Jumps and cosmic rays
Nonlinearity (classic and count-rate dependent)
Electronic gain
Pixel sensitivity/pixel area
Transient signals after reset
Interpixel capacitance
Persistence
Burn-in
Brighter-fatter effect
Thin film ice
Eric Switzer
Stephanie Cheung
Thushara Perera
Bernie Rauscher
Greg Mosby
Tathagatha Pal
Analia Cillis
Jeff Kruk
Stefano Casertano
Dan Kelly
Sarah Betti
Javier Sanchez
… and many more
All due to work by:

## Slide 16
Persistence follows a nice 1/t power law

## Slide 17
Average persistence from 1-11 minutes after illuminating to 155 ke-
FPA Handbook, Cheung et al.

## Slide 18
Example: integral nonlinearity (from the analog-to-digital converter)
Lab tests on Roman detector
electronics: known (sinsoidal)
voltage in, measure signal out.
Difference between data and
model (apart from clipping at 0,
65535) is integral nonlinearity

## Slide 19
Example: integral nonlinearity (from the analog-to-digital converter)
Lab tests on Roman detector
electronics: known (sinsoidal)
voltage in, measure signal out.
Difference between data and
model (apart from clipping at 0,
65535) is integral nonlinearity

## Slide 20
Integral nonlinearity (INL) is:
Highly structured
Symmetric about 32768 (= 215)
Unique to each readout channel
(c.f. Loose et al. 2018)

## Slide 21
Raw Read-to-Read Count Differences in Flatfield Images

## Slide 22
INL-Corrected Read-to-Read Count Differences in Flatfield Images

## Slide 23
Significant Impacts on Gain and Classic Nonlinearity

## Slide 24
Significant Impacts on Gain and Classic Nonlinearity

## Slide 25
How do we apply the correction with on-board read averaging?

## Slide 26
How do we apply the correction with group averaging?
Iterative approach:
Perform a nonlinearity correction to the first and last reads (which are not averaged)
Estimate the counts in each read, including the averaged ones
Adjust the estimated counts to match the read-averaged values
Apply nonlinearity corrections to the refined estimates of the counts in each read
Average the nonlinearity corrections by resultant

## Slide 27
Current Status
Good progress and/or solution found (bold=on ADS):
Tentative path forward:
Losing sleep; I hope to learn from all of you:
Nonlinearity
Electronic gain
Ramp fitting
Jump detection
Pixel area/sensitivity
Transient signals
Correlated noise
Interpixel Capacitance
Persistence
Thin-film Ice
Brighter-fatter effect
Other new and wonderful things?

## Slide 28: Backup slides

## Slide 29: Nonlinearity

## Slide 30: Nonlinearity

## Slide 31: Nonlinearity

## Slide 32: Burn-in

## Slide 33: Ramp fitting
See Brandt 2024a, b, published in PASP
Possible to write down, minimize chi squared pixel-by-pixel with (nearly) the right covariance matrix
Mitigates subtle biases in fitted count rates
Enables likelihood ratio tests for jump detection

## Slide 34: Brighter-fatter

## Slide 35: Brighter-fatter

## Slide 36: Transient signals

## Slide 37: Transient signals

## Slide 38: Transient signals