## Slide 1
Python x Pixel The collaborative detection simulation framework
10/03/2026
ESA SCI-FIV
Frédéric Lemmel, Vincent Affatato, Eloy Hernandez, Amitha Jha
ESO
Benoît Serra, Elizabeth George

## Slide 2: ESA SCI-FIV Lab: detectors tested in the last 5 years
ESA SCI-FIV Payload Technology Validation  Support for Future Science Missions
IBEX

## Slide 3: What do these ESA missions have in common ?
Same image detector technology: S-FPAs
Independent instrument simulator
Notes: Charge Couple Devices
For each of these projects an independent instrument simulator was developed.

## Slide 4: How does a detector work ?
Charge generation
Charge collection
Charge measurement
Readout electronics
Photons (ph)
Charge (e-)
Pixels (e-)
Signal (V)
Image (adu)
Photon collection
Charge transfer
Ph
e-
e-
e-
e-
V
V
V
ADU
ADU
ADU
Pixels (e-)
Detection chain
Notes: An imaging detector is a type of detector that is specifically designed to capture images of an object or scene.
It is a device that converts incident electromagnetic radiation, photons into an electrical signal that can be processed and displayed as an image.
Question to ask to choose detector: What do I want to observe? Which wavelength?

## Slide 5: What is a detection (chain) simulation?
IN
OUT
Notes: Input image for detection simulation. Add different kind of models that will add effects to the image, such you have an output image which you can proceed data processing with.

## Slide 6: Why simulating detection chains ?
Instrument and detector simulations are needed at each stage of a project
Technology and concept trade-off
Performance estimate
Instrument parameter optimization
Performance verification
Data processing pipeline validation
Instrument optimization and calibration
Performance verification
Calibrating out instrumental effect
Supporting data analysis
Definition
Design
Design Consolidation
Manufacture & Testing
Launch/First light
Commissioning
First science data
Operation
Scientific exploitation
Notes: Definition phase: Choose between different possibilities
Desgin: First estimate of performance
Detector modeling is key for

## Slide 7: Pyxel: Motivation & Principles
Reusability
Avoid duplication of work within and between institutes
Open source
Flexible
Multi-purpose
Knowledge Transfer
Collaborative
User-oriented
Python
Gitlab
Documentation
Reliability
Provide a reliable, validated set of detector models
Transparency
Integrated testing
Readability: YAML
Notes: Avoid duplication of work within and between institutes
Foster knowledge transfer in the instrumentation community
Provide a reliable, validated set of detector models

## Slide 8: Pyxel in a nutshell
A collaborative detection simulation framework
Simulates instrument effects on images from optics down to readout electronics
Supports CMOS, CCDs, APDs, MKIDs
Open-source Python Package (MIT)
History: 2017 (SCI-lab)  2019 (ESO joins)  2022 (Public release: v1.0)  2026 v2.17
First peer-reviewed paper: ”Pyxel: Detector and end-to-end instrument simulation” Arko M. et al. (2022)
https://esa.gitlab.io/pyxel/

## Slide 9: Pyxel in a nutshell
Active development: ~1 release/month + monthly meetings with external developers (ESO, …)
Strong collaborations with the community:
  MSSL: CIS304 pipeline (ARRAKIHS ESA mission)
  CRAL: H4RG pipeline (HARMONI instrument for ESO ELT)
  CEA Paris-Saclay: IBEX models (from Leonardo)
  ISAE-SUPAERO: radiation-induced dark current & RTS models
New users:
  ArcSec Space: star trackers for small satellites
  NEOMIR (NEO Mission in the InfraRed) image simulator: detection of asteroids near the Sun
https://esa.gitlab.io/pyxel/

## Slide 10: Example of built-in models in Pyxel
Charge generation
Charge collection
Charge measurement
Readout electronics
Photons unit: ph or ph/nm
Charge unit: e-
Pixels
unit: e-
Signal
unit: V
Image
unit: ADU
Photon collection
Charge transfer
More info about all implemented models: https://esa.gitlab.io/pyxel/doc/stable/references/models.html
Load star map
Scene
generation
Load image
Simple illumination
Stripe pattern
Shot noise
Load PSF
Multi-wavelength PSF
Photoconversion
Custom QE map monochromatic or multiwavelength
Load charge
Charge injection
CosmiX
Dark current
Charge deposition
Simple collection
Simple full well
Fixed pattern noise
Inter-pixel capacitance
Persistence
Simple charge-measurement
Non-linearity
DC offset
Pixel reset voltage
Readout noise
Simple ADC
Simple amplification
DC crosstalk
AC crosstalk
Dead time filter
Data Processing
Statistics
Extract Region of Interest
Mean-variance
Linear regression
Remove cosmic rays
Signal-to-noise ratio
Data unit: Not applicable
Scene unit: ph/nm/cm2
Charge-
Transfer
Inefficency

## Slide 11: Example of a Pyxel configuration file
YAML Configuration file:
Human-readable
Easy to edit
Groups of models and models
Detector info

## Slide 12: The three running modes
Exposure mode
the simple mode for health check or simulation of non-destructive readout
Observation mode
multiple pipelines exploring ranges of model or detector parameters
Calibration mode
optimize model or detector parameters to fit target data sets (model fitting, instrument optimization)

## Slide 13: The three running modes
Exposure mode
the simple mode for health check or simulation of non-destructive readout
Observation mode
multiple pipelines exploring ranges of model or detector parameters
Calibration mode
optimize model or detector parameters to fit target data sets (model fitting, instrument optimization)

## Slide 14: The three running modes
Exposure mode
the simple mode for health check or simulation of non-destructive readout
Observation mode
multiple pipelines exploring ranges of model or detector parameters
Calibration mode
optimize model or detector parameters to fit target data sets (model fitting, instrument optimization)

## Slide 15: The three running modes
Exposure mode
the simple mode for health check or simulation of non-destructive readout
Observation mode
multiple pipelines exploring ranges of model or detector parameters
Calibration mode
optimize model or detector parameters to fit target data sets (model fitting, instrument optimization)

## Slide 16: Output example: exposure mode
Optical PSF model
CosmiX
Charge distortion

## Slide 17: Output example: Calibration mode
H4RG generic pipeline calibrated using ESO MOONS lab data
Measured vs simulated PTC comparison
Calibrated model for non-linearity in SF pixels. Donor density, diode diameter, and fixed capacitance (Cf) as free parameters
Good match until saturation

## Slide 18: Pyxel is a collaborative framework
Pyxel 2.17
With your help!
Now
Towards v3.0

## Slide 19: What’s next ? For version 3.0
In development
GUI to edit configuration files
GUI catalogue of pre-configured pipelines (CIS304, H2RG, IBEX, …)
Improved LLM integration (Claude, ChatGPT, …) via MCP (Model Context Protocol)
ESA/ESO contributions
Channels, reference/masked pixels, Focal Plane Array support
Integration into ATREIDS (ARRAKIHS image simulator) for H2RG and CIS304 detectors
Improved compatibility with ScopeSim (ESO MICADO instrument)
Future work (help welcome)
New detector families (e.g. bolometers, …)
X-rays handling capability
Improved support of MKIDs (Microwave Kinetic Inductance Detectors)
External contribution
External contribution
From MSSL

## Slide 20: Take-home message
Pyxel - the collaborative detection simulation framework
One-liner installation
Try it: GUI, runs on binder, and remotely on browser
Tutorials and detailed documentation
Very flexible framework
Join the community!
https://esa.gitlab.io/pyxel/
pyxel@esa.int
Try it today ! More at the Poster Sessions
Play the Pyxel Quiz and
win Pyxel stickers !
See a live demo during the Posters session

## Slide 21
To all Pyxel developers present and past: Vincent Affatato, Eloy Hernandez, Amitha Jha, Frédéric Lemmel, Thibault Pichon, Jean Le Graët, Benoit Serra, Elizabeth George, Thibaut Prod’homme, Constanze Nghiem, Matej Arko, Dávid Lucsányi, Enrico Biancalani, Bradley Kelman, Hans Smit, Kieran Leschinski,
And to new collaborators since the v2.0 launch:
A big thank you

## Slide 22: Take-home message
Tutorials (https://esa.gitlab.io/pyxel-data..):
Simulating the AIRS detector /use_cases/CMOS/ARIEL_AIRS/airs.html
Saphira /workshops/irsa_workshop_2025/saphira.html
H2RG /use_cases/HxRG/h2rg.html
Photon Transfer Curve /workshops/developer_workshop_2024/ptc_exposure.html
Dark current vs Temperature /examples/models/dark_current/dark_current_rule07.html
…
Much more here: https://esa.gitlab.io/pyxel-data