## Slide 1: STILES
Anechoic chambers for full range radiation pattern characterization
March 17th, 2026

## Slide 2: STILES Proposal: Upgrading Next‑Generation Anechoic Chamber Capabilities
INAF Arcetri Astrophysical Observatory
AI#6201 – Anechoic Chamber
This activity consists in deploying a state-of-the-art anechoic chamber at the Arcetri Astrophysical Observatory (OAA), with operational coverage from VHF/UHF bands up to 110 GHz
  Refurbish old disused buildings on the OAA hill
  Install a fully operational shielded anechoic chamber (8 m × 4 m × 4 m) to overcome the current 2 GHz limitation imposed by the reduced size of the existing chamber
  Upgrade the nearby mechanical workshop for in‑house fabrication of custom mechanical components supporting operations
Participants are 2 staff technologists and 1 staff technician
Università degli Studi di Milano
AI#6202 – High Frequency Test Ranges
This activity aims to upgrade the antenna test facilities at the University of Milan (UniMi), extending their operational frequency range from 10 GHz up to 750 GHz
  Replace the current CATR with a much-improved dual-reflector CATR up to 600 GHz to perform high precision tests on electrically large antennas
  Install a thermally-controlled Planar Near-Field antenna measurement system up to 750 GHz
Participants are 1 professor and 2 TD technician

## Slide 3: AI#6201 – Anechoic Chamber
Far-Field Measurement
The AUT rotates in azimuth
The test antenna is fixed
Measurement: amplitude
Near-Field Measurement
The AUT is fixed
The test antenna probes the near AUT field
Measurement: amplitude and phase
What is an anechoic chamber
Past and future activities
  National facilities feed tests: Medicina, Noto, SRT;
  International projects: SKA, ALMA;
  External Services
Use: Antenna Beam Measurements
How it works

## Slide 4: AI#6201 – Anechoic Chamber
STILES grant CUP C33C22000640006: Budget: 425 k€ (VAT included)
Planned |  | 
Description | Original | Variation
Anechoic chamber | 168.500,00 | 168.500,00
Planar Scanner | 42.290,00 | 42.290,00
Computer/Workstation | 3.280,00 | 3.280,00
Accessories (software, cabling, etc.) | 63.180,00 | 63.180,00
Security costs | 3.450,00 | 0,00
Installation and on-site activity | 35.640,00 | 0,00
TOTAL | 316,340,00 | 277.250,00
Payments | 
Milestones | Payment
Advance Payment | 64.052,35
KM1: Planar Scanner | 62.310,67
KM2: Software + Workstation | 62.310,67
KM3: Anechoic Chamber Shipment | 62.310,67
KM4: Acceptance | 27.800,00
TOTAL | 278.784,36
Notes: Planned: Include la differenza tra l’offerta economica in risposta al bando di gara (Original) e la Variazione (Variation) dovuta al fatto che l’installazione ed i relativi costi di sicurezza sono stati rimossi a causa della indisponibilità del sito in cui la camera anecoica doveva essere installata
Payments: la tabella descrive le milestone di pagamento. La differenza con il ‘Planned’ (278.784,36 - 277,250,00) è dovuta agli extra costi, principalmente legati agli interessi.

## Slide 5: AI#6201 – Anechoic Chamber Design: view inside OAA building (map)
Planar Scanner
Anechoic chamber
Measurement and control Instrumentation
Controller
Auxiliary Rotator
Notes: Planned: Include la differenza tra l’offerta economica in risposta al bando di gara (Original) e la Variazione (Variation) dovuta al fatto che l’installazione ed i relativi costi di sicurezza sono stati rimossi a causa della indisponibilità del sito in cui la camera anecoica doveva essere installata
Payments: la tabella descrive le milestone di pagamento. La differenza con il ‘Planned’ (278.784,36 - 277,250,00) è dovuta agli extra costi, principalmente legati agli interessi.

## Slide 6: KM1: Planar Scanner Movitec and Controller ELCO
Installation and test: 4 September 2025

## Slide 7: KM2: Software and Workstation
Installation and test:
13, 14 and 15 October 2025

## Slide 8: KM3: Anechoic chamber delivery
Delivery at Medicina site:
5 November 2025

## Slide 9: AI#6202 – High Frequency Test Ranges
The small anechoic chamber “Barbie”
The big anechoic chamber “Ken”
Measurements of waveguide components

## Slide 10: AI#6202 – High Frequency Test Ranges
  IR0000034_PRO020 75 GHz – 750 GHz VNA extender modules
  IR0000034_PRO021 VNA with TestSet
  IR0000034_PRO041 Spectrum analyzer
  IR0000034_PRO042 Microwave absorber
  IR0000034_PRO043 CATR RX positioner
  IR0000034_PRO044 Optical table for NF
  IR0000034_PRO045 Compact Antenna Test Range (first tender)
  IR0000034_PRO199 CATR air‑conditioning and climatic chamber for NF
  IR0000034_PRO216 NF positioners
  IR0000034_PRO217 Ticra Tools license 2023
  IR0000034_PRO218 Ticra Tools license 2024
  IR0000034_PRO219 Ticra Tools license 2025
  IR0000034_PRO227 CST Studio 2023
  IR0000034_PRO228 CST Studio 2024
  IR0000034_PRO319 Compact Antenna Test Range
  IR0000034_PRO330 Passive components for NF
  IR0000034_PRO360 CATR completion
  IR0000034_PRO00516 Up/Down conversion system
20 procedures (total budget 2,149,641.83 € VAT included)
2 procedures for recruiting TD personnel (204.118,13 €)
  IR0000034_PRO013 (C. Franceschet)
  IR0000034_PRO037 (D. Capelli)
18 procurement procedures for identifying suppliers of goods, services, and works (1.945.523,70 €)

## Slide 11: Compact Antenna Test Range
Technical specifications
  Monolithic dual-reflector CATR
  1.9 m  1.7 m projected aperture
  r.m.s.  (/100)
  X-pol < -45 dB on principal axes
  Amplitude/phase ripples @40 GHz: &
Motion
  Azimuth, elevation, polarization, center of phase
Software development
  6-axis control & signal acq. and pre-processing (WIP)
Environment
  8 m  4 m  3.3 m anechoic chamber
  Controlled temperature (± 2°C) and RH (< 50%)

## Slide 12: Compact Antenna Test Range
Side-fed Offset Cassegrain with 4.4 m equivalent focal length
Study of spurious reflections/diffractions inside the anechoic chamber (in progress)
Study of the coupling of the real wavefront with the AUT (post processing – in progress)
Optical design

## Slide 13: Compact Antenna Test Range
Study of several linear and shaped profiles resulted in a serration profile
Development of a code for drawing parametrized profiles
  Number of “petals” per side
  h/D ratio
  parameter
  Tip position modulation factor (angle)
Simulation of more than 50 profiles to minimize the impact of diffraction in the Quiet Zone in terms of amplitude/phase ripples
Optimization of amplitude taper due to the feedhorn illumination (still in progress)
Parametric design of the serrations

## Slide 14: Compact Antenna Test Range
Amplitude cuts in the Quiet Zone at 20.35 GHz & 40 GHz
20.35 GHz
40.0 GHz

## Slide 15: Compact Antenna Test Range
Phase cuts in the Quiet Zone at 20.35 GHz & 40 GHz
20.35 GHz
40.0 GHz

## Slide 16: Compact Antenna Test Range
Modified anechoic chamber…
Main reflector…
… and sub-reflector!
Sub-reflector serrations
CATR installation
Credits: Media Lario S.r.l.

## Slide 17: Compact Antenna Test Range

## Slide 18: Compact Antenna Test Range
Main reflector fine adjustment
Main reflector serrations
Back of the main reflector
The two reflectors are machined on the back with a mesh pattern for lightweighting
The weight of each reflector including its support structure is 800 kg
We built reinforced concrete plinths under the floor to ensure load-bearing capacity and stable alignment over time

## Slide 19: Compact Antenna Test Range
Complete the hardware & software
  Conductive gap-filler between reflectors and serrations
  Polishing of reflector surface
  Cable routing (TX & AUT local oscillators, IF signals, etc.)
  Complete the development of launchers/horns
Verification
  Dynamic range up to 600 GHz, signal degradation inside chamber, etc.
  Mechanical repeatability of positioners
Post processing
  Study of antenna pattern correction (APC) techniques from literature and simulation
Work to be done before “turning on” the system…

## Slide 20: Near-field Measurement System
Technical specifications
  400 mm x 400 mm planar scanner
  Nominal fmax = 400 GHz (/50)  750 GHz (/25)
  Motion
    XY-axes (R.M.S. )
    Z-axis (100 mm travel)
    Polarization axis
Software development
  NF2FF routines verified at simulation level
  Motion/acquisition software integration being completed
Environment
  Climatic chamber w/ temperature (±0.3°C) and RH (±5%) control
  Possible upgrade to ISO-8
  Optical table with passive isolation (2.5 m  1.2 m)
Near-field climatic chamber
Near-field Test Range
up to 750 GHz

## Slide 21: Radiation pattern measurements
Sardinia Radio Telescope
49 radiation patterns at 43 GHz
19 radiation patterns at 41.5 GHz
LSPE/Strip
Co-polar and cross-polar pattern @13 GHz
Tenerife Microwave Spectrometer (TMS)

## Slide 22: Radiation pattern measurements
LiteBIRD MHFT BB1, H-plane at 100 GHz
Breadboard model “BB1” of the LiteBIRD MHFT instrument
  Frequency band: 90-110 GHz (W-band)
  Measurement-simulation agreement at the level of 0.1 dB down to near sidelobes

## Slide 23: Anechoic chambers for full range radiation pattern characterization
SKA – Square Kilometre Array
  SKA-Low: 50 MHz – 350 MHz
  SKA-Mid: 350 MHz – 15.4 GHz
ALMA – Atacama Large Millimeter/submillimeter Array
  10 bands in the range 35 – 950 GHz
LiteBIRD
  15 bands in the range 30 – 450 GHz
Many other INAF and UniMi projects
Service to industry and institutions
AI#6201 & AI#6202 will operate from 30 MHz to 750 GHz

## Slide 24: STILES
Anechoic chambers for full range radiation pattern characterization