## Slide 1
Mass Production and On-Site Deployment of the 10.5° Wide-Field SiPM Cherenkov Cameras for the ASTRI Mini-Array
From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO
20 – 24 July 2026, Sexten
Giovanni Contino – INAF IASF Palermo
on behalf the camera team – for the ASTRI Project

## Slide 2
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Outline
The ASTRI Project: from ASTRI Horn telescope prototype to Mini Array
Camera design: main subsystems
Camera tests and assembly phase
Overview of first results
Cameras mass production and deployment
Conclusions

## Slide 3
ASTRI (Astrofisica con Specchi a Tecnologia Replicante Italiana) is a project funded by the Italian Ministry of Education, University and Research (MIUR) and led by the Italian National Institute for Astrophysics (INAF).
The initial objective was to develop and construct an end-to-end prototype for the Small-Size Telescopes (SST) of the Cherenkov Telescope Array Observatory (CTAO); the result was the ASTRI-Horn telescope, at 1725 m a.s.l. in Serra La Nave, on Etna volcano, in Sicily.
The innovative 4-meter diameter dual-mirror Schwarzschild–Couder configuration enables a compact and lightweight camera design.
The ASTRI camera focal-plane is equipped with Silicon Photomultipliers (SiPMs) comprising 2368 pixels, designed to detect the Cherenkov light emitted by particle showers produced when high-energy gamma rays interact with the atmosphere.
These optical and sensors allows the ASTRI telescope to achieve a 10.5° Field of View (FOV), the largest ever attained by Cherenkov telescopes.
Overview of the ASTRI Project
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI - Horn

## Slide 4
The ASTRI–Horn results
Lombardi et al. 2020
The ASTRI-Horn camera has demonstrated high performance, reliability, and robustness, successfully operating even in the challenging volcanic environment of Mount Etna
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Leto et al. 2026, TBP
2017: First light
2018: The ASTRI-Horn telescope was the first Schwarzschild–Couder system to detect the Crab Nebula (Lombardi et al. 2020).
2023-2024: Extensive campaigns to reach the Crab spectrum (Leto et al. 2026, TBP)

## Slide 5
Telescopes currently in operation are marked with red circles
Map of the telescopes layout
The ASTRI Mini-Array
The ASTRI Mini-Array is the second phase of the project whose purpose is to construct, deploy and operate an array of 9 Cherenkov telescopes at the Observatorio del Teide in Tenerife (Spain), in collaboration with Instituto de Astrofísica de Canarias
The project is supported by other international partners, including the University of Sao Paulo – Brazil, North-West University, Fundaciòn Galileo Galilei, and Université de Geneve
All 9 telescope structures are already installed
3 cameras are currently operational and collecting Cherenkov events
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTR 1
ASTRI 3
ASTRI 2

## Slide 6
ASTRI Camera – 3D Exploded View
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Lids
Optical Filter
SiPMs
Front-End Electronics
Back-End Electronics
Voltage Distribution Box
Lid Motor Controllers
Heatsinks
Peltier Cells
Basket Fans
Basket Doors
Outlet Heatsink Fans
Inlet Heatsink Fans
Power & Data connectors
TEC Controllers

## Slide 7
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI CAMERA: The Focal Plane
The focal plane is composed of an array of 37 Photon Detection Modules (PDMs).
The PDM integrates one SiPM tile and the front-end electronics.
The tile features an 8×8 matrix of 7 mm × 7 mm pixels.
2,368 pixels
SiPM tile - 8x8 Pixels
57.6mm
57.6mm
7mm
7mm
.
Fully populated Focal Plane
PDM
SiPM Specifications | 
Model | S14521
Pixels arrangement | 8x8
Pixel dimensions [mm] | 7 x 7
Cell size [µm] | 75
PDE 405-450 nm | 50% - 54%
Gain @ 3V O.V. | 
DCR@ 0.5PE 15°C | 2800 kHz
OCT | 4.5%
Vbr @25°C [V] | 38.5
SiPM Specifications | 
Model | S14521
Pixels arrangement | 8x8
Pixel dimensions [mm] | 7 x 7
Cell size [µm] | 75
PDE 405-450 nm | 50% - 54%
Gain @ 3V O.V. | 
DCR@ 0.5PE 15°C | 2800 kHz
OCT | 4.5%
Vbr @25°C [V] | 38.5

## Slide 8
ASTRI PDM: Components
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
  CITIROC ASIC custom-developed by Weeroc in collaboration with INAF
  Low-noise Pre-amplifier
  Fast Peak Detector
  Trigger
ASIC board
SiPMs Tile
FPGA board
SiPM tile - 8x8 Pixels
57.6mm
57.6mm
7mm
7mm
  Hamamatsu MPPC-S14521 specifically developed for ASTRI
  Pixel size: 7mm x 7mm
  Cell size: 75 mm
  Xilinx Artix-7
  Digitalization
  Topological Trigger
  …

## Slide 9
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
  The ASIC board hosts two CITIROCs (by Weeroc)
    Reads out 32 SiPM signals, then 2 ASICs are needed to process 64 pixels of one PDM
    Two conditioning chains with different gain to cover a very high dynamic range: 0 – 2000 P.E. @ SiPM gain
    Both chains include a high-performance peak detector to capture the peak of the shaped pulses; only these peaks are digitally converted
    Lower power consumption compared to Cherenkov cameras operating in fast continuous sampling mode.
  The FPGA board is built around a Xilinx Artix-7 FPGA
    Configurable topological trigger algorithm runs in the FPGA of PDM
    The camera uses the powerful variance method, which does not introduce dead time; used to monitor pixel NSB
    Time-to-Digital Converter (TDC) for each trigger channel
CITIROC: Functional Block Diagram
FPGA
32 x 2
Triggers
Data
ASTRI Camera: Front-End Electronics

## Slide 10
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Camera: Back-End Electronics
ASTRI BEE designed by
Trigger FPGA
Data FPGA
Readout SoC
37 – PDM Data Connectors
Main functions:
  Collects & formats data from 37 PDMs
  Generates global Camera Trigger
  Manages slow control of all subsystems
Architecture:
  Zynq Ultrascale+ SoC (Linux OS)
  2× Artix-7 FPGAs:
    Trigger FPGA → processes 37 PDM trigger lines
    Data/Control FPGA → receives science data handles slow control
    Interconnection using axi chip2chip
  Robust connectors & shielded links
  Low latency on trigger path < 25ns RTT
Timing & Synchronization:
  Interfaces with White Rabbit PPS + 10 MHz clock
  Provides sub-nanosecond event timestamps
Supervisor and Control:
  Voltage Distribution subsystem
  Thermoelectric subsystem
  Calibration subsystem
  LIDs

## Slide 11
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Camera: Voltage Distribution Box
Typical Modular Archtecture – 37 VDB-PDM
Low-noise power supply for the Front-End Electronics
Individually calibrated HV outputs ensuring stable SiPM bias voltage
Bias voltage to SiPM detectors – current is limited to 70mA (max. current capablility 100mA) per tile
Calibration setup for the VDB-HV module
VDB block diagram
VDB High Voltage Module
VDB-PDM
ASTRI VDB designed by
Observations even under high Night Sky Background and moonlight conditions
Automated calibration of all HV channels

## Slide 12
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Camera: Thermal Control System
The Embedded Thermal Control System (TCS) has a crucial role for the ASTRI camera
Focal_Plane_T
up to a max ambient temp of 25°C
Reliable Thermal Control System based on 12 Peltier Cells
No additional external equipment or liquid-cooling circuit
ASTRI Mini-Array Focal Plane Support Structure:
Mechanical Support: Provides high-precision alignment for the sensor frames.
Thermal Management: Acts as a vital heat transmission backbone to stabilize focal plane operating temperatures.
Heat-Sink
Heat-Spreader
Large Thermal Insulation
ASTRI Mini-Array Camera TCS: Warm Side
Copper heat-spreaders interface directly with the Peltier cells' warm side.
Heat-sinks remove heat via forced air flow (4 fans per heat-sink).
Large thermal insulation decouples the warm electronics environment from the cooler operating components of the focal plane structure.
Missing SiPM Frame
SiPM Frams resting on the Focal Plane support Structure
SiPM focal plane thermal map from the AIV GUI. The temperature distribution across all tiles is highly uniform, stabilized within a ±1 °C range.
Voltage compensated for temperature variations

## Slide 13
Thermal Control System Performance
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten

## Slide 14
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Camera: Embedded Calibration System
Architecture of the Calibration System
2
X
2
50:50
Blue Laser
Green Laser
Fiber Optic
Coupler
Side Glow Fiber
Window
The ASTRI Camera integrates a sophisticated calibration system that enables the relative calibration of the focal plane, even in daylight
Integration of the window and the side glow fiber
Laser diodes holder and fiber couplers
Lid light-tightness gasket
Laser Pulser
Laser Driver
Laser Diode
Active Cooling System
Lids
Window
SiPM detectors
Side glow optical iber
Scattered light
Light pulses
Notes: The ASTRI Camera calibration system uses diode laser light, injected into a side-glow optical fiber that uniformly illuminates the focal-plane

## Slide 15
The Calibration System
Low Intensity Continuous-Light Measurements
Typical Variance vs SiPM Vbias curve for a pixel
dLog/dV
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Dark Conditions Measurements - Typical Staircase Curves
Pulsed-Light Measurements
Typical Pulse Height Distribution Curve
Light-tight lids allow high-statistics calibration during the day.
100% of night-time is preserved for scientific observations.
Breakdown Voltage Identification
Notes: Precise breakdown voltage identification is essential for setting the optimal bias voltage on each pixel. To this aim, we perform continuous-light measurements tracking signal variance vs. SiPM bias voltage
The staircase trigger rates and the pulse height distributions allow us to calibrate the absolute gain for every single pixel in the camera

## Slide 16
The results of the on-site calibration show:
gain uniformity ≤ 5 %
trigger threshold uniformity ≤ 3%
SiPM prompt cross-talk measurements in agreement with lab measurements
ASTRI-1
ASTRI-2
ASTRI-3
The Calibration System
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Notes: Precise breakdown voltage identification is essential for setting the optimal bias voltage on each pixel. To this aim, we perform continuous-light measurements tracking signal variance vs. SiPM bias voltage
The staircase trigger rates and the pulse height distributions allow us to calibrate the absolute gain for every single pixel in the camera

## Slide 17
ASTRI Camera: Control Software Architecture
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
AIV/AIT software client developed by INAF for multi-camera monitoring and control
The camera is equipped with a Control Software running in the BEE Processing Unit, which manages all the sub-systems and allows the slow control operations through an OPC-UA interface

## Slide 18
INAF Engineering Graphical User Interface
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Focal Plane Real-time Thermal Map
Variance High and Low Gain Visualization
Camera Rate and Dead time
High and Low Gain Scientific Events Visualization
Thermal Control System (TCS) Data Monitoring
Details of SCADA software system in Panebianco talk (22/07)

## Slide 19
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera tests
Tests of every single board
ASIC
FPGA
SiPM

## Slide 20
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera tests
Tests of every single board
ASIC
FPGA
SiPM
BEE
VDB
LV (PDM)
HV (Calibration)

## Slide 21
1 PPS
10MHz Clock
BEE Under test
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera tests
Electric tests of the camera
Startup of each individual subsystem
Calibration procedures (for validation)
Back End Electronics
Thermal Control System
Voltage Distribution Boards
Photon Detection Modules
Focal Plane
Calibration System
Dark
Continuous Light (LED)
with a specific tool
Temperature sensors calibration
Breakdown Voltage
Staircase curves
Pulse Height Distribution curves
Light-tight LIDs tests
LIDs mechanical stress test
Water tightness test of the camera
Test equipment for the VDB subsystem

## Slide 22
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan
1
Basket Assembly
2
Electronic Subframe
& Basket coupling
0
Electronic Subframe
Assembly
3
Wiring 1/2
4
Basket & Focal Plane
coupling
6
First start-up test
5
Wiring 2/2
Window & focal plane
temporary coupling
Thermal Control System
Test without light and
with continuous light
Kapton removal
Calibration System tests,
Calibration,
Other tests
LIDs test
Wiring finalization
Packaging
0
Focal Plane
Assembly
Calibration System
first test

## Slide 23
PDMs Mapping Verification
PDM mapping verification using a localized light source. The variance map identifies the illuminated PDM, allowing the correspondence between the focal-plane assembly and the BEE firmware mapping to be validated.
PDM 13
PDM 19
PDM 25
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten

## Slide 24
Scientific observations: >250h over 43 nights in various configurations:
Standard and high-zenith observations
Off-axis pointings up to 3.5°
Moonlight conditions up to 70% lunar phase
Crab Nebula detection:
~10σ detection in just 9h exposure
Spectrum up to ~30 TeV (consistent with other IACTs)
Position accuracy: 0.03° from nominal Crab location
Event rate:
80–95 Hz in dark nights
50–60 Hz under moonlight
Off-axis acceptance:
Flat up to 2.5°, ~40% drop at 3.5°
Moonlight observations:
14.6 ± 2.1 events/h; annual observing time: ~1900 h
ASTRI 1: Crab Observation Campaign (2024–2025)
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Details in Vercellone & Giuliani talk (20/07)

## Slide 25
ASTRI 1: Crab spectrum
power-law, 1 – 40 TeV logparabola, 1 – 40 TeV
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Details in Vercellone & Giuliani talk (20/07)

## Slide 26
ASTRI-1/3: Crab stereo observation
February 2026: first successful Crab stereoscopic observation with ASTRI-1 and ASTRI-3
Signal-to-Noise (S/N) Improvement: Great improvement in terms of Signal/Noise ratio with respect to single-telescope results
Lower Point Spread Function (PSF): Viewing the same atmospheric Cherenkov shower from two distinct vantage points allows the more accurate reconstruction of the shower axis
High-Energy Spectrum: significant spectral points in the 0.6–60 TeV with only about 22.5 hours
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
24.7σ in 22.5h
0.6-60 TeV
logparabola, 0.6 – 60 TeV
Details in Vercellone & Giuliani talk (20/07) and Vercellone talk (22/07)

## Slide 27
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
First Results: Stereoscopic Events
Example of atmospheric Cherenkov showers recorded simultaneously by ASTRI-1, ASTRI-2, and ASTRI-3.
Confirms that both the optics and the sensor array perform as expected
1
2
3
1
2 3
1
2 3
1
2 3
1
2
3

## Slide 28
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Mini-Array: First results
Since June 2026, the Cygnus region is being observed using the three currently operational telescopes. ASTRI's wide field of view allows it to capture multiple high-energy sources in the crowded Cygnus field within a single pointing
In January 2026, the ASTRI-1 telescope detected a high-energy flare (≈2.3 Crab Units) from the blazar Markarian 421 (ATel #17602)
3 days Light curve of the blazar Markarian 421 during a major flaring activity in January 2026
Ongoing Observation
Details in Quartiroli talk (20/07)

## Slide 29
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Mini Array Cameras: Timeline Installations and Operations
The consortium CAEN – EIE Group with important participation of Nuclear Instruments produced the ASTRI 1 camera. In September 2024, it was installed and achieved first light.
Since December 2024 INAF has taken charge of the production, integration and tests of the remaining cameras to populate the ASTRI Mini Array
October 2025 ASTRI 3 installation and first light
June 2026 ASTRI 2 installation and first light
Key milestones under INAF's leadership include:
Credits: A. Abba – F. Caponio
ASTRI 1 – Sept 2024
ASTRI 2 – June 2026
ASTRI 3 – Oct 2025

## Slide 30
Fourth Camera
Fifth Camera
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
ASTRI Mini Array cameras: future deployment roadmap
July 2026 – Installation of the fourth ASTRI camera
July 17th – ready for departure
probably today – shipping to Tenerife (by air)
next week – installation on ASTRI-4 telescope
Telescopes currently in operation are marked with red circles
Map of the telescopes layout
September 2026 – Installation of the fifth camera (on ASTRI-8 telescope)
November 2026 – Installation of the sixth (on ASTRI-9 telescope) and seventh cameras
Spring 2027 – Installation of the eighth and ninth cameras, completing the ASTRI Mini-Array
Cameras production are in charge of Istituto di Astrofisica Spaziale e Fisica Cosmica di Palermo and Osservatorio Astrofisico di Catania

## Slide 31
Cameras production, integration and tests time
# CAMERA | ASTRI 3 | ASTRI 2 | ASTRI 4
Start of production | June 1st 2025 | February 1st 2026 | May 1st 2026
Delivery to Tenerife | October 17th 2025 | June 5th 2026 | July 19th 2026
Time for the whole process | 4 ½ months | 4 months | 2 ½ months
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Chart: Production time
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 4.5 | 4 | 2.5 | 2.4 | 2.3 | 2.2 | 2.1 | 2
Serie 2 | 4.5 | 4 | 2.5

## Slide 32
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Conclusions
• The ASTRI Camera adopts a set of elegant, robust, and highly innovative engineering solutions:
– 7 mm x 7 mm SiPM pixels enabling excellent angular resolution – The largest (10.5°) FoV ever achieved in a Cherenkov telescope, obtained with a compact camera (just 500 mm diameter) with 2368 pixels, mounted on the 4-m diameter Schwartzschild-Couder dual mirrors ASTRI telescope, for wide-sky coverage – Use of the CITIROC ASIC with a low-noise, low-power, high-performance peak detector – A fully integrated, high-performance and self-contained thermal control system – this is the first Cherenkov camera operating without external liquid-cooling refrigerator – Reliable operation even under high NSB and moonlight conditions – A calibration system capable of operating in daylight, maximizing night-time observation time
• The Camera architecture meets the scientific and operational requirements for the full deployment of the ASTRI Mini-Array
• A key requirement is the maintainability: a rapid maintenance minimize intervention time
Notes: In addition to the outstanding reliability demonstrated since the ASTRI-Horn prototype, the ASTRI Mini-Array camera has been designed with maintainability as a key requirement. The camera incorporates a set of elegant and highly innovative engineering solutions, among which its modular architecture is one of the most distinctive. This architecture enables rapid corrective maintenance and the replacement of critical components with minimal intervention time, thereby minimizing telescope downtime. Such a capability is a crucial requirement for the efficient operation of a telescope array, where high instrument availability is essential to maximize the overall scientific performance.

## Slide 33
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Mass Production and On-Site Deployment of the 10.5° Wide-Field SiPM Cherenkov Cameras for the ASTRI Mini-Array
Thank You for Your Attention

## Slide 34
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan – PDM composition

## Slide 35
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan – Focal Plane assembly

## Slide 36
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan – Electronic Subframe assembly

## Slide 37
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan – TEC tests

## Slide 38
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
Camera assembly plan – Laser assembly

## Slide 39
Timing and Synchronization
G. Contino for the ASTRI project, From 9 to 40: the SST Telescopes and Gamma-Ray Science with ASTRI and CTAO 20 – 24 July 2026, Sexten
White Rabbit (WR) Integration: Delivers the 1 Hz Pulse-Per-Second (PPS) and a continuous 10 MHz reference clock to the Back-End Electronics (BEE).
Common Time Base: The 10 MHz reference is deterministically distributed to the BEE and all 37 PDMs. Phase-locked higher-frequency clocks are locally generated from the 10 MHz reference, enabling sub-nanosecond synchronization
BEE TDC Precision: An internal Time-to-Digital Converter measures PPS fractions with 1 ns resolution, enabling sub-nanosecond timestamping of camera triggers
Trigger Capture & Distribution: When a camera trigger is generated, its timestamp relative to the PPS is captured in the BEE and simultaneously distributed to all 37 PDMs.
White Rabbit System
10 MHz Clk
1 Hz PPS
PDM
1
PDM
37
BEE
10 MHz Clk
Trigger
FPGA
PLL
Read-Out
FPGA
Zynq
NTP
Camera Trigger
PDM Trigger
PDM
2