## Slide 1: Radar Measurements for the Characterization of Resident Space Objects
Final Meeting
Martedì 30 Giugno – Giovedì 02 Luglio
OAC - Osservatorio Astrofisico di Arcetri
M.A. De Luca

## Slide 2: TABLE OF CONTENTS
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
01
Background
02
Synodic Spin Period Estimation
05
Conclusions
03
BIRALES Test Case
04
Sidereal Spin Period + Spin Axis Estimation (from RCS time series)

## Slide 3: BACKGROUND
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Resident Space Object (RSO)
active satellites, decommissioned spacecrafts, orbital debris
~54000 RSO in orbit ( > 10 cm)*
For space traffic monitoring, effective characterization of orbiting objects is essential
Orbital Motion
Physical Properties
Rotational Motion
* https://sdup.esoc.esa.int/discosweb/statistics/ (Accessed 29/06/26)

## Slide 4: BACKGROUND
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
For space traffic monitoring, effective characterization of orbiting objects is essential
Orbital Motion
Physical Properties
Rotational Motion
Light Curves
OPTICAL SENSORS
RCS time series
Range and Doppler measurements
RADAR SENSORS
* https://sdup.esoc.esa.int/discosweb/statistics/ (Accessed 29/06/26)
Resident Space Object (RSO)
active satellites, decommissioned spacecrafts, orbital debris
~54000 RSO in orbit ( > 10 cm)*

## Slide 5: BACKGROUND
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Light Curves
OPTICAL SENSORS
RCS time series
Range and Doppler measurements
RADAR SENSORS
Determining the full attitude vector is inherently challenging. It requires:
Accurate shape
Reliable surface properties
Data rarely available in SSA operations
Resident Space Object (RSO)
active satellites, decommissioned spacecrafts, orbital debris
~54000 RSO in orbit ( > 10 cm)*
* https://sdup.esoc.esa.int/discosweb/statistics/ (Accessed 29/06/26)

## Slide 6: BACKGROUND
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Light Curves
OPTICAL SENSORS
RCS time series
Range and Doppler measurements
RADAR SENSORS
Determining the full attitude vector is inherently challenging. It requires:
Accurate shape
Reliable surface properties
Data rarely available in SSA operations
Estimate only key attitude-related parameters of rotating targets:
  Spin Period
  Spin Axis Direction
Model-Free approach: No prior knowledge of the target is exploited
CORE RESEARCH IDEA
Resident Space Object (RSO)
active satellites, decommissioned spacecrafts, orbital debris
~54000 RSO in orbit ( > 10 cm)*
* https://sdup.esoc.esa.int/discosweb/statistics/ (Accessed 29/06/26)

## Slide 7: SYNODIC SPIN PERIOD ESTIMATION
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
RCS time series
1
The estimation strategy depends on the nature of the available measurements :
Estimated synodic spin period
Time series
Lomb-Scargle (LS) Periodogram
Phase Dispersion Minimization (PDM)
Power Spectral Density (PSD)
Data Pre-Processing

## Slide 8: SYNODIC SPIN PERIOD ESTIMATION
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
RCS time series
1
The estimation strategy depends on the nature of the available measurements :
Lomb-Scargle Periodogram is used to estimate the PSD of the RCS time-series
The strongest peaks in the PSD are used to identify candidate rotation periods
Estimated synodic spin period
Time series
Lomb-Scargle (LS) Periodogram
Phase Dispersion Minimization (PDM)
Power Spectral Density (PSD)
Data Pre-Processing

## Slide 9: SYNODIC SPIN PERIOD ESTIMATION
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
RCS time series
1
The estimation strategy depends on the nature of the available measurements :
Estimated synodic spin period
Time series
Lomb-Scargle (LS) Periodogram
Phase Dispersion Minimization (PDM)
Power Spectral Density (PSD)
Data Pre-Processing
The candidates are given as input to the Phase Dispersion Minimization: calculates which one returns the lowest dispersion statistic

## Slide 10: SYNODIC SPIN PERIOD ESTIMATION
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
RCS time series
1
The estimation strategy depends on the nature of the available measurements :
Depending on the available input measurements, other strategies can be adopted and compared:
Estimated synodic spin period
Time series
Lomb-Scargle (LS) Periodogram
Phase Dispersion Minimization (PDM)
Power Spectral Density (PSD)
Data Pre-Processing
ACF: Autocorrelation Function
MED: Maximum Entropy Deconvolution
…..

## Slide 11: SYNODIC SPIN PERIOD ESTIMATION
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Micro-Doppler Spectrogram
The estimation strategy depends on the nature of the available measurements :
Micro-Doppler spectrogram
Time-Frequency Domain Autocorrelation (TFAC)
Estimated synodic spin period
TFAC: variant of the classic autocorrelation algorithm specific for time-frequency data [1]
[1] Serrano, A., et al., “Long baseline bistatic radar imaging of tumbling space objects for enhancing space domain awareness” ,2024
2

## Slide 12: BIRALES TEST CASE
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Estimated periodicity: 3.76 s
Frequency: 0.27 Hz
Periodicity: 3.76 s
BIRALES detection on November 1st, 2025
Target: Haiyang 2C (Norad ID 46469)
Reference target periodicity: 3.5-4 s
Bandwidth: 10.43 Hz
Signal power trend

## Slide 13: BIRALES TEST CASE
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
BIRALES detection on November 1st, 2025
Target: Haiyang 2C (Norad ID 46469)
Reference target periodicity: 3.5-4 s
Micro-Doppler
Estimated periodicity: 3.76 s
Bandwidth: 2.61 Hz

## Slide 14: SIDEREAL SPIN PERIOD + SPIN AXIS ESTIMATION (FROM RCS TIME SERIES)
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Key idea: Even if is constant, the synodic period changes over time as the observation geometry varies  this variation is exploited
Goal: estimate the sidereal (inertial) spin period and spin-axis direction
3
Clustering & Cleaning
Group and filter the candidate solutions
4
4
Best estimate
Select best cluster and best estimate
2
Patternsearch
Constrained optimization over 3 variables
1
Estimate
(synodic spin period estimation)

## Slide 15: SIDEREAL SPIN PERIOD + SPIN AXIS ESTIMATION (FROM RCS TIME SERIES)
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
3
Clustering & Cleaning
Group and filter the candidate solutions
4
4
Best estimate
Select best cluster and best estimate
2
Patternsearch
Constrained optimization over 3 variables
1
Estimate
(synodic spin period estimation)
Search Domain
 | LB | UB
 | −180° | 180°
 | −90° | 90°
[s] | 3 | 250
 | LB | UB
 | −180° | 180°
 | −90° | 90°
 | 3 | 250
ƒ
Objective function
Based on a variant of Phase Dispersion Minimization
Constraint function
Predicted synodic period from must be compatible with
Multi-Start: 500 Latin-Hypercube start points

## Slide 16: SIDEREAL SPIN PERIOD + SPIN AXIS ESTIMATION (FROM RCS TIME SERIES)
3
Clustering & Cleaning
Group and filter the candidate solutions
4
4
Best estimate
Select best cluster and best estimate
2
Patternsearch
Constrained optimization over 3 variables
1
Estimate
(synodic spin period estimation)
Missione 4 • Istruzione e Ricerca
Search Domain
 | LB | UB
 | −180° | 180°
 | −90° | 90°
[s] | 3 | 250
 | LB | UB
 | −180° | 180°
 | −90° | 90°
 | 3 | 250
ƒ
Objective function
Based on a variant of Phase Dispersion Minimization
Constraint function
Predicted synodic period from must be compatible with
Multi-Start: 500 Latin-Hypercube start points

## Slide 17: SIDEREAL SPIN PERIOD + SPIN AXIS ESTIMATION (FROM RCS TIME SERIES)
3
Clustering & Cleaning
Group and filter the candidate solutions
4
4
Best estimate
Select best cluster and best estimate
2
Patternsearch
Constrained optimization over 3 variables
1
Estimate
(synodic spin period estimation)
Missione 4 • Istruzione e Ricerca
As a final step, a grid search is carried out around the identified best-fit to map all local minima of the objective function in
 Geometrically ambiguous solutions:

## Slide 18: SIDEREAL SPIN PERIOD + SPIN AXIS ESTIMATION (FROM RCS TIME SERIES)
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Can the ambiguities be resolved by simultaneously observing the object from multiple locations?
TIRA LOCATION
MEDICINA LOCATION

## Slide 19: CONCLUSIONS
Missione 4 • Istruzione e Ricerca
Missione 4 • Istruzione e Ricerca
Different radar measurements can characterize spinning objects:
  RCS: estimates spin period and spin-axis direction
  Micro-Doppler: estimates spin period (spin-axis direction estimation is under development)
Ambiguities are intrinsic to the problem, arising from the observation geometry:
  Multiple simultaneous observations of the same object from different locations may resolve or reduce them
BIRALES test case  potential for spin-axis characterization:
  Acquisition time window increase thanks to the FoV extension
  Conduct analysis with CW only

## Slide 20: Thank You For Your Attention!
Final Meeting
Martedì 30 Giugno – Giovedì 02 Luglio
OAC - Osservatorio Astrofisico di Arcetri
M.A. De Luca