## Slide 1: Εuropean Exascale System Ιnterconnect & Storage
Manolis Marazakis and Manolis Ploumidis,
Systems Software Engineers
Foundation for Research & Technology - Hellas (FORTH)
ExaNode, ExaNeSt, EcoScale Joint Application Workshop
INAF, Trieste - September 19-20, 2016
www.exanest.eu

## Slide 2: The ExaNeSt Consortium
Storage & data
UK
Italy
Greece - coordinator
UK
UK
UPV - ES
Technology
Interconnects
Netherlands
Germany
Applications
Italy
Italy
Italy
www.exanest.eu

## Slide 3: What ExaNeSt is about
ARMv8, UNIMEM Partitioned Global Address Space (PGAS)
  Low-energy compute nodes
  Low-overhead communication
  Heterogeneous: FPGA accelerators
  Working closely with ExaNoDe, EcoScale (& EuroServer)
Network: unified compute & storage, low latency
Storage: distributed, in-node non-volatile memories
Extreme Compute Density: totally-liquid cooling
Prototype: 1K cores, 4 Tby DRAM, 40 Tby SSD, 0.5 M DSP sl’s
Real Applications: Scientific, Engineering, Data Analytics

## Slide 4: The UNIMEM Architecture, used in ExaNeSt
Realistic rack-level shared-memory based on Unimem
Single owner per page: every memory page in at most one node’s cache
  no system-level hardware coherence traffic
  owner can be any node - not just the (local) one adjacent to DRAM
Example usage models
Remote memory accesses, remote mailbox, remote interrupts:
  for fast synchronization & processing of distributed (read-only) data
Zero-copy remote direct memory transfer (RDMA)
  sockets over zero-copy RDMA
  MPI over sockets
Remote-page borrowing for memory disaggregation
Extension to in-node fast NVM
Every file in one node’s NVM cache

## Slide 5: ExaNeSt: Unimem PGAS Memory Model
Enables remote loads/stores to global address space
System-wide coherent memories w/o expensive hardware
  only one node may cache data
Global Virtual Address Space
  Resiliency : page can move seamlessly upon node failures
  Difficult to maintain a global page table

## Slide 6: ExaNeSt Unimem Implementation
Enables remote loads/stores to global address space
System-wide coherent memories w/o expensive hardware
  only one node may cache data
Global Virtual Address Space
  Resiliency : page can move seamlessly upon node failures
  Difficult to maintain a global page table
ExaNeSt pages stay within a coherence island (node)

## Slide 7: ExaNeSt Node: Quad-FPGA-DaughterBoard (QFDB)
4 Ultrascale+ FPGAs
  all-to-all connectivity
    2 x HSS (GTH) + 16 x LVDS
64 GBytes DDR4
  16 GB/FPGA @ 160 Gb/s
512 GBytes SSD/NVMe
  4x PCIe v2 (8 GBytes/s)
10 HSS links to remote
  10 Gb/s per link
    16 Gb/s best case
120x130mm2
Currently in layout + fabrication

## Slide 8: The ExaNeSt Prototype (2016 – 17)
Electronics immersed in
3M Novec liquid
Rack-level water circulation
Using Xilinx Zynq UltrScale+ FPGAs
  Four 64-bit ARM cores per FPGA
Quad FPGA Daugther Boards (QFDB)
  Four FPGAs per QFDB
8 QFDB’s per Blade
System: Dozen Blades

## Slide 9: ExaNeSt Storage Architecture
Bring data closer to compute  inside QFDB-level SSDs
QFDBs w. SSD storage

## Slide 10: ExaNeSt: Per-Job On-Demand SSD Caches
File Payload : cache-hit @ SSDs cache; on miss  storage server

## Slide 11: Applications, Traces
Traces generated:
  Scalasca profiling tool:
  MPI calls instrumented,
  several GBytes per trace,
  filtered down to tens of Mbytes by keeping what our network simulators will need;
  generally, to be made publicly available.
Main Applications:
  Material science: LAMMPS
  Climate change: REGCM
  Engineering: openFoam, SailFish
  Astrophysics: Gadget, Pinocchio, Changa, Swift
  Neuroscience: DPSNN
  High Energy Physics: LQCD
  Data Analytics: MonetDB
Next – Applications Porting & Tuning:
  currently porting selected App’s to ARM, on the EuroServer+ExaNoDe Prototype

## Slide 12: Inter-Project Areas for Collaboration
MPI for UNIMEM [ExaNoDe + ExaNeSt]
  App. Profiling: time-based + network patterns
  Implementation: MPICH vs OpenMPI ?
  Evaluation
Accelerators [ECOSCALE + ExaNoDe + ExaNeSt]
  Native + VMs
  Toolchain and development workflow (OpenCL ?)
  Evaluation
Resilience (cross-cutting concern  HARD)
  Checkpoints
  Replicated execution
  RAS properties

## Slide 13: Εuropean Exascale System Ιnterconnect & Storage
Interconnection Network
In-node Storage
Advanced Cooling
Real Applications
www.exanest.eu

## Slide 14: Notes on MPI

## Slide 15: MPI: Implementations
MPICH
  High performance and widely portable implementation of the Message Passing Interface (MPI) standard
  https://www.mpich.org/
OpenMPI
  An open source high performance message passing library
  https://www.open-mpi.org/
MVAPICH
  MPI over InfiniBand, Omni-Path, Ethernet/iWARP, and RoCE
  http://mvapich.cse.ohio-state.edu/

## Slide 16: MPI: Messaging passing protocols (1)
Point-to-point
Collective communications
One-sided communications

## Slide 17: MPI: Message passing protocols (2)
short (eager-to-send) vs long protocol (rendezvous)
for point-to-point communication

## Slide 18: MPI: Message passing protocols (3)
Collective operations in MPICH
(implemented through point-to-point2 communications)
Source: W. Gropp, E. Lusk, N. Doss, and A. Skjellum. A high-performance, portable implementation of the MPI message passing interface standard

## Slide 19: MPI: Message passing protocols (4)
Byte-Transfer Layers (BTL)
Communications framework (PML)
point-to-point communication in OpenMPI

## Slide 20: Message passing protocol optimization
Employing remote memory operations
Assuming underlying hardware support
Receiver advertises a buffer and tag for expected data
Sender directly writes to receiver’s advertise buffer
Osamu Tatebe and Yuetsu Kodama and Yoshinori Yamaguchi and Satoshi Sekiguchi
Highly Efficient Implementation of M PI Point-to-point Communication Using Remote Memory Operations
ICS '98 Proceedings of the 12th International Conference on Supercomputing

## Slide 21: Notes on UNIMEM

## Slide 22: The UNIMEM Architecture, used in ExaNeSt
System-level interconnect
island
island
cache
P
P
Memory
cache
P
P
Memory
cache
P
P
Memory
NO system-wide
H/W coherence
Global Address Space
H/W cache-coherence island

## Slide 23: UNIMEM Remote Accesses: coherent at destination
System-level interconnect
island
cache
P
P
Memory
cache
P
P
Memory
Remote store
(and load)
NO system-wide
H/W coherence
H/W cache-coherence island
Global Address Space

## Slide 24: UNIMEM Coherent Remote Direct Memory Access
System-level interconnect
island
cache
P
P
Memory
cache
P
P
Memory
RDMA
NO system-wide
H/W coherence
H/W cache-coherence island
Global Address Space

## Slide 25: Page Borrowing: pages used & cacheable only remotely
System-level interconnect
island
cache
P
P
Memory
cache
P
P
Memory
Page borrowing
NO system-wide
H/W coherence
H/W cache-coherence island
Global Address Space