## Slide 1: Expected performances of ASPIICS/Proba-3: simulated data
S. V. Shestov, A. N. Zhukov, B. Inhester, L. Dolla, M. Mierla
Royal Observatory of Belgium,
Max Planck Institut für Sonnensystemforschung

## Slide 2
Shestov et al. // A&A 652, A4, 2021

## Slide 3: ASPIICS/Proba-3 summary
144 m
6 spectral channels:
    • white light (535-565 nm) • 3 polarized white light • Fe XIV passband at 530.5 nm • He I D3 passband at 587.7 nm
2048x2048 pixels (2.8 arc sec per pixel)
cadence 60 s / 2 s (using ¼ FoV)
Launch: Q2 2023
Orbit 19h38m; 6h – formation flying
ROB – Science Operation Center
Advantages of ASPIICS:
  minimal FoV ~ 1.097 R⊙
  and
  extremely low straylight

## Slide 4: ASPIICS simulated data: optical effects
Optical throughput / sensitivity;
Spectral sensitivity;
Vignetting by the external occulter;
Flat field;
Straylight – diffraction, scattering, ghost light;
objective Ø (5 cm);
lenses&filters;
2.81 “/pix;
wide-band (535-565 nm),
for FeXIV line (0.6/530.5 nm),
for HeI line (2/587.7 nm);
~25 pix circular zone, inner FOV;
Aime (2013), Rougeot et al. (2017);
Shestov&Zhukov (2018);
Shestov et al. (2019);
detector sensitivity;

## Slide 6: ASPIICS simulated data: detector effects
ISPHI CMOS from CMOSIS, 2k × 2k, 10 μ pixel, 14 bits;
Quantum efficiency (~65%);
Flat field;
Gain ~ 0.12 DN/el;
Read-out noise ~ 8 DN;
Dark current (small at <-40 °C) + bias;
Nonlinearity;
Noises (incl. shot, read-out, ADC);

## Slide 7: Simulated images [DN] for texp 0.1, 1.0, and 10 s;

## Slide 8: Influence of random noise

## Slide 9: Summary
Physical model for ASPIICS simulated images;
Correct parameters as input → realistic images, sensitivity, SNR, etc;
Main contribution of noise – readout noise;
IDL code;
Also in the manuscript:
  Discussion of assumption & models;
  Influence of noises and systematic errors;
  Possibility to work with 2 texp to cover full dynamic range;
“Expected performances of the PROBA-3/ASPIICS solar
coronagraph: Simulated data” Shestov et al. // A&A 652, A4, 2021