## Slide 1: SHARK-NIR
Daniele Vassallo on behalf of SHARK-NIR team
OAPd days, June 18 2019

## Slide 2: THE Padova SHARK-NIR TEAM
PI: Jacopo Farinato
System Engineer: Valentina Viotto
Project Manager: Maria Bergomi
Optical design: Davide Greggio, Demetrio Magrin
Mechanical design: Tomelleri Srl with a local interface: Luca Marafatto
Procurement: Maria Bergomi, Davide Greggio, Daniele Vassallo, Valentina D’Orazi, Luca Marafatto, Simonetta Chinellato
AIV Team: Luca Marafatto, Federico Biondi, Elena Carolo, Luigi Lessio, Gabriele Umbriaco, Maria Bergomi, Marco Dima, Davide Greggio, Daniele Vassallo, Kalyan Radhakrishnan
SW Team: Marco De Pascale, Andrea Baruffolo, Bernardo Salasnich, Daniela Fantinel
Data reduction: Dino Mesa, Elena Carolo, Daniele Vassallo
Coronagraphic performance & simulation: Daniele Vassallo, Elena Carolo
Science Team: Valentina D’Orazi, Raffaele Gratton, Silvano Desidera
Notes: 40 ordini

## Slide 3: THE SHARK-NIR CONSORTIUM
Steward Observatory (LBTI interfaces, NIR camera sub-system)
MPIA (Motors electronics and SW design support)
IPAG (Coro mask design)
INAF-Brera (Dispersive elements design)
INAF-Trieste (Data archiving)
INAF-Arcetri (AO Interface)
INAF-Roma (Synergy with VIS Channel)
Science team (astronomers from 12 institutes)

## Slide 4: WHAT IS SHARK-NIR?
Camera for high-contrast imaging and spectroscopy in the NIR, mainly dedicated to detection and characterization of exoplanets
Observing modes:
  Classical Imaging
  Coronagraphic imaging
  Long Slit spectroscopy
  Dual Band Imaging
Synergy with other LBT instruments
(SHARK-VIS, LMIRCAM)
SHARK-VIS
LBTI
SHARK-NIR

## Slide 5: INSTRUMENT SPECIFICATIONS
SHARK-NIR main characteristics | 
Observing Modes | Imaging/Coronagraphy/Spectroscopy/DBI
Detector format [px] | 2048x2048 (≈1220x1220 used area)
Waveband [μm] | 0.96 – 1.7
FoV ["] | 18 x 18
FoV along the diagonal ["] | 25.5
Plate scale [mas/px] | 14.5
Airy Radius @ 0.96 micron [px] | 2
Nominal Strehl at <18’’ FoV diameter (in all Bands) | >98%

## Slide 6: OPTO-MECHANICAL LAYOUT
Weight: 350 kg
Size: 1500 x 800 x 800 mm

## Slide 7
DM
apodizer
ADC
beam splitter to
the tip-tilt WFS
off-axis
parabola
off-axis
parabola
off-axis
parabola
off-axis
parabola
fold mirror
fold mirror
fold mirror
cryostat
window
Narcissus
mirror
cold baffle
detector
Science filter
wheels
occulters
and slit
Pupil lens
(deployable)
incoming
light
~300 mm
Lyot stop,
GRISM
Coronagraphic planes
~600mm
OPTO-MECHANICAL LAYOUT

## Slide 8: SPECTROSCOPIC MODE
DISPERSIVE ELEMENTS |  | 
 | Low Res | Medium Res
Dispersing element | Prism | Grism
R | 100 | 700
CORO SLITS WITH OCCULTER |  | 
 | Slit width | Occulter size
Coro slit 1 | 100 mas | 100 mas
Coro slit 2 | 100 mas | 200 mas
Focal plane

## Slide 9: DUAL BAND IMAGING MODE
DUAL BAND FILTERS |  |  |  | 
Name | λ1 [nm] | Δλ1 [nm] | λ2 [nm] | Δλ2 [nm]
HOLE (no DBI) | - | - | - | -
H2-H3 | 1588.8 | 53.1 | 1667.1 | 55.6
ContJ-Pa β | 1215.7 | 18.3 | 1281.3 | 20.9
ContH-Fe II | 1557.8 | 24.1 | 1645.5 | 26.1
Phase diversity | Window |  | Defocusing lens | 
Radial FoV 1”
Pupil plane
NIR Camera
Window

## Slide 10: THE HIGH-CONTRAST IMAGING FORMULA
How do we obtain high contrast in the vicinity of such bright stars?
XAO correction +
Optimized wavefront control strategy +
Coronagraph(s) +
Post-processing pipeline =
High contrast

## Slide 11: WAVEFRONT CONTROL
WFS Camera
InGaAs camera (C-RED2)
Sensitive in the full SHARK-NIR waveband (0.96-1.7 μm)
Frame-rate up to 14 kHz (with 32X32 px window)
Low RON (<30 e- )
3-5 mas precision up to R=10 @ 1KHz
Deformable Mirror
ALPAO DM 97-15
97 actuators, 13.5 mm pupil, up to 2 kHz speed
NCPA can be corrected internally without affecting pyramid’s performance
NCPA measured with phase diversity on science image
A deformable mirror to correct for instrumental aberrations and to stabilize the PSF

## Slide 12: WAVEFRONT CONTROL - ON-GOING ACTIVITIES
  RTC tests, applying a time history taken from real data at LBT
RTC by Microgate:
TT control loop and quasi static NCPA application
1 KHz correction
45 mas disturbance

## Slide 13: CORONAGRAPHS
Apodizer Mask
1st pupil
plane
2nd pupil
plane
Occulter Mask
Lyot Stop
Scientific
image
Intermediate
focal plane
Science
focal plane
Weak companion
Lyot stop
Weak companion
13
Exoplanets | FQPM Working in H-band Access to the whole 18ⅹ18’’ FoV Very small IWA (~50 mas) High throughput Very sensitive to low-order aberrations | SHAPED PUPIL Working in H-band Small field (100-300 mas) High contrast near to the star Robust to low-order aberrations
Disks/Jets/ AGN |  | GAUSSIAN LYOT Optimized for both J and H band observations Moderate contrast Access to the whole FoV

## Slide 14: CORONAGRAPHS - ON-GOING ACTIVITIES
  Coronagraphic masks characterization, performance analisys, alignment procedure
Simulated Real
Simulated Real

## Slide 15: MILESTONES
2016 Feb. Conceptual Design Review end 2017 Jan. Final Design Review 2017 Apr. FDR delta review 2017 Jul. Board approval 2017 Aug. Start of procurement phase 2017 Nov. Start of AIV phase with component tests 2017 Nov. Delivery of the Electronics Rack from MPIA to INAF 2018 Oct. Delivery of the coronagraphic masks from IPAG to INAF 2019 Sep. Delivery of the NIR camera sub-assembly from SO to INAF 2019 Sep. Delivery of dispersive element 2019 Dec. End of SW MAIT 2019 Dec. End of AIV phase 2020 Mar. PAE review 2020 Mid Start of commissioning at LBT 2020 Fall SHARK-NIR in operation

## Slide 16: Thank you for your attention!