## Slide 1: MAORY AO description
Work Package END TO END SIMULATION team
Presented by W.P. manager Guido Agapito

## Slide 2: How will MAORY AO work?
Telescope collimates (Active optics correction, phasing, …).
Telescope turns on LGS on and points them where MAORY needs them.
LGS light on MAORY WFSs.
Telescope gives control to MAORY.
MAORY starts collimating optical relay and corrects HO turbulence – no TT correction, no plate scale correction, no truth correction.
MAORY acquires LO and starts correcting TT, plate scale and truth.

## Slide 3: How will MAORY AO work?
Telescope collimates (Active optics correction, phasing, …).
Telescope turns on LGS on and points them where MAORY needs them.
LGS light on MAORY WFSs.
Telescope gives control to MAORY.
MAORY starts collimating optical relay and corrects HO turbulence – no TT correction, no plate scale correction, no truth correction.
MAORY acquires LO and starts correcting TT, plate scale and truth.

## Slide 4: MAORY AO
MAORY corrector is M (=3) DMs, M4 at 600m and 2 post focal DMs at 8 and 16km.
DMs
Telescope pupil
Technical FoV
Science FoV

## Slide 5: MAORY AO
Technical FoV
Science FoV
Edge of DMs is not used for Science FoV correction.
DMs
Telescope pupil

## Slide 6: MAORY AO
We want to optimize correction on a FOV of interest (science FoV) while sensing a large FOV (technical FoV).
Reconstruction is done on the full sensed atmospheric volume discretized in N layers (N>M) and n modes for each layer.
Then this reconstruction is projected on DMs maximizing performance on the FoV of interest.
layers
DMs
Telescope pupil

## Slide 7: MAORY AO
LGS:
slopes (6 stars, 80x80 SHSs): 54k elements
Reconstruction matrix: 54k × 28k elements
Projection matrix: 28k × 6k elements
layers
DMs
Telescope pupil

## Slide 8: MAORY AO
layers
DMs
Telescope pupil
LGS launcher
telescope
LGS spot

## Slide 9: MAORY AO
layers
DMs
Telescope pupil
Multiple LGSs, like human binocular vision, gives the ability to perceive a three-dimensional image (phase).
LGS launcher
telescope
LGS spot
LGS spot
tech. FoV
X”

## Slide 10: MAORY AO
layers
DMs
Telescope pupil
Technical FoV is partially uncontrolled:
DMs and layers edge is not sensed by LGS.
LGS launcher
telescope
LGS spot
LGS spot

## Slide 11: MAORY AO – LGS/HO
MAORY uses “multi direction vision” given by LGSs to measure aberration (no TT) and reconstruct it on a discretized volume:
  N (=7) planes, called layer or reconstructed layers.
  n (=4000) shapes, called modes, for each plane/layer.
MAORY projects the reconstructed aberration from the discretized 3D volume to M (=3) planes collocated on the DMs (M4 and the post focal ones).
  The projection is optimized to maximize performance on science FoV without affecting too much PSF quality technical FoV (correction on NGSs is required to get good SNR).
MAORY RTC integrates the actual shape with each new aberration residual measurement.
  Integration is done at the level of DMs modes.

## Slide 12: How will MAORY AO work?
Telescope collimates (Active optics correction, phasing, …).
Telescope turns on LGS on and points them where MAORY needs them.
LGS light on MAORY WFSs.
Telescope gives control to MAORY.
MAORY starts collimating optical relay and corrects HO turbulence – no TT correction, no plate scale correction, no truth correction.
MAORY acquires LO and starts correcting TT, plate scale and truth.

## Slide 13: MAORY AO
layers
DMs
Telescope pupil
NGSs are used by:
LO WFSs:
  Correct Tip-Tilt.
  Correct plate scale errors (quadratic ones).
Reference WFSs:
  Truth sensing (NCPA, sodium related aberrations).

## Slide 14: MAORY AO
layers
DMs
Telescope pupil
Multiple NGSs, like LGSs, gives the ability to perceive a three-dimensional image (phase), but their position (asterism) depends on their availability…
tech. FoV
X”

## Slide 15: MAORY AO
layers
DMs
Telescope pupil
LO:
slopes: 24 elements
Reconstruction matrix: 24 × 5 elements
Reference:
slopes: 450 elements
Reconstruction matrix: 450 × 1400 elements
Projection matrix: 1400 × 600 elements

## Slide 16: MAORY AO
layers
DMs
Telescope pupil
… and pick-up geometry

## Slide 17: MAORY AO
layers
DMs
Telescope pupil
NGSs are always outside science FoV and so they pass through the edge of the layers/DMs…

## Slide 18: MAORY AO
layers
DMs
Telescope pupil
… and even through the volume not sensed by LGS

## Slide 19: MAORY AO – NGS/LO-reference
LO control can be done with a direct reconstruction of TT and plate scale (quadratic term) on DMs without passing through layers.
Reference has same reconstruction and projection scheme of HO/LGS.
LO control is almost* independent from HO/LGS one (*LO SNR depends on PSF quality, PSF quality depends on HO correction).
Reference gives zero point for HO/LGS.