## Slide 1: Work Package END TO END SIMULATION
Work Package END TO END SIMULATION team
Presented by W.P. manager Guido Agapito

## Slide 2: Stereo-SCIDAR profiles

## Slide 3: New atmospheric profiles
After a long discussion with ESO and the discovery of some inaccuracies we have rejected the 4 profiles proposed by ESO in 2018, but despite this ESO asks us to use the stereo-SCIDAR atmospheric profiles data released by Osborn et al.  they are 10k profiles, so we can not run sky coverage analysis on all of them.
Ollie Farley propose a method to cluster them based on morphology, but we want to choose profiles that correspond to a certain level of performance.

## Slide 4: Reference profiles
Median k=seeing/theta0 and median performance of Fourier analysis agree
0.37
So, we extract reference profiles for 10, 25, 50, 75, 90 percentile
We estimate MAORY HO performance on all 10k profiles with a Fourier based code, but ESO asks us to select profiles with a merit function independent from performance.
10p
25p
50p
75p
90p
Perc. | 10 | 25 | 50 | 75 | 90
k | 0.176 | 0.247 | 0.375 | 0.589 | 0.878
prof. index | 3101 | 536 | 2773 | 872 | 5280
prof. ε[“] | 0.486 | 0.552 | 0.663 | 0.784 | 0.922
prof. θ0 [“] | 2.74 | 2.23 | 1.76 | 1.34 | 1.06

## Slide 5: HO/LGS tomographic reconstruction, projection and control

## Slide 6: Best rec. layers altitude
Search for the best rec. layers altitude (tomo+fitting errors):
best configuration (v3, red line) altitude vector is [0, 2, 4.4, 7.6, 11, 15, 18] km.
The gain w.r.t. the old configuration (blue line) is ~70nm (161 vs 146nm), and full E2E simulation confirms this.
off-axis [arcsec] | old | old without gen. fitting | v2 | Δh=3km | v3 | v4
0 | 162 | 134 | 150 | 147 | 146 | 150
15 | 194 | 172 | 183 | 184 | 179 | 180
25 | 209 | 186 | 200 | 202 | 196 | 198
30 | 222 | 197 | 212 | 215 | 209 | 212
45 | 294 | 271 | 288 | 296 | 285 | 296
55 | 342 | 312 | 339 | 350 | 338 | 357
70 | 462 | 431 | 460 | 477 | 466 | 491
85 | 593 | 567 | 592 | 612 | 602 | 628
“All” Cn2 profile
2PFDMs 4000modes

## Slide 7: No. LGS and no. modes
6 LGSs
12 LGSs
PFDMs with 700 – 4000 modes difference is bigger with 12 LGSs because tomography gives more margin to projection
green line is without gen. fitting error

## Slide 8: No. LGS and no. modes
Correction on modes 2000-4000 is limited by tomography, more actuators will be useless
6 LGSs
12 LGSs
green line is without gen. fitting error

## Slide 9: Gen. fitting (projection) error
PFDMs with 4000modes
Same projection matrix, same PFDMS  almost same error for 6 and 12LGSs
PFDMs with 700modes
Difference between 7 layers (DMs) correction and 3 DMs correction

## Slide 10: Gen. fitting (projection) error
Left and right show good agreement (note: curve level depends on frequency sampling!)
Generalized fitting error code
PFDMs with 700modes
Difference between 7 layers (DMs) correction and 3 DMs correction

## Slide 11: Considerations on POLC
the use of the correct loop delay to compute the error term is important: we gain ~30nm using the new expression.
The matrix (dimension ) has a clear statistical meaning: it is the expected noise (in the modal space) given the DM commands.
Pseudo Open Loop Control (POLC) is used because it gives a stable MCAO control.
Equations (previous version):
limits the propagation of noise at time , but residual slopes are also affected by noise propagated through closed loop at time , ) term takes this into account.
New version:

## Slide 12: Other activities

## Slide 13: LGS/HO loop
Better rejection f<3Hz
Lower noise prop. f>20Hz
As you will see increasing the number of LGSs gives significative advantage in term of performance, but noise propagation will be affected, so we have studied:
No. of LGS SHS sub-aperture
temporal error
0.5% loss with 60x60sa
2.4% loss with 48x48sa
5.5% loss with 40x40sa
On-axis:
no. sub-aperture
temp. error
more complex temp. control

## Slide 14: Reference WFSs
on-axis SR(K)
Ref. WFSs bring SR back to ~100%
Different ref. WFSs bandwidth
No atmosphere
with atmosphere
We run simulation with sodium elongation to have some bias to be corrected by reference WFSs.
Conclusion:
3 10x10sa Refs with a good asterism:
can correct ~200modes on each DM
zero the truncation effect (res. 50-70nm, depends on asterism).
do not introduce a tomographic error on HO correction if bandwidth is slow enough (~0.01Hz)
Without atmosphere ref. WFSs works really well, but when atmosphere is there, ref. WFSs correct it with higher tomographic error than LGSs.

## Slide 15: Sodium layer focus correction
Can we use ref. WFSs to correct for tracking sodium layer focus variations and so using a single sub-aperture SH for LO?
LO SHS 1x1 has a small gain with respect to 2x2 (measuring only TT) of ~65nm.
We will be limited by the brightest star to get enough bandwidth (~1Hz) with a 10x10 SHS.
1Hz bandwidth will give a significative correction of turbulence focus, so we will get an isoplanatic error.
Probability of getting a sufficient bright star (R<22) is not 100%.
Turb (foc)
Sodium focus
~35nm
7.7%
1PFDM
Sky coverage 1x1 VS 2x2
Focus (turb. and sodium) residual

## Slide 16: Support to optical design
1
2
3
4
5
6
Impact of LGS objective aberrations:
interface zemax with IDL to get tomographic reconstruction of LGS objective aberrations.
help choosing best optical design.
6 LGS aberrations
(from old objective – MOC)
Effect on DMs

## Slide 17: Simulator test
ESO E2E simulations (Octopus/FRIM) are in good agreement

## Slide 18: Sky Coverage

## Slide 19: Error budget comparison (median spec. profile)
Making MAORY great again!
# LGS | 6 | 6 | 6 | 6 | 6 | 12 | 6+6
# PFDMs | 1 | 1 | 1 | 2 | 2 | 2 | 2
pitch | coarse | coarse | coarse | coarse | fine | fine | fine
# subaps LO | 2 | 2 | 2 | 2 | 2 | 2 | 2
# LO modes | 5 | 5 | 2 | 2 | 2 | 2 | 2
Dual AO | x | x | x | x | x | x | x
Telescope | 145 | 50 | 50 | 50 | 50 | 50 | 50
Residual (nm) | 355 | 328 | 312 | 299 | 293 | 279 | 277
Difference with 1st | 0 | 136 | 170 | 192 | 201 | 220 | 222
Step difference | 0 | 136 | 102 | 90 | 59 | 89 | 31
SR (K) | 0,357 | 0,416 | 0,452 | 0,483 | 0,497 | 0,530 | 0,534
SR (J) | 0,041 | 0,066 | 0,086 | 0,105 | 0,115 | 0,140 | 0,143
We “reduce” the 145nm error from the telescope to 50nm following HARMONI computation on ELT data package (wind shake, M1 phasing, …). Now we are making the same computation to verify this assumption.
We list the main steps which improve the performance from one year ago baseline configuration, SR(K)36%, to the best one we could have, SR(K)=53%.
50% sky cov. performance
Parameters

## Slide 20: Median SPEC profile
Technical FoV
Solid = 180’’
Dashed = 160’’
All SR(K)>30% for 50% sky.
We selected:
LO measures only TT (2LO in legend)  significative performance improvement
Technical FoV 160”  better for optical design

## Slide 21: LGS asterism 1 VS 2 rings
2 rings option gives better performance, but having LGS at r=60” is a real challenge for optical design

## Slide 22: Stereo-SCIDAR P=50% profile
Technical Fov = 160’’
Single post focal DM case is below SR(K)=30% at 50% sky.
2 rings options gives better results, but LGS at r=60” is challenging for optical design.
6+6 means:
6 at r=45” and 6 at r=60”

## Slide 23: Other LGS asterism and dual AO
4+4LGSs gives the same performance as 6+6
Optimization shown in previous slides benefits more the 2 post focal DMs case :
Dual AO improves significatively performance, but not at the level of 2 post focal DMs case.

## Slide 24: 2 PFDMs coarse 6 LGS
K band
J band
Sky coverage computed with the new stereo SCIDAR profiles gives a good way to visualize expected MAORY performance

## Slide 25: Small scientific FoV (20x20’’)
P=50%
P=75%
P=90%
Sky coverage with small Sc. FoV is much higher and could compete with HARMONI one.